From webber@fnal.gov Thu Jan 23 18:38:10 2003
Date: Thu, 23 Jan 2003 13:36:00 -0600
From: Bob Webber <webber@fnal.gov>
To: Stephen Pordes <stephen@fnal.gov>, Shekhar Mishra <mishra@fnal.gov>,
     Sergio Zimmermann <zimmer@fnal.gov>, Sam Childress <childress@fnal.gov>,
     Pushpalatha Bhat <bhat@fnal.gov>, Peter Prieto <prieto@fnal.gov>,
     Peter Limon <pjlimon@fnal.gov>, Paul Czarapata <pcceed@fnal.gov>,
     Mike Church <church@fnal.gov>, Mark Bowden <bowden@fnal.gov>,
     Joel Butler <butler@fnal.gov>, Jim Crisp <crisp@fnal.gov>,
     James Patrick <patrick@fnal.gov>, Duane Voy <voy@fnal.gov>,
     Craig McClure <mcclure@fnal.gov>, Charlie Briegel <briegel@fnal.gov>,
     Brajesh Choudhary <brajesh@fnal.gov>, Aisha Cadorna <cadornaa@fnal.gov>,
     Peter Wilson <pjw@fnal.gov>
Subject: 1_21_03 RR BPM Meeting minutes (DDC algorithms)


Minutes of Tuesday 1/21/03 RR BPM Meeting to discuss DDC algorithms

Attending: P. Prieto, J. Crisp, W. Schappert, B. Choudhary, B. Webber

Purpose of meeting was to focus efforts to address the questions:

1)  Do we conceptually understand in sufficient detail how we intend to use
the proposed EchoTek DDC board to make each of the required measurements for
each of the specified beam structures?

Required Measurement table:
-----------------------------------------------------------------------
                         TYPE             |          MODE             |
-----------------------------------------------------------------------
                   TBT   ClsdOrb   Flsh   SnglBnch  Head/Tail  Ensmbl |
-----------------------------------------------------------------------
2.5MHz structure |  Y  |    Y    |   Y   |    Y    |   N     |    Y   |
7.5MHz structure |  Y  |    Y    |   Y   | ~3bnchs |   N     |    Y   |
Unbunched beam   |  Y  |    Y    |   Y   |    N    |   Y     |    Y   |
-----------------------------------------------------------------------

2)  Are we confident that the proposed EchoTek DDC board is actually able to
make each of these measurements?
3)  Do we understand in sufficient detail the resulting data available in
the EchoTek FIFO for each measurement/mode to have some assurance that the
VME system can handle the data quantity and rate?

Initial discussion:
   Warren mentioned three items of concern: dynamic range, possibility of
adjustable gain stage, bandwidth limitation to prevent preamp saturation due
to high frequency (e.g. 53MHz) signal components.
Bob agreed with importance of addressing each item in system design, but
suggested that DDC algorithm was more important topic of this meeting.

   Peter reported that he had spoken with EchoTek in the morning and they're
still interested in selling us boards. (Peter has pricing information.) Some
discussion of 105 MHz vs. 80 MHz digitizer version of board.  Benefit of
higher digitization rate was not obvious to group and Peter expressed
concern about significantly higher power dissipation of faster digitizers.
He did not have price differential information between the two boards.
Agreed that 80MHz version should be our Plan A.

Signal processing discussion:
   Issue of digitization clock requirements arose and whether the clock need
be beam synchronous (editorial comment: even the definition of beam
synchronous in this context is a bit fuzzy).  For purposes of this meeting
we proceeded with the assumption that a synchronous clock, if necessary,
would be made available.
   There was quick concurrence that constraining discussions to TBT
measurements for each of the beam structures and measurement modes (single
bunch, head/tail, ensemble) was sufficient to ensure the possibility of
flash (one turn TBT) and closed orbit (post-processed averaging of TBT
array) measurement from EchoTek board perspective.
   Peter described internals of the DDC chip and how it was set up to make
the test beam position measurements of the RR 2.5MHz structure beam during
the past months.  There was general confidence that the path for the 2.5MHz
ensemble measurement and the corresponding 7.5MHz beam structure measurement
is clear, although concerns were raised about ability to make specified
measurements with unbunched beam "nearby". [Can be as close as 680ns
36/53MHz]
   Discussions then centered on 2.5MHz single bunch measurement and
un-bunched beam measurements (detailed talk about filters, data decimation,
etc.) Many possibilities of DDC set-up, how it might work, etc. were
offered, but definitive answers were not completely available.  It was
suggested that only simulation or demonstration could assure that any
specific design would be defensible.  A test stand is required in any case
for an eventual system and to some large extent already exists. That offers
the potential of demonstrated solutions, however the hardware guys are
presently occupied by shutdown activities and the demonstration path might
be slow.  As a parallel path to timely assurance that a design can be made
using processing provided by EchoTek board, Warren was tasked with producing
a model of the DDC signal processing chain.  Preliminary work that provides
input signal models exists.
   Questions were raised as to requirements for measuring dynamic hot beam
structures (e.g. as 2.5MHz structure debunches).  The requirements document
is silent about this situation and we are proceeding as though no specific
design considerations are requested for this case.  BRAJESH::Please comment
if the requirement is otherwise.
   Important issues of timing were raised during the discussions.  It was
noted that in the present design of the EchoTek board all eight channels
operate with a common trigger.  It is essential that the arrival time skew
of signals at each board be understood quantitatively (for proton signals,
pbar signals, and perhaps calibration signals) to determine if there is an
untractable problem.  This has the potential, although the probablility is
likely low, to be a SHOW STOPPER with the current EchoTek board design.
[Subsequent to the meeting I was informed that EchoTek has indicated they
might be able to implement channel-by-channel adjustable trigger delays on
the board.  But we need to know if we need them to do this!]
   Tentatively set Monday, Jan.27, as date for next meeting on this subject.
By then we expect to have signal timing skew information and see
considerable progress with Warren's simulations.



Bob Webber           mailto:webber@fnal.gov
phone (630)840-5415  pager (630)722-0085