Fermilab/BD/TEV

Beams-doc-475

March 3, 2003

Commissioning of the Tune Drift Compensations System in the Tevatron

J. Annala, M. Martens, P. Bauer*

Fermilab, Beams Division

*Fermilab, Technical Division

### Introduction

The Tevatron tune drift compensation system was commissioned and implemented during Tevatron studies on 9/23/02 and has been used successfully in Collider operations. After adjustments to the parameters in the compensation algorithm, the measured tune drift was less than 0.001 over forty minutes at 150 GeV and the measured minimum tune split was below 0.003 units during this time. These magnitudes should be compared to measured tune drifts of about 0.01 and minimum tune split drifts of 0.02 if the drifts are left uncompensated. Figure 1 shows a summary plot of the measured tune drifts before and after the compensation system was implemented.

Figure 1 Comparison of the tune drift at 150 GeV with and without the tune drift compensation. The measured tunes are plotted from data collected on 5/15/02 with no tune drift compensation, and data collected on 9/23/02 with the tune drift compensation active.

The tunes at the start of the ramp were also measured to investigate the “unwind” algorithm during the snapback at the start of the Tevatron ramp. Limitations on the accuracy of the tune measurements make it difficult to quantify how well the snapback algorithm works, but the preliminary data suggests the resulting tune drift at the start of the ramp is not a problem with the snapback correction in place. For future reference the beam position and the settings of the dipole correctors during these measurements were recorded and documented.

The rest of this memo presents the data collected during the commissioning of the tune drift system.

### Summary of Measurements

The data presented in this memo is summarized as follows:

- Measurement #1. Checked that the hardware and software were operating as expected. Made rough adjustments to the tunes and coupling and verified that the system was working.

- Measurement #2. Made precise measurements of the tune and coupling drift as a function of time on the 150 GeV front porch. During this store the tunes drifted by about 0.002 units over 130 minutes and the minimum tune split remained below 0.003 tune units.

- Calibrated the tune circuits.  The tune circuits used for the tune drift compensation, T:QDD1 and T:QFA4, were calibrated by measuring the tune as a function of  current in the trim quadrupole circuits.

- Adjusted drift algorithm. Used the results of the tune circuit calibration to modify the parameters in the drift compensation algorithm.

- Measurement #3. Made precise measurements of the tune and coupling drift with the update parameters. During this store the tunes drifted by only 0.001 units over 40 minutes and the minimum tune split remained below 0.003 tune units.

- Measurement #3 snapback. Measured the tunes on the Tevatron ramp to verify that the correction for the tune drift snapback worked correctly.

In addition to these measurements, the BPM orbits in the Tevatron and the DFG settings at 150 GeV were collected and the data is listed in Appendix A.

### Data from Measurement #2

The horizontal and vertical tunes were measured as a function of time at 150 GeV and the data are plotted in Figure 2. As evident from the plots, the tunes drifted by about 0.002 units over the two hours they were measured. During this front porch the coupling was measured at 5.5, 11.2, 18.2, 32.7, and 82 minutes and the minimum tune split was below 0.0027 units at all of these times. Thus the first attempt at correcting the tune drift reduced the amount of tune drift considerably, but left room for improvement.

Figure 2 Measured tune as a function of time on the 150 GeV front porch during measurement #2.

The ramp history of the Tevatron magnets is important since it may affect the tune and coupling drift. For these studies the Tevatron was ramped to a 980 GeV flattop (and to low beta) with a flattop time of 2446 seconds (40.7 minutes) and a back porch time of 83 seconds. For a Collider shot setup the ramp history is typically a dry squeeze with a 980 GeV flattop time of 15-20 minutes and a back porch time of 60-90 seconds. Thus the ramp history for this measurement is representative of the conditions during a Collider shot setup.

The tune drift compensation algorithm was determined from previous measurements of the tune and coupling drift at 150 GeV. The drift compensation used during this measurement is given in Equations 1-3

<((x> = -0.00778 + 0.0019 * ln(t) 				Equation 1

<((y> = 0.0127 - 0.0031 * ln(t)  				Equation 2

<((SQ> = 0.0250 - 0.0061 * ln(t)  				Equation 3

where t is the time (in seconds) from the start of the front porch. The currents in the trim quadrupole circuits are then determined from Equations 4-6 which relate currents in the trim quadrupoles to the change in tunes

IQFB2 (in Amps) = (* <((x> +(3.15) <((y>		Equation 4

IQDB2 (in Amps) = (* <((x> +(-9.74) <((y>  		Equation 5

ISQB2 (in Amps) = * <((SQ>.				Equation 6

The actual currents used for this measurement are plotted in Figure 3. For this measurement no current was used in the C:SQ0B2 (=T:SQA0) circuit.

Figure 3 Plot of currents in tune drift circuits as a function of time at 150 GeV.

The BPM orbits at 150 GeV and the dipole corrector (DFG) settings were recorded during these measurements and the data are listed in Appendix A.

### Calibration of tune circuits

After it was discovered that the tune drift algorithm did not completely compensate for the tune drifts, the trim quad circuits T:QDD1 and T:QDF4 were calibrated. A measurement of the tune shifts versus the current in the trim quads was performed and the results are plotted in Figure 4 and Figure 5. From linear fits to the data we find the matrix relationship between tune changes and current changes in the tune quad circuits,

(Measured tune response)

and inversely,

.

Based on this calibration, the coefficients in Equations 4 and 5 of the tune drift algorithm were updated and used for the next set of measurements of the tune drift at 150 GeV.

Figure 4 Plot of tune versus current in T:QFA4 at 150 GeV and the results of a linear fit to the data.

Figure 5 Plot of tune versus current in T:QDD1 at 150 GeV and the results of a linear fit to the data.

For comparison, we give the matrix relationship derived from a MAD file of the design lattice and the design strengths of the trim quadrupole magnets

(Calculated tune response)

and inversely

.

This shows that the trim quads are stronger than expected by about 10-30%.

### Data from Measurement #3

The horizontal and vertical tunes were measured as a function of time at 150 GeV with the updated tune drift algorithm based on the trim quad calibration data of the previous section. The data are plotted in Figure 6 and show that the tune drifted by less than 0.001 over the 40 minutes at 150 GeV. During this front porch the coupling was measured at 9.17, 22, and 34.83 minutes and was below 0.0031 units at all of these times.

Figure 6 Measured tune drift as a function of time at 150 GeV for measurement #3.

The Tevatron ramp cycle before this measurement had flattop time of 2399 seconds (40 minutes) and a back porch time of 79 seconds. This is similar to the ramp history in measurement #2 and for a typical shot setup. The orbits and DFGs for this measurement were similar to those for measurement #2 and are listed in Appendix A.

For comparison we plot the tune drift with the compensation system active on the same plot as measurements made on 5/15/02 with no tune drift compensation.

Figure 7 Comparison of horizontal and vertical tune drift with and without the compensation system active. The measurements without the compensation system were taken on 5/15/02.

### Data from Measurement #3 snapback

The circuits used to correct the tune and coupling drift at 150 GeV are also used to compensate for the snapback of the tune and coupling drift at the start of the ramp. Since we don’t know the source of the tune drift at 150 GeV we somewhat arbitrarily decided to use a 6 second unwind of the drift compensation at the start of the ramp. This is the same amount of time used to unwind the chromaticity correction circuits to compensate for the drifting b2 in the Tevatron dipoles. The amount of current accumulated in the tune and coupling compensation circuits is ramped down to zero current in 6 seconds using a quartic function given in Equation 7

I(t) = I0[1 -2 (t/T)2 + (t/T)4]  				Equation 7

where t is the time in seconds, and T is the time of the unwind curve.

The measured tunes during the snapback portion of the ramp are shown in Figure 8. Plotted are the measured tunes during the first 6 seconds of the Tevatron ramp. During this first 6 second of the ramp, the Tevatron energy increases parabolically with time from 150 GeV to about 153 GeV. In addition to the unwind of the correction circuits, the horizontal tune settings (on C49) remain constant at a value of Qh = 0.607, while the vertical tune setting changes from a value of Qv = 0.576 at 150 GeV to 0.570 units at 153.09 GeV.

The measured tunes during the snapback suggest that the snapback portion of the tune drift is adjusted adequately. However, the imprecision of the measurements means that the tunes can easily be in error by as much as tune 0.002 units. A more precise measurement of the tunes at the start of ramp is needed before it can be determined just how well the snapback is corrected.

Figure 8 Plot of measured horizontal and vertical tunes during the 6 seconds of snapback at the start of the Tevatron ramp. These measurements can easily be in error by as much as tune 0.002 units. During the time the Tevatron ramps from 150 GeV to about 153 GeV. In addition to the unwind of the snapback correction, the horizontal tune settings (on C49) remain constant at Qh = 0.607, while the vertical tune setting changes from Qv = 0.576 at 150 GeV to 0.570 units at 153.09 GeV.

The measured tunes and tune settings at the breakpoints on the Tevatron ramp were recorded in hopes that this would help determine how well the snapback was tuned up. These are plotted in Figure 9. As is evident from the plot, the tunes and tune settings jump around by about 0.005 units at breakpoints near the start of the ramp. This makes it difficult to tell exactly how well the snapback correction works. It is also uncertain how well the coupling has been corrected for this particular ramp. For future reference the settings of the coupling circuit T:SQ are shown in Figure 11.

Figure 9 Measured tunes on the ramp at the C49 breakpoints and the C49 tune setting values (Qh and Qv) at the breakpoints on the ramp. With the variations in the tune measurements and the tune settings it is difficult to estimate how well the snapback portion of the tune compensation system is adjusted.

Figure 10 Same data as in Figure 9 but only showing the data at the breakpoints near the beginning of the Tevatron ramp.

Figure 11 Settings of the Sq skew family (in C49 units) at the energy breakpoints on the ramp.

### Conclusions

The tune drift compensation scheme was tuned up and implemented successfully. With the system active the tunes drift by less than 0.001 units over the period of 40 minutes and the minimum tune split remains below 0.003 units.

### Appendix A: BPM and DFG data collected during tune drift studies.

Figure 12 and Figure 13 show the orbits in the Tevatron taken while sitting at 150 GeV with the separators off and with uncoalesced beam circulating in the Tevatron. Below these figures the BPM readings and the settings of the dipole correctors (DFGs) are listed.

Figure 12 BPM snapshot of the horizontal orbit while on the 150 GeV front porch. This is the central orbit (with helix off) and with uncoalesced beam.

Figure 13 BPM snapshot of the vertical orbit while on the 150 GeV front porch. This is the central orbit (with helix off) and with uncoalesced beam.

#### Listing of BPM data from Figure 12 and Figure 13.

T39 file:  202

Date: 09/23/02  2223

Title: 150 GeV b4 ramp 1784

s(meters)             position  s(meters)             position

from E0   BPM name    (mm)      from E0   BPM name    (mm)     .

32.74000 T:HPE11     -0.4000    35.45200 T:VPE11     -1.2500

91.28000 T:HPE13     -0.7000    62.40100 T:VPE12     -0.5800

150.76601 T:HPE15     -0.4000   121.02300 T:VPE14     -0.4000

210.25301 T:HPE17     -0.7500   180.50999 T:VPE16      0.6200

269.73999 T:HPE19     -0.5200   239.99699 T:VPE18      0.5800

329.22699 T:HPE22     -0.7400   299.48300 T:VPE21     -0.0200

388.71399 T:HPE24     -1.0029   358.97000 T:VPE23     -0.5000

448.20001 T:HPE26     -0.8057   418.45700 T:VPE25     -0.5014

507.68701 T:HPE28     -0.5500   477.94400 T:VPE27     -0.3093

567.17401 T:HPE32     -0.8000   537.43103 T:VPE29     -1.9500

626.66101 T:HPE34     -0.5800   596.91699 T:VPE33      0.9800

686.14801 T:HPE36     -0.6500   656.40399 T:VPE35     -2.6300

745.63397 T:HPE38     -0.8300   715.89099 T:VPE37     -0.2700

805.12097 T:HPE42     -0.2300   775.37799 T:VPE39     -0.2200

864.60797 T:HPE44     -0.3900   834.86499 T:VPE43      0.3400

924.09497 T:HPE46     -1.1300   894.35101 T:VPE45     -0.7200

983.58197 T:HPE48     -1.3700   953.83801 T:VPE47     -0.7700

1011.95502 T:HPE49     -4.0200  1016.80499 T:VPE49      4.1100

1052.32300 T:HPF0LU    -5.7468  1052.13196 T:VPF0LU     3.3715

1068.01697 T:HPF0LD    -5.7223  1068.20801 T:VPF0LD     3.8978

1079.93799 T:HPF11     -5.0500  1082.64905 T:VPF11      7.1300

1138.47705 T:HPF13     -0.2100  1109.59802 T:VPF12      1.8800

1197.96399 T:HPF15     -0.0300  1168.21997 T:VPF14     -0.0800

1257.45105 T:HPF17     -0.9000  1227.70703 T:VPF16      0.2000

1316.93701 T:HPF19      0.0100  1287.19397 T:VPF18      0.1200

1376.42395 T:HPF22     -0.5200  1346.68103 T:VPF21     -0.2000

1435.91101 T:HPF24     -0.4500  1406.16797 T:VPF23      0.0000

1495.39795 T:HPF26      0.5000  1465.65405 T:VPF25      0.2800

1554.88501 T:HPF28     -0.8200  1525.14099 T:VPF27     -0.1700

1614.37097 T:HPF32     -1.2000  1584.62805 T:VPF29     -0.2200

1673.85803 T:HPF34     -0.7000  1644.11499 T:VPF33      0.1000

1733.34497 T:HPF36      0.0300  1703.60205 T:VPF35      0.1500

1792.83203 T:HPF38      0.2700  1763.08801 T:VPF37      0.4400

1852.31897 T:HPF42     -0.8900  1822.57495 T:VPF39      0.0500

1911.80505 T:HPF44     -2.1500  1882.06201 T:VPF43      0.0500

1971.29199 T:HPF46     -1.0300  1941.54895 T:VPF45      0.0300

2030.77905 T:HPF48      3.5400  2001.03601 T:VPF47      0.9400

2058.92993 T:HPF49      2.7000  2064.00293 T:VPF49      4.3700

2088.51489 T:HPA0U      1.3500  2088.70508 T:VPA0U      0.2000

2100.13403 T:HPA0D      3.0600  2099.89502 T:VPA0D      7.8500

2127.16992 T:HPA11      3.7300  2130.01611 T:VPA11      2.5700

2185.67700 T:HPA13     -0.0500  2156.96411 T:VPA12      0.8500

2245.16309 T:HPA15     -0.6000  2215.41992 T:VPA14     -0.1800

2304.64990 T:HPA17     -1.1900  2274.90698 T:VPA16     -0.0900

2364.13696 T:HPA19     -1.0800  2334.39404 T:VPA18      0.1800

2423.62402 T:HPA22     -0.8500  2393.87988 T:VPA21     -0.5500

2483.11108 T:HPA24     -0.6600  2453.36694 T:VPA23      0.3200

2542.59692 T:HPA26      0.0800  2512.85400 T:VPA25     -0.2000

2602.08398 T:HPA28     -0.9200  2572.34106 T:VPA27     -0.4000

2661.57104 T:HPA32      0.2000  2631.82788 T:VPA29     -0.3600

2721.05811 T:HPA34     -1.0300  2691.31396 T:VPA33      0.0900

2780.54492 T:HPA36     -0.4000  2750.80103 T:VPA35      0.1500

2840.03101 T:HPA38     -0.2500  2810.28809 T:VPA37     -0.5200

2899.51807 T:HPA42     -0.2800  2869.77490 T:VPA39     -0.0800

2959.00488 T:HPA44     -0.1500  2929.26196 T:VPA43     -0.3500

3018.49194 T:HPA46     -0.5300  2988.74805 T:VPA45     -1.0700

3080.61011 T:HPA48      1.4100  3048.23511 T:VPA47      0.4300

3108.98291 T:HPA49     -0.8800  3080.83789 T:VPA48      1.7400

3134.11108 T:HPB0U     -0.5500  3109.21191 T:VPA49      1.2400

3149.07788 T:HPB0D      1.5500  3134.23096 T:VPB0U     -1.4300

3174.20508 T:HPB11      0.6300  3148.95703 T:VPB0D      0.1400

3206.62598 T:HPB12     -0.2800  3173.97607 T:VPB11     -0.4700

3232.87402 T:HPB13     -0.4700  3206.85498 T:VPB12     -0.0500

3292.36108 T:HPB15     -0.7500  3262.61792 T:VPB14      1.0600

3351.84790 T:HPB17     -0.5000  3322.10400 T:VPB16     -0.2000

3411.33496 T:HPB19     -0.2200  3381.59106 T:VPB18     -0.6700

3470.82104 T:HPB22     -0.0400  3441.07788 T:VPB21     -0.7500

3530.30811 T:HPB24     -0.9300  3500.56494 T:VPB23      0.1300

3589.79492 T:HPB26     -1.3400  3560.05200 T:VPB25      0.2500

3649.28198 T:HPB28     -0.8200  3619.53809 T:VPB27      0.0500

3708.76904 T:HPB32     -0.8500  3679.02490 T:VPB29     -0.7500

3768.25488 T:HPB34      0.2100  3738.51196 T:VPB33     -0.4400

3827.74194 T:HPB36     -0.5200  3797.99902 T:VPB35      0.2000

3887.22900 T:HPB38     -1.8700  3857.48608 T:VPB37      0.7700

3946.71606 T:HPB42     -1.3600  3916.97192 T:VPB39      0.3600

4006.20288 T:HPB44     -0.2500  3976.45898 T:VPB43     -0.2000

4065.68896 T:HPB46      0.0600  4035.94604 T:VPB45     -0.4700

4125.17578 T:HPB48      1.6500  4095.43311 T:VPB47      0.0200

4153.54980 T:HPB49     -0.1500  4158.39990 T:VPB49      0.9000

4221.53320 T:HPC11     -2.2300  4224.24414 T:VPC11     -0.7500

4280.07178 T:HPC13     -0.9300  4251.19287 T:VPC12      0.5500

4339.55908 T:HPC15     -1.0700  4309.81494 T:VPC14      0.3500

4399.04492 T:HPC17     -0.6300  4369.30176 T:VPC16     -0.2700

4458.53223 T:HPC19     -0.9000  4428.78906 T:VPC18     -0.4300

4518.01904 T:HPC22     -0.4300  4488.27588 T:VPC21      0.2900

4577.50586 T:HPC24     -0.5300  4547.76221 T:VPC23      0.9400

4636.99316 T:HPC26     -1.0800  4607.24902 T:VPC25      0.3900

4696.47900 T:HPC28     -0.7500  4666.73584 T:VPC27     -0.4500

4755.96582 T:HPC32     -0.3500  4726.22314 T:VPC29     -0.3700

4815.45313 T:HPC34     -0.4200  4785.70996 T:VPC33      0.3600

4874.93994 T:HPC36     -0.3100  4845.19580 T:VPC35      0.3600

4934.42676 T:HPC38     -0.8300  4904.68311 T:VPC37      0.7300

4993.91309 T:HPC42     -0.7000  4964.16992 T:VPC39     -0.3500

5053.39990 T:HPC44     -0.1000  5023.65723 T:VPC43     -0.7300

5112.88721 T:HPC46     -0.9800  5083.14404 T:VPC45     -0.1300

5175.00488 T:HPC48     -1.0200  5142.62988 T:VPC47      0.7800

5202.26807 T:HPC49     -1.5000  5175.23291 T:VPC48     -0.3500

5228.50586 T:HPD0U      1.9900  5201.03320 T:VPC49     -1.2000

5243.47314 T:HPD0D      2.6500  5228.62598 T:VPD0U      1.4600

5269.70996 T:HPD11      0.1500  5243.35205 T:VPD0D     -0.1000

5301.02100 T:HPD12      0.1800  5270.94580 T:VPD11     -0.1500

5327.26904 T:HPD13     -0.2700  5301.25000 T:VPD12     -0.1400

5386.75586 T:HPD15     -1.4000  5357.01318 T:VPD14     -0.0700

5446.24316 T:HPD17     -1.0300  5416.50000 T:VPD16     -0.4200

5505.72998 T:HPD19     -0.2800  5475.98584 T:VPD18      0.1100

5565.21680 T:HPD22      0.1300  5535.47314 T:VPD21      0.4300

5624.70313 T:HPD24      0.0800  5594.95996 T:VPD23     -0.2000

5684.18994 T:HPD26     -0.0700  5654.44678 T:VPD25     -0.1900

5743.67676 T:HPD28     -1.0800  5713.93408 T:VPD27     -0.7900

5803.16406 T:HPD32     -1.7200  5773.41992 T:VPD29      0.7500

5862.65088 T:HPD34     -0.5000  5832.90723 T:VPD33      0.5500

5922.13721 T:HPD36     -0.5200  5892.39404 T:VPD35      0.1400

5981.62402 T:HPD38     -0.7500  5951.88086 T:VPD37      0.1400

6041.11084 T:HPD42     -1.0100  6011.36816 T:VPD39     -0.5700

6100.59814 T:HPD44     -0.8000  6070.85400 T:VPD43     -0.0200

6160.08496 T:HPD46     -0.6500  6130.34082 T:VPD45      0.0200

6219.57080 T:HPD48     -1.1800  6189.82813 T:VPD47      0.4300

6247.94482 T:HPD49      0.1300  6252.79492 T:VPD49     -0.4700

#### Listing of dipole corrector (DFG) settings

These are DFG settings (in mrad) for the 150 and 200 GeV energy slots.

DFG       150    200           DFG       150    200

Name      GeV    GeV           Name      GeV    GeV

T:HE11    .073   .069          T:VE11    .0052  .0056

T:HE13   -.0406 -.0403         T:VE12    0      0

T:HE15    .0205  .0136         T:VE14   -.0324 -.0384

T:HE17   -.033  -.0344         T:VE16   -.0082 -.0055

T:HE19   -.0383 -.0396         T:VE18    .0028  .0012

T:HE22    .0296  .0292         T:VE21    .0181  .0178

T:HE24   -.0008  .0035         T:VE23   -.042  -.0463

T:HE26   -.0428 -.0455         T:VE25    .0691  .0738

T:HE28   -.003   .0013         T:VE27    .0251  .0225

T:HE32   -.0017  .003          T:VE29    .0703  .0744

T:HE34    .0121  .0067         T:VE33    .0917  .0869

T:HE36    .0016  .0029         T:VE35    .0563  .068

T:HE38   -.0065 -.0135         T:VE37    .0094  .0028

T:HE42   -.0437 -.051          T:VE39    .0628  .0686

T:HE44    .0165  .0223         T:VE43    .0601  .0645

T:HE46   -.0336 -.0429         T:VE45   -.0582 -.0649

T:HE48    .1955  .1923         T:VE47    .0701  .0791

T:HE49   -.0736 -.06           T:VE49    .0126  .0081

T:HF11   -.0101 -.0171         T:VF11    .003   .0078

T:HF13    .1221  .1202         T:VF12    .0401  .0401

T:HF15    .0121  .0114         T:VF14    .0082  .004

T:HF17   -.0305 -.0322         T:VF16   -.0048 -.005

T:HF19   -.0128 -.0197         T:VF18    .0301  .0334

T:HF22    .0002  .0051         T:VF21   -.0516 -.0607

T:HF24    0      .003          T:VF23    .0322  .0379

T:HF26    .0052 -.0027         T:VF25   -.0542 -.0537

T:HF28   -.0331 -.0243         T:VF27   -.014  -.0161

T:HF32    .0342  .0317         T:VF29    .0193  .0186

T:HF34   -.0028 -.0001         T:VF33   -.0406 -.0399

T:HF36    .0104  .0119         T:VF35    .022   .0157

T:HF38    .0067  .0026         T:VF37    .0193  .024

T:HF42    .0169  .017          T:VF39   -.0097 -.0129

T:HF44   -.0174 -.0158         T:VF43   -.011  -.0108

T:HF46    .022   .0115         T:VF45    .0389  .0381

T:HF48    .0785  .0688         T:VF47    .1188  .1435

T:HF49   -.1001 -.0975         T:VF49   -.1107 -.1377

T:HA11    .0901  .0716         T:VA11    .0904  .1129

T:HA13   -.099  -.102          T:VA12    .0221  .0221

T:HA15   -.0191 -.0252         T:VA14    .0978  .1045

T:HA17    .0673  .0734         T:VA16    .0906  .0902

T:HA19    .0529  .0468         T:VA18    .0845  .0906

T:HA22    .016   .0184         T:VA21    .0834  .0794

T:HA24   -.069  -.07           T:VA23    .0943  .1044

T:HA26    .0257  .0223         T:VA25    .0207  .0263

T:HA28    .0054  .0087         T:VA27    .0087  .0069

T:HA32   -.0386 -.0445         T:VA29   -.0049  .005

T:HA34    .0065  .0101         T:VA33   -.0106 -.0054

T:HA36   -.0057 -.0077         T:VA35   -.0033 -.0011

T:HA38    .0017  .0032         T:VA37    .004   .0058

T:HA42   -.0611 -.0554         T:VA39    .0013  .0059

T:HA44    .0124  .0101         T:VA43    .0244  .0221

T:HA46   -.0391 -.0341         T:VA45   -.0271 -.0248

C:HA48    0      0             T:VA47    .0038  .0035

T:HA48    .0912  .0927         C:VA48    0      0

T:HA49    .0529  .0571         T:VA49   -.1594 -.1528

T:HB11   -.0574 -.0634         T:VB11   -.03   -.03

C:HB12    0      0             T:VB12    .033   .033

T:HB13   -.0006 -.0016         T:VB14    .0559  .0595

T:HB15    .0477  .0448         T:VB16    .0393  .0368

T:HB17   -.0486 -.0578         T:VB18    .0943  .0961

T:HB19   -.041  -.0332         T:VB21    .0716  .0779

T:HB22    .0094  .0017         T:VB23    .0996  .0996

T:HB24    .0075  .0101         T:VB25    .0712  .0749

T:HB26    .0059  .0087         T:VB27   -.009  -.0084

T:HB28    .0398  .0397         T:VB29    .0424  .0424

T:HB32   -.0301 -.0263         T:VB33    .0049  .0076

T:HB34   -.0068 -.0079         T:VB35    .0218  .0197

T:HB36    .0402  .041          T:VB37   -.0389 -.0381

T:HB38    .0035  .0024         T:VB39   -.0261 -.0299

T:HB42    .0284  .0288         T:VB43   -.044  -.0431

T:HB44   -.0062 -.0068         T:VB45    .0057  .0018

T:HB46   -.0232 -.0264         T:VB47    .0145  .0228

T:HB48    .076   .0938         T:VB49   -.0051 -.0049

T:HB49   -.1008 -.1001         T:VC11    .018   .021

T:HC11   -.0998 -.0663         T:VC12    0      0

T:HC13    .0157  .0144         T:VC14   -.0221 -.0181

T:HC15    .0123  .0115         T:VC16    .0661  .0701

T:HC17    .0192  .015          T:VC18    .0435  .0387

T:HC19   -.0021  .0034         T:VC21   -.0046 -.0043

T:HC22    .0069  .0013         T:VC23    .0784  .0739

T:HC24   -.0254 -.0253         T:VC25    .0195  .0182

T:HC26    .0104  .0111         T:VC27    .0087  .005

T:HC28    .0442  .0459         T:VC29    .0025 -.0011

T:HC32   -.0139 -.0182         T:VC33   -.046  -.046

T:HC34   -.0203 -.0175         T:VC35   -.0057 -.0122

T:HC36   -.0206 -.0259         T:VC37   -.0257 -.0234

T:HC38   -.0168 -.0126         T:VC39    .0193  .0128

T:HC42    .0291  .036          T:VC43    .0198  .0209

T:HC44    .0009 -.0097         T:VC45    .0015 -.0016

T:HC46    .0112  .0204         T:VC47    .0216  .023

C:HC48    0      0             C:VC48    0      0

T:HC48   -.07   -.07           T:VC49    .1105  .0945

T:HC49   -.0007 -.016          T:VD11    .0168  .0117

T:HD11    .0198 -.0104         T:VD12   -.05   -.05

C:HD12    0      0             T:VD14    .0539  .0553

T:HD13    0      .0059         T:VD16   -.0468 -.0384

T:HD15   -.0116 -.012          T:VD18    .0364  .0335

T:HD17   -.0322 -.031          T:VD21    .0115  .0171

T:HD19    .0117  .0106         T:VD23    .0377  .0293

T:HD22   -.0033 -.0047         T:VD25    .0329  .0435

T:HD24   -.0025 -.0001         T:VD27   -.012  -.0216

T:HD26    .0011  .0001         T:VD29    .0112  .0122

T:HD28    .0804  .0826         T:VD33   -.0437 -.0412

T:HD32   -.0629 -.0626         T:VD35    0      0

T:HD34   -.0004 -.0012         T:VD37    .0137  .0162

T:HD36    .0032  .0066         T:VD39    .0036  .0055

T:HD38    .0116  .0104         T:VD43    .0376  .0414

T:HD42    .0093  .0088         T:VD45    .0402  .0436

T:HD44   -.0127 -.0155         T:VD47    .0929  .0917

T:HD46   -.0016 -.003          T:VD49   -.0372 -.0387

T:HD48    .0018 -.0003

T:HD49    .021   .0187

### Appendix B: Tune drift at 150 GeV over period of days.

Also of interest is the repeatability of the tunes at 150 GeV over the period of several days.  The measured tunes and C49 tune settings at 150 GeV over several days during and after the tune drift compensation system was implemented are listed in Table 1. These show that the tune is kept constant (after adjustment for setting changes) to within about 0.002 units over the period of several days.

| Measurement | Date | Setting Qh (C49) | Setting Qv (C49) | Measured (x | Measured (x | Time at 150 GeV |
| --- | --- | --- | --- | --- | --- | --- |
| Measurement #2 | 9/23/02 | .607 | .576 | .5872 | .5729 | 3.7 |
| Measurement #3 | 9/23/02 | .607 | .576 | .5872 | .5731 | 5.5 |
| Shot setup 1787 | 9/24/02 | .602 | .579 | .5832 | .5749 | ??? |
| Octupole studies | 9/25/02 | .6025 | .579 | .583 | .575 | ??? |
| Shot setup 1797 | 9/27/02 | .603 | .578 | .5837 | .5749 | ??? |
| Shot setup 1799 | 9/28/02 | .602 | .5785 | .5832 | .5749 | ??? |
| TEL studies | 9/29/02 | .6025 | .578 | .5833 | .5748 | ??? |
| Shot setup 1806* | 9/30/02 | .6025 | .582 | .583 | .575 | ??? |
| Shot setup 1810 | 10/1/02 | .6015 | .579 | .583 | .575 | ??? |

Table 1 Measured tunes and settings at 150 GeV over several days during and after the tune drift compensation system was implemented.  After adjusting for the intentional changes to the tune settings, the measured tunes drifted by less than 0.002 over several days. (* During tune-up for shot 1806 the TECAR energy on the front porch was changed from 150.02 to 150.00 GeV. This was also after the Tevatron was off for repairs to the A3 power supply unit.)

# Footnotes

Details of the hardware and software algorithms for the tune drift system can be found in the note “Chromaticity, Tune, and Coupling Drift and Snapback Correction Algorithms in the Tevatron”, Mike Martens, Jerry Annala, Beams-doc-467, http://beamdocs.fnal.gov/cgi-bin/public/DocDB/ShowDocument?docid=467