Tevatron Magnet Roll Measurement

January 14 to February 7, 2003

Hans Jostlein, Craig Moore,

Ray Stefanski, Jim Volk

# Introduction

In the summer of 2002, Mike Syphers presented corrector magnet data that implied a vertical alignment problem in the Tevatron. With this as an incentive, AMG was asked to collect roll and elevation measurement in the Tevatron. These measurements confirmed the suspicion that several parts of the ring were misaligned relative to the original tolerance set for the machine: Originally no Tevatron dipole had a roll greater than 0.37 mrad, and the rms for all the dipoles was 0.20 mrad.. In several parts of the ring magnet elevations had changed relative to 1995 measurements.

The data that were available from the AMG were necessarily fragmented, since there wasn’t sufficient time to measure the entire ring. The January shutdown gave us an opportunity to complete these measurements, but surveyors tend to be completely booked in a typical shutdown. Craig and Hans suggested a method similar to one used in the Main Ring: to measure magnet roll with a fixture, using a Taylor Hobson Talyvel Clinometer. Two people working in tandem can carry the fixture along to each magnet. One person positions the fixture on the magnet, while the other logs the readings - originally by pencil and paper, but finally directly into an Excel spreadsheet.

# The Measurement Fixture

The fixture consists of a level bar on which is mounted a sensitive Talyvel Clinometer system. The bar is about 16 inches long so that it can be set on top of the survey lugs found on the sides of Tevatron dipoles and quadrupoles. (Only magnets with outside steel were measured in this survey.) The bar also was equipped with a level gauge set at ninety degrees to the plane of the measurement so that the fixture could be set vertical before a measurement was taken. A photo of the use of the fixture is shown if figure 1.

# Calibration

A calibration setup consisted of a level table upon which the measurement fixture could be set. By raising one end of the fixture by a known amount, a corresponding reading could be taken by the clinometer. The readings were first calibrated in minutes, as shown in figure 2a. Readings are taken with an external voltmeter. The calibration of the external voltmeter is shown in Figure 2b. The relevant number for the measurements done in the Tevatron is that a 7 mV reading corresponds to one minute of tilt. The clinometer readings, as read by the external voltmeter, saturated at about 50 mV.

# Methods

People working in pairs for about 2 to 4 hours per day carried out the measurements. Ultimately, about 950 magnets were measured providing the first comprehensive survey of the Tevatron since 1995.

Except for those that had an obstruction preventing a measurement, each magnet was measured at two points – using the survey lugs at the upstream and downstream end of each magnet, each point being measure three time to check for consistency. Each set of three measurements consisted of a normal measurement, followed by a measurement with the fixture reversed, culminated by a final normal measurement. In the analysis the first and second measurements was averaged to give a measure of roll. The third measurement was used only as a consistency check. For lack of time, only about half of the magnets had both ends measured. The remaining magnets had only one end measured, usually the upstream end, if it was accessible.

Some magnets had larger roll than could be measured with the measurement fixture alone. For these magnets a shim was used in conjunction with the fixture. Two shims were used, 66 mV thickness and 132 mV thickness, where the readings in mV correspond the offset in the voltmeter reading produced by the shim. These readings correspond to 2.69 mrad and 5.38 mrad of roll respectively.

# Analysis

Various cuts on the data were used to eliminate duplicate or faulty measurements:

- Readings were excluded if they were greater than 50 mV, that is if the clinometer reading was saturated.

- Only one reading was kept in the analysis for each end of the magnet. Sometimes the choice was arbitrary.

- If a shim was used, the reading with the largest shim was taken, and the others excluded, unless the reading was saturated. Then the reading with the next largest shim was taken, again if it wasn’t saturated, etc.

As mentioned earlier, each end of a magnet was measured three times. The first two readings were averaged and converted to mrad. For magnets that had both ends measured, the measurements were averaged together to provide an average roll for the magnet. The difference in the two measurements gave a measure of magnet twist.

Figure 3 shows all rolls for dipoles and quads. The origin of the plot starts at A0. Rolls greater that 8 mrad are seen in A sector. Clusters of rolled magnets are also seen in B, C, D and E sectors, with the biggest clusters in B and E. A remarkable effect seen in these measurements is that magnet rolls tend to be positive along the entire ring. (A positive roll is clockwise when looking down the beam in the proton direction.)

The quadrupoles define the beam’s principal ray in the Tevatron, so they need to be considered separately. The quadruloes with the largest roll measured by this survey are given in Table 1.

Table 1: Quadrupoles with roll greater than  2 mrad compared also

to previous measurements by the AMG.

|  |  | 9-Nov | 14-Jun | 19-Nov |
| --- | --- | --- | --- | --- |
|  |  | 2001 | 2002 | 2002 |
| Quads | survey | survey |  |
|  |  | 2001 | 2003 |  |
| A15-1 | 4.18 | 1.28 |  | 4.19 |
| A16-1 | 2.75 | 2.75 |  |  |
| A23-1 | 2.16 | 4.12 | 2.41 |  |
| A24-1 | 2.44 | 3.62 | 2.98 |  |
| A25-1 | 3.80 | 2.53 | 3.68 |  |
| C24-1 | 3.04 |  |  |  |
| D46-1 | 2.17 | -0.03 |  |  |
| E32-1 | 2.97 | 4.91 |  |  |
| E39-1 | 2.56 | 4.06 |  |  |
| E43-1 | 2.59 | 2.09 |  |  |

Table 2: Comparison of roll measurements with results from AMG surveys.

| Sector | Date | Ave. | Standard |
| --- | --- | --- | --- |
|  |  | Diff. | Deviation |
| A | Jan 2003 | 0.02 | 0.13 |
| A | Jun 2002 | -0.03 | 0.21 |
| B | May 2000 | -0.32 | 0.12 |
| B | Nov 2001 | -.023 | 0.10 |
| B | Feb 2003 | 0.09 | 0.13 |
| D | May 2000 | -0.32 | 0.12 |
| D | Nov2001 | -0.23 | 0.10 |
| D | Feb 2003 | 0.09 | 0.13 |

The distribution of rolls greater than one mrad along the ring is about the same for dipoles and quadrupoles.

# Comparison with previous measurements

As a check on how well this process works, we compared the measurements to previous surveys made by the AMG. The results, given in Figure 4, show that there is very good agreement between measurements as taken in A Sector. (Outliers were ignored in this comparison.) The mean difference between measurements is 0.23+- -0.13 mrad. The comparison with more recent measurements taken in January, 2003 gives the result –0.03 +/- -0.21. Comparison with other measurements made in B and D sectors gives similar results as summarized in Table 2.

# Results

As was shown in Figure 3, rolls greater than 1 mrad come in about five clusters around the ring, in A, B, C, D and E sectors. The largest clusters, and the magnets with the largest roll are located in A, B and E sectors. In a more quantitative way, these distributions are given in Table 3.  There are 9 magnets with roll greater than 5 mrad, and 8 are located in A sector. There are 67 magnets with roll greater than 2 mrad, and all but 9 are located in A, B and E sectors. F sector has only six magnets with roll greater than 1 mrad, and none with roll greater than 2 mrad.

Table 3: Distribution of Magnet Roll in the Tevatron.

|  |  |  |  |  |  |  |  | Number of |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Sector | Roll Angle > N mrad | Magnets |
|  |  |  |  |  |  |  |  | Measured |
|  | >1 | >2 | >3 | >4 | >5 | >6 | >7 | in sector. |
| A | 42 | 24 | 12 | 9 | 4 | 3 | 1 | 163 |
| B | 41 | 16 | 3 | 1 |  |  |  | 161 |
| C | 14 | 4 | 2 | 1 |  |  |  | 154 |
| D | 16 | 5 | 1 | 1 | 1 |  |  | 156 |
| E | 47 | 18 |  |  |  |  |  | 163 |
| F | 6 |  |  |  |  |  |  | 156 |
| Total > N | 166 | 67 | 18 | 12 | 5 | 3 | 1 | 953 |

Correlation with vertical corrector magnet currents

We can now test the supposition that magnet role might be responsible for elevated corrector magnet currents. In the Tevatron, there is one vertical and one horizontal corrector for each set of two cells. A cell typically consists of a quadrupole, a spoolpiece, and four dipoles. In Figure 5a, we plot the vertical corrector angle verses the measured roll of each quadrupole and dipole in the corresponding cell. As seen in the Figure, magnets with roll greater than 2 mrad are correlated with angle corrections between zero and 0.2 mrad. We saw in Figure 3 that magnet roll in the Tevatron tends to be positive along the entire ring. So also are the corrector currents associated with them.

For comparison, we also made the same plot for horizontal correctors. We suspect that magnet roll should not be correlated to horizontal corrections. In Figure 5b, we plot the horizontal corrector angle verses measured magnet roll in the corresponding cell. For roll angle greater than 2 mrad, the corrector angles lie between –0.1 and +0.1 mrad. That is no correlation exists between horizontal corrections and magnet roll, as expected.

# Twist

Out of 953 magnets measured, 487 were measured at both ends. These measurements were used to determine if any twist exists in the magnets. When delivered to the Tevatron, all magnets have their survey lugs adjusted so that the magnet sits level. Any measure of twist indicates a change in the magnet after the survey lugs were set. These changes may have occurred in delivery of the magnets to the Main Ring tunnel. Table 4 shows the results of the measurements. Significant twist is seen in many magnets, within a range of about –2.0 to +2.0 mrad. This is a significant distortion, and may confuse any understanding of magnetic fields within the magnet.

| Table 4: Magnets with twist greater than one mrad. |
| --- |
| A21-3 | 2.97 |
| A21-4 | 1.18 |
| A29-4 | 1.14 |
| B13-2 | -1.03 |
| B15-3 | 1.64 |
| B16-5 | 1.15 |
| B37-2 | 2.13 |
| C10-4 | -2.11 |
| C14-5 | 1.03 |
| C15-2 | -1.25 |
| C16-2 | -1.21 |
| C17-5 | -1.01 |
| C24-2 | -1.17 |
| C47-1 | -1.11 |
| D16-1 | 1.13 |
| E19-2 | 1.41 |
| E26-1 | 1.01 |
| E26-3 | -1.16 |
| E29-5 | 1.98 |
| F12-4 | -1.2 |

| Table 5: Comparison of Twist Measurements with Elevation Measurements by ANG. |
| --- |
| Sector | No. of | Ave. | Standard |
|  | Diff. | Diff. | Deviation |
| A | 18 | 0.0170 | 0.0307 |
| B | 39 | -0.1324 | 0.0862 |
| C | 20 | 0.0677 | 0.1231 |
| D | 3 | -0.0959 | 0.1369 |
| E | 38 | -0.1761 | 0.979 |
| Average of 5 Sectors | 118 | -0.0888 | 0.0890 |

In order to gauge the precision of the twist measurements, we compared them to the most recent elevation measurements. As shown in Figure5, the average difference between measurements is –0.0888. The average standard deviation for the five sectors is 0.0890.

# Removal of Main Ring magnets from the Tunnel

A possible explanation of the roll measurement and twist results would be a correlation between magnet roll with parts of the tunnel where ring magnets were removed. Figure 6 shows the magnet rolls in areas where ring magnets were removed compared to areas where ring magnets are still present. It’s suggestive that F Sector has smaller magnet rolls than the rest of the Tevatron, and no ring magnets were removed from that sector. However, F sector also has no history of water problems, which may be a better explanation for smaller rolls in that sector. The average roll in areas where ring magnets are present is 0.61 +- 0.013 mrad. In areas where ring magnets were removed the average roll is 0.58 +- 0.010 mrad. These results give no indication of correlations due to ring magnet removal.

However, There may be a correlation between magnet twist and the presence of main ring magnets in the tunnel. In Table 6, we give the distribution of magnets with twist greater that 1 mrad for Tevatron magnets in areas where ring magnets were removed, and areas where they remain. Two samples were studied: One with Ring Magnets removed directly above, and the second with ring magnets removed either above or to either side of the Tevatron magnet with twist greater than 1 mrad. We conclude that about 2/3 of the Tevatron magnets in this sample are in areas where ring magnet removal took place. Although this represents a real correlation, it is probably not the only activity that influences magnet twist.We suspect that these magnets may also reside preferentially in areas that have water damage, or corroded magnet stands.

Table 6: Correlation Between Tevatron Magnets with Twist greater than 1 mrad, and the presence of Nearby Main Ring Magnets.

| Status of Nearby | Directly | Above and |
| --- | --- | --- |
| Main Ring Magnets | Above | on Either |
|  |  | Side |
| Removed | 13(61.9%) | 38(64.4%) |
| Remaining | 8(38.1%) | 21(35.6%) |

The Beams Division removed 47% of the ring magnets from the tunnel.

# Roll Created by Movement in Magnet Stands

In search of possible causes for magnet roll in the Tevatron, one must consider the possibility that magnet stands are themselves moving, or in some way, causing the effect. Tunnel workers have long been aware that some magnet stands look deteriorated. Most of the visual rust or chemical accumulation is probably cosmetic, but some damage may actually be present. A photo of one of the most suspicious magnets is given in Figure 7. There is evidence of rust on the magnet stand, and an accumulation of white material thought to be released salts from the concrete floor. These effects occurred because, for a time, the tunnel floor was wet from water seepage through cracks in the concrete walls and floor.

The stands shown in Figure 7 were removed and replaced in the January shutdown. The base of the stand was in bad condition, and represents a possible hazard if the magnet alignment were ever to be redone. This exercise will probably lead to a program of magnet stand replacement or upgrade in the coming months. Further measurements of magnets in this part of the tunnel are being done with clinometers and hydrostatic level sensors to map changes that may occur from day to day. This part of the tunnel has magnets with the largest magnet roll.

# Conclusions

The measurements done in the January shutdown represent the first comprehensive alignment survey since 1995. They provide the Laboratory with a measure of the condition of this one aspect of the accelerator.

More needs to be done: Because twist is seen in many Tevatron magnets, these measurements should be completed for the remainder of the ring. About 500 magnets remain to be measured on both ends. It is also useful to repeat the roll measurement periodically, to monitor the Tevatron alignment. To make this feasible, the measurement process would need to be streamlined so that the measurements could be made in a few working days. There is also an effort being made to develop continuous, real-time, measures of roll and relative elevation. A few test configurations have already been installed.

# Acknowledgements

We’re grateful to Jim Williams for assisting with taking the data.

# APPENDIX

The original measurements are available at http://home.fnal.gov/~volk/Janshtdwn/alignment.

# Footnotes

SSC CLOSED-ORBIT CORRECTION
Craig Moore, Thornton Murphy, James Norem, Michael Zisman
Accelerator Physics Issues for a Superconducting Super Collider
APS Workshop Report p. 78-92, Ann Arbor, Michigan 12-17 December 1983

Stefanski etal, to be published.

# Text boxes

Figure 1

Figure 2a

Figure 3

Figure 3

Figure 2b

Figure 4

A19 to A 26

Outliers in 2002 measurement were: -1.52; 1.78 mrad.

Outliers in 2003 measurement were: -1.81; 3.02 mrad.

outliers

Figure 7

Roll-meter compared to Jan, 2003 survey: 0.02 +/- 0.13

Roll-meter compared to Jun, 2002 survey: 0.03 +/- 0.21

Figure 5a

Figure 5b