Cogging Plan

- Re-establish Beam on old DDS firmware then switch to new firmware

- Tune up curves with new DDS firmware

- Re-scan high field aperture using RPOS bump

- Measure emittance vs. RPOS

- Establish cogging on $17 cycles

  - Multiple notch triggers (all other events will remain on old system)

  - Need to redo extraction sync firmware (Rev. marker input)

  - Monitor parameters over period of time (Trip plan drift, notch vs. BES)

  - Possibly set up pinger to work with Vertical notcher

  - Work on ACNET parameters

  - Corrections to software as needed (OAA vs our OAA correction)

- Establish cogging on MI cycle

- Using a MI study cycle establish Cogging ($xx ??)

- Investigate Extraction jitter and losses (Test Desired Bucket offset)

- Simplify turn on/off of cogging (establish semi-permanent setup)

- Work on operational diagnostics and ACNET interface

- Establish cogging on multi batch cycles

- Sync MI reset with internal Booster marker and Booster gen. OAA

- Software/Firmware work ???

- ACNET controls

- ACNET diagnostics

- Notching issues (one Notch early, other notches late in cycle)

- Operational Work

  - Establish software control over RF curve loading

  - Diagnostics, Learning Algorithm and other running mode parameters

  - Spare hardware testing

*	Other Related Work:  Creating a notch in the pre-acc and synchronizing to it.

Collimator installation and placement – vertical pinging.

Cogging Operational Issues

- Generation of Cogging Trip Plan

  - When to make a new trip (guidelines)

  - Error signal(s) to monitor (gap error at transition, Booster Drift)

  - Safeguards (beam gate, large gap errors)

  - Software trigs and normal RF curve loading

- Control of Cogging

  - How to enable/disable (similar to notch control)

  - Signals to datalog (losses, gap position vs OAA)

  - Pinger timing and Notch trigger alignment

  - Offset controls (similar to Notch delays)

  - Control of RF curve loading (Load only on $12 – before cog cycles)

  - Dedicated scope signals (gap, OAA, Kickers ????)

- VXI Interface

  - Ability to send and receive curves and parameters (gains, Trip Plan)

  - Link with present Notch and Transfer Sync hardware

  - Make boot and file structure similar to GMPS and  LL DDS card

- Phase Lock and Cogging

  - Bucket control

  - Extraction Timing / parameters  (Acceptable MI bucket location)