Fermilab/BD/TEV

Beams-doc-924-v1

November 25, 2003

Version 1.0

Notes on Tev BPM offset changes in November 2003.

M. Martens, F. DeJongh, M. Olson

Fermilab, Beams Division

### Introduction

This is a collection of notes on Tevatron BPM offset changes implemented based on measurements made during the fall of 2003 shutdown. A more complete set of measurements exists, but this memo is limited to the changes made to the offsets used by the Tevatron BPM program T39. A complete list of the changes made to the offsets is given in a separate Excel spreadsheet, including the offsets used by T39 prior to November 2003 and the updated values implemented on November 25th, 2003.

[Note: The changes to the offsets were first implements on 11/17/03 at 11:00, but then a few errors were found. The corrected version of the offsets were implemented on 11/25/03 at 15:00.]

### Explanation of Offsets

There are two components to the offset, an electrical offset and a mechanical (or survey) offset. T39 calculates the position from the raw digitized data, D, with the transform

where A0, the lookup table f, , and  are retrieved from the database.  The raw data, D, is an 8 bit number, and is the digitized version of the output voltage of the BPM analog box.  The lookup table is shown in Appendix A. For small position offsets from the center of the BPM’s the lookup table is approximately linear and the position is equal to X (mm) = 0.15*(128 – D).  The offsets for all detectors are from the database and are computed in the manner shown above.

The F0 detectors are also done in this way, but their position scale factors are 2.83 rather than 1.0. The BPMs near F0 have a different scaling factor since the stripline pickups are physically different.

Most detectors use the lookup table to determine their positions.  There are four special detectors at E2 (HE24, HE26, VE25, and VE27) which had used a different algorithm altogether.  For these, position = (float) (((128.0 - raw_data) / 0.112) / 100.0 + offset. During the fall 2003 shutdown the electronics for these detectors was replaced with the standard type of electronics used elsewhere in the ring. The electrical offsets measured for this shutdown were made after the electronics was replaced with the standard version.

### Measurements of the Electrical Offsets

Measurements of the electrical offsets were made by injecting a common signal onto the pbar end of the pickups, thus simulating a beam going through the center of the pickups. The signal was generated with a waveform generator and simulated 30 uncoalesced bunches. The measured position and the raw counts with this signal were recorded and translated into offset numbers. Almost all of the BPMs were measured in this manner except for a few locations (such as the B0 and D0 BPMs) which were inaccessible,

The spreadsheet of offsets contains two sets of data related to the electrical offset. The first is based on the position recorded by T39 when the signal is injected into the pbar plates. From the T39 position and the offsets used by T39 a new electrical offset can be determined. A more straightforward method is to record the raw digital signal produced by the BPMs and then this value becomes the electrical offset. For small values of the beam position the electrical offset = (128-Raw) * 0.15 (Scale to mm). Both of these methods were used, but this resulted in some inconsistencies in the electrical offset and these BPMs were measured again.

There were a number of BPMs which showed a change in the electrical offset of more than 1 mm. These are listed in the table below. Almost all of the BPMs showed a smaller electrical offset now than was previously used by T39. These are the changes made to the BPM offsets in T39 on November 25th, 2003. The changes were based on measurements of the electrical offsets and a review of the survey offsets.

With these changes in T39, the reported BPM positions will change by the negative of the amount of the offset in the difference columns. For instance, if actual position of the beam were not moved, then the BPM at T:HPE44 would report a position +1.67 mm further to the radial outside.

|  | Electrical Offsets |
| --- | --- |
| BPM | Original | After changes | Difference |
| T:VPA23 | 3.20 | 0.00 | -3.20 |
| T:VPD45 | 2.89 | 0.15 | -2.74 |
| T:HPC15 | 1.96 | 0.00 | -1.96 |
| T:HPD46 | 1.51 | -0.30 | -1.81 |
| T:HPE44 | 2.42 | 0.75 | -1.67 |
| T:VPA47 | 1.51 | 0.15 | -1.36 |
| T:HPE46 | 1.66 | 0.30 | -1.36 |
| T:HPC34 | 1.35 | 0.00 | -1.35 |
| T:VPD25 | 0.90 | -0.45 | -1.35 |
| T:HPF44 | 1.20 | 0.15 | -1.05 |
| T:HPA48 | 0.60 | -0.45 | -1.05 |
| T:VPE43 | 1.05 | 0.00 | -1.05 |
| T:VPF12 | 0.75 | -0.30 | -1.05 |
| T:VPF27 | 0.75 | -0.30 | -1.05 |
| T:VPD39 | 1.35 | 0.30 | -1.05 |
| T:HPA13 | -0.45 | 0.60 | 1.05 |
| T:HPD38 | -0.15 | 0.90 | 1.05 |
| T:VPE47 | -0.90 | 0.15 | 1.05 |
| T:VPE45 | -1.20 | 0.00 | 1.20 |
| T:HPA17 | -1.51 | 0.00 | 1.51 |
| T:HPB12 | -0.90 | 0.90 | 1.80 |
| T:HPC11 | -2.12 | -0.15 | 1.97 |

### Review of the Mechanical Offsets

A review of the mechanical offsets of the BPMs with respect to the center of the quadrupole field was undertaken. There were a number of BPMs which showed a change in the mechanical offset of more than 1 mm. These are listed in the table below. With these changes in T39, the reported BPM positions will change by the amount of the total offset in the difference columns. For instance, if actual position of the beam were not moved, then the BPM at T:VPF11 would report a position 0.73 mm further downwards.

|  | Mechanical Offset |
| --- | --- |
| BPM | Original | After Changes | Difference |
| T:VPF11 | 0.00 | -0.73 | -0.73 |
| T:HPC49 | 0.32 | 0.00 | -0.32 |
| T:VPD11 | 0.00 | -0.15 | -0.15 |
| T:VPA29 | -0.02 | 0.03 | 0.05 |
| T:HPE48 | 0.00 | 0.53 | 0.53 |

There are several elements for which the mechanical offsets are still needed:

TSHA315      T:VPA11

TSH345         T:VPB49

TSH387         T:VPC11

TSH314         T:VPE49

TSH386         T:VPF49

### Appendix A: Lookup table to convert digital value of BPM readback into millimeters.

This is the Tevatron BPM scaling lookup table. The scaled values should be divided by 100 to convert to millimeters.

raw_value   scaled_value

----------- ------------

0        10000

1        10000

2        10000

3        10000

4        10000

5        10000

6        10000

7        10000

8        10000

9        10000

10         6271

11         5165

12         4615

13         4246

14         3967

15         3744

16         3557

17         3397

18         3256

19         3131

20         3018

21         2915

22         2821

23         2733

24         2652

25         2576

26         2505

27         2438

28         2375

29         2315

30         2257

31         2203

32         2151

33         2101

34         2053

35         2006

36         1962

37         1919

38         1878

39         1838

40         1799

41         1761

42         1725

43         1689

44         1655

45         1621

46         1588

47         1557

48         1525

49         1495

50         1465

51         1436

52         1408

53         1380

54         1353

55         1326

56         1299

57         1274

58         1248

59         1223

60         1199

61         1175

62         1151

63         1128

64         1105

65         1083

66         1060

67         1038

68         1017

69          995

70          974

71          953

72          933

73          913

74          893

75          873

76          853

77          834

78          814

79          795

80          777

81          758

82          740

83          721

84          703

85          685

86          667

87          650

88          632

89          615

90          598

91          580

92          563

93          547

94          530

95          513

96          497

97          480

98          464

99          447

100          431

101          415

102          399

103          383

104          367

105          351

106          336

107          320

108          304

109          289

110          273

111          258

112          242

113          227

114          212

115          196

116          181

117          166

118          151

119          135

120          120

121          105

122           90

123           75

124           60

125           45

126           30

127           15

128            0

129          -15

130          -30

131          -45

132          -60

133          -75

134          -90

135         -105

136         -120

137         -135

138         -151

139         -166

140         -181

141         -196

142         -212

143         -227

144         -242

145         -258

146         -273

147         -289

148         -304

149         -320

150         -336

151         -351

152         -367

153         -383

154         -399

155         -415

156         -431

157         -447

158         -464

159         -480

160         -497

161         -513

162         -530

163         -547

164         -563

165         -580

166         -598

167         -615

168         -632

169         -650

170         -667

171         -685

172         -703

173         -721

174         -740

175         -758

176         -777

177         -795

178         -814

179         -834

180         -853

181         -873

182         -893

183         -913

184         -933

185         -953

186         -974

187         -995

188        -1017

189        -1038

190        -1060

191        -1083

192        -1105

193        -1128

194        -1151

195        -1175

196        -1199

197        -1223

198        -1248

199        -1274

200        -1299

201        -1326

202        -1353

203        -1380

204        -1408

205        -1436

206        -1465

207        -1495

208        -1525

209        -1557

210        -1588

211        -1621

212        -1655

213        -1689

214        -1725

215        -1761

216        -1799

217        -1838

218        -1878

219        -1919

220        -1962

221        -2006

222        -2053

223        -2101

224        -2151

225        -2203

226        -2257

227        -2315

228        -2375

229        -2438

230        -2505

231        -2576

232        -2652

233        -2733

234        -2821

235        -2915

236        -3018

237        -3131

238        -3256

239        -3397

240        -3557

241        -3744

242        -3967

243        -4246

244        -4615

245        -5165

246        -6271

247       -10000

248       -10000

249       -10000

250       -10000

251       -10000

252       -10000

253       -10000

254       -10000

255       -10000