Fermilab/BD/TEV

Beams-doc-xxx-v1

December 10, 2004

BPM Sub Rack Technical Details

Bill Haynes, Vince Pavlicek, Ken Treptow

Fermilab, Computing Division, CEPA

Jim Steimel

Fermilab, Accelerator Division, Accelerator Controls Department

Abstract

This document contains technical details that will assist the assembly of electronics sub racks for the BPM system installation.

Index

BPM VME sub rack setup.	3

Sub Rack Maps	3

Timing Generator/Fanout Module Addressing	6

Filter Module Addressing	7

Appendix	11

Numbers of sensors by service building.	11

# BPM VME sub rack setup.

The following Module Maps are defined to assist airflow.

If modules are not installed, the slots must be filled with air dams.

Fan legend:  B = blade, H = hub,  N = nothing, in order of preference.  The airflow is expected to be highest over the blades, less over the hubs and the least over the gaps between the blades.  The boards are placed

There are five different configurations to accommodate the variety of the number of BPMs sensors in a service building.  All of the Timing Generator/Fanout modules have the same address.  The Echotek and Filter modules addresses depend on the number of modules in the sub rack and the position of the modules within the sub rack.  Maps for the service buildings, in order of quantity of modules needed, follow.

## Sub Rack Maps

11 or 12 BPM Crate for Service Buildings E4, F1

| Slot | Contents | VME Address | TGF Address | Fan |
| --- | --- | --- | --- | --- |
| 1 | MVME CPU | Lots | ---------- | B |
| 2 | Timing Generator Fanout | 0x2000 | Master | B |
| 3 | TGF panel | ---------- | ---------- | H |
| 4 | Air Dam | ---------- | ---------- | H |
| 5 | Filter #0 | ---------- | 0 | B |
| 6 | Echotek #0 | 0x8000 | ---------- | B |
| 7 | Air Dam | ---------- | ---------- | N |
| 8 | Filter #1 | ---------- | 1 | B |
| 9 | Echotek #1 | 0x9000 | ---------- | B |
| 10 | Filter #2 | ---------- | 2 | H |
| 11 | Echotek #2 | 0xA000 | ---------- | H |
| 12 | Filter #3 | ---------- | 3 | B |
| 13 | Echotek #3 | 0xB000 | ---------- | B |
| 14 | Air Dam | ---------- | ---------- | N |
| 15 | Air Dam | ---------- | ---------- | N |
| 16 | Filter #4 | ---------- | 4 | B |
| 17 | Echotek #4 | 0xC000 | ---------- | B |
| 18 | Air Dam | ---------- | ---------- | H |
| 19 | Air Dam | ---------- | ---------- | H |
| 20 | Filter #5 | ---------- | 5 | B |
| 21 | Echotek #5 | 0xD000 | ---------- | B |

9 or 10 BPM Crate for A2, A4, B2, B4, C2, C4, D2, D4, E2, F2, F4, A1, B1, C1, D1, E1.

| Slot | Contents | VME Address | TGF Address | fan |
| --- | --- | --- | --- | --- |
| 1 | MVME CPU | Lots | ---------- | B |
| 2 | Timing Generator Fanout | 0x2000 | Master | B |
| 3 | TGF panel | ---------- | ---------- | H |
| 4 | Air Dam | ---------- | ---------- | H |
| 5 | Filter #0 | ---------- | 0 | B |
| 6 | Echotek #0 | 0x8000 | ---------- | B |
| 7 | Air Dam | ---------- | ---------- | N |
| 8 | Filter #1 | ---------- | 1 | B |
| 9 | Echotek #1 | 0x9000 | ---------- | B |
| 10 | Air Dam | ---------- | ---------- | H |
| 11 | Air Dam | ---------- | ---------- | H |
| 12 | Filter #2 | ---------- | 2 | B |
| 13 | Echotek #2 | 0xA000 | ---------- | B |
| 14 | Air Dam | ---------- | ---------- | N |
| 15 | Air Dam | ---------- | ---------- | N |
| 16 | Filter #3 | ---------- | 3 | B |
| 17 | Echotek #3 | 0xB000 | ---------- | B |
| 18 | Air Dam | ---------- | ---------- | H |
| 19 | Air Dam | ---------- | ---------- | H |
| 20 | Filter #4 | ---------- | 4 | B |
| 21 | Echotek #4 | 0xC000 | ---------- | B |

7 or 8 BPM Crate for A3, B3, C3, D3, E3, F3.

| Slot | Contents | VME Address | TGF Address | fan |
| --- | --- | --- | --- | --- |
| 1 | MVME CPU | Lots | ---------- | B |
| 2 | Timing Generator Fanout | 0x2000 | Master | B |
| 3 | TGF panel | ---------- | ---------- | H |
| 4 | Air Dam | ---------- | ---------- | H |
| 5 | Filter #0 | ---------- | 0 | B |
| 6 | Echotek #0 | 0x8000 | ---------- | B |
| 7 | Air Dam | ---------- | ---------- | N |
| 8 | Filter #1 | ---------- | 1 | B |
| 9 | Echotek #1 | 0x9000 | ---------- | B |
| 10 | Air Dam | ---------- | ---------- | H |
| 11 | Air Dam | ---------- | ---------- | H |
| 12 | Filter #2 | ---------- | 2 | B |
| 13 | Echotek #2 | 0xA000 | ---------- | B |
| 14 | Air Dam | ---------- | ---------- | N |
| 15 | Air Dam | ---------- | ---------- | N |
| 16 | Filter #3 | ---------- | 3 | B |
| 17 | Echotek #3 | 0xB000 | ---------- | B |
| 18 | Air Dam | ---------- | ---------- | H |
| 19 | Air Dam | ---------- | ---------- | H |
| 20 | Air Dam | ---------- | ---------- | B |
| 21 | Air Dam | ---------- | ---------- | B |

6 BPM Crate for B0.

| Slot | Contents | VME Address | TGF Address | fan |
| --- | --- | --- | --- | --- |
| 1 | MVME CPU | Lots | ---------- | B |
| 2 | Timing Generator Fanout | 0x2000 | Master | B |
| 3 | TGF panel | ---------- | ---------- | H |
| 4 | Air Dam | ---------- | ---------- | H |
| 5 | Filter #0 | ---------- | 0 | B |
| 6 | Echotek #0 | 0x8000 | ---------- | B |
| 7 | Air Dam | ---------- | ---------- | N |
| 8 | Filter #1 | ---------- | 1 | B |
| 9 | Echotek #1 | 0x9000 | ---------- | B |
| 10 | Air Dam | ---------- | ---------- | H |
| 11 | Air Dam | ---------- | ---------- | H |
| 12 | Filter #2 | ---------- | 2 | B |
| 13 | Echotek #2 | 0xA000 | ---------- | B |
| 14 | Air Dam | ---------- | ---------- | N |
| 15 | Air Dam | ---------- | ---------- | N |
| 16 | Air Dam | ---------- | ---------- | B |
| 17 | Air Dam | ---------- | ---------- | B |
| 18 | Air Dam | ---------- | ---------- | H |
| 19 | Air Dam | ---------- | ---------- | H |
| 20 | Air Dam | ---------- | ---------- | B |
| 21 | Air Dam | ---------- | ---------- | B |

4 BPM Crate for A0.

| Slot | Contents | VME Address | TGF Address | fan |
| --- | --- | --- | --- | --- |
| 1 | MVME CPU | Lots | ---------- | B |
| 2 | Timing Generator Fanout | 0x2000 | Master | B |
| 3 | TGF panel | ---------- | ---------- | H |
| 4 | Air Dam | ---------- | ---------- | H |
| 5 | Filter #0 | ---------- | 0 | B |
| 6 | Echotek #0 | 0x8000 | ---------- | B |
| 7 | Air Dam | ---------- | ---------- | N |
| 8 | Filter #1 | ---------- | 1 | B |
| 9 | Echotek #1 | 0x9000 | ---------- | B |
| 10 | Air Dam | ---------- | ---------- | H |
| 11 | Air Dam | ---------- | ---------- | H |
| 12 | Air Dam | ---------- | ---------- | B |
| 13 | Air Dam | ---------- | ---------- | B |
| 14 | Air Dam | ---------- | ---------- | N |
| 15 | Air Dam | ---------- | ---------- | N |
| 16 | Air Dam | ---------- | ---------- | B |
| 17 | Air Dam | ---------- | ---------- | B |
| 18 | Air Dam | ---------- | ---------- | H |
| 19 | Air Dam | ---------- | ---------- | H |
| 20 | Air Dam | ---------- | ---------- | B |
| 21 | Air Dam | ---------- | ---------- | B |

## Timing Generator/Fanout Module Addressing

The address switches are identified below. The switch pack is 8 switches, four of which set the board address and the other four are option selectors for the module logic.  The address switches are the four bits of the most significant digit of the 16 bit address of the module, in other words N of 0xN000.

The address for the TGF module is always 0x2000 which is selected using the following table.  Switch ON is bit = 0, switch OFF is bit =1.

| TGF address | SW0-LSB | SW1 | SW2 | SW3-MSB |
| --- | --- | --- | --- | --- |
| 2 | On | Off | On | On |

## Filter Module Addressing

The address switches are identified below.

The addresses are selected using the following table.  See detailed view below.

| Filter address | SW0 | SW1 | SW2 |
| --- | --- | --- | --- |
| 0 | Off | Off | Off |
| 1 | On | Off | Off |
| 2 | Off | On | Off |
| 3 | On | On | Off |
| 4 | Off | Off | On |
| 5 | On | Off | On |
| 6 | Off | On | On |
| 7 | On | On | On |

Setting the switches.

Echotek Module Addressing

The address switches are identified below.

The switches set the high hexadecimal digit (N) of the board VME address, or 0xN000. Echotek addresses must be 0x8000 or higher for the VxWorks driver, so SW3, the 8 bit,  is always on.

| VME address | SW0 - LSB | SW1 | SW2 | SW3 - MSB |
| --- | --- | --- | --- | --- |
| 0x8000 | Off | Off | Off | On |
| 0x9000 | On | Off | Off | On |
| 0xA000 | Off | On | Off | On |
| 0xB000 | On | On | Off | On |
| 0xC000 | Off | Off | On | On |
| 0xD000 | On | Off | On | On |
| 0xE000 | Off | On | On | On |
| 0xF000 | On | On | On | On |

Setting the switches.

# Appendix

## Numbers of sensors by service building.

| Service Building | BPMs | Modules | Slots | MT |  | BLMs |
| --- | --- | --- | --- | --- | --- | --- |
| A0 | 4 | 2 | 7 | 14 |  | 12 |
| B0 | 6 | 3 | 9 | 12 |  | 9 |
| D0 | 6 | 3 | 9 | 12 |  | 9 |
| A3 | 8 | 4 | 11 | 10 |  | 8 |
| B3 | 8 | 4 | 11 | 10 |  | 8 |
| C3 | 8 | 4 | 11 | 10 |  | 22 |
| D3 | 8 | 4 | 11 | 10 |  | 9 |
| E3 | 8 | 4 | 11 | 10 |  | 9 |
| F3 | 8 | 4 | 11 | 10 |  | 8 |
| A2 | 9 | 5 | 13 | 8 |  | 12 |
| A4 | 9 | 5 | 13 | 8 |  | 12 |
| B2 | 9 | 5 | 13 | 8 |  | 9 |
| B4 | 9 | 5 | 13 | 8 |  | 8 |
| C2 | 9 | 5 | 13 | 8 |  | 8 |
| C4 | 9 | 5 | 13 | 8 |  | 23 |
| D2 | 9 | 5 | 13 | 8 |  | 9 |
| D4 | 9 | 5 | 13 | 8 |  | 9 |
| E2 | 9 | 5 | 13 | 8 |  | 8 |
| F2 | 9 | 5 | 13 | 8 |  | 8 |
| F4 | 9 | 5 | 13 | 8 |  | 9 |
| A1 | 10 | 5 | 13 | 8 |  | 9 |
| B1 | 10 | 5 | 13 | 8 |  | 8 |
| C1 | 10 | 5 | 13 | 8 |  | 11 |
| D1 | 10 | 5 | 13 | 8 |  | 12 |
| E1 | 10 | 5 | 13 | 8 |  | 9 |
| E4 | 11 | 6 | 15 | 6 |  | 8 |
| F1 | 12 | 6 | 15 | 6 |  | 8 |

# Text boxes

Front

Panel

MSB (8)

Right = on = 1

LSB

(1)

Toward FP = on = 1

Address Switches

Sw2 – MSB (4)

Sw0 – LSB (1)

Address Switches

UP = ON = 0

MSB

LSB