Some Thoughts and Observations on Tevatron HV Separators Conditioning

1. Introduction

After FY’05 start-up of the Tevatron we experienced many problems with separators. They cost us several (4-5) stores lost and required lengthy conditioning at 150 kV.

Process of conditioning at higher voltage was always helpful for decreasing sparking rate. A simple theory says (theory to be added) that the number of sparks should scale as

where A(E,S) is function of surface quality (number of imperfections, area) and electric field E, decay time ( is also function of E.

Fig.1: Conditioning at 150 kV, Dec.9-13 2004.

Fig.2: Conditioning process: sparks in various seprators vs time at 150 kV

Fig.3: Total number of sparks during Dec.9 conditioning and exponential decay model fit.

Fig.4: Condioning repeated on Dec.13

Fig.5: Different conditioning curves for A47H separator and the rest of HV separators, Dec.13 data.

Fig.6: At the end of conditioning (Dec.13, 2004, 150kV) A47H power supply could not keep up the current.

Fig.7: Cumulative plot of conditioning at 150 kV: total number of sparks in all HV separators vs time.

Fig.8: Cumulative plot of conditioning at 150 kV and best fit with two exponential decays (for early stage and later stages of conditioning).

Fig.9: Conditioning at 150 kV: total number of sparks in all HV separators vs time and fit curve.

Fig.10: Conditioning at 150 kV with different polarities (C:B1HSP).

The table below compares sparking rates under  various conditions:

| conditioning at 120 kV | ~1 spark/hr |
| --- | --- |
| conditioning at 150 kV | ~330 sp/hr ( 6 sp/hr |
| operations at 100-120kV Dec 2004 | ~0.02-0.04 sp/hr |
| operations at 105-120 kV FY’04 (doc-1273) | ~0.002 sp/hr |

Conclusions:

1. Observed number of sparks during conditioning can be approximated by

At the beginning (first 2-3 hrs of conditioning) ( was about 1/5-2 hrs, after some 5 hrs ( increased to 9-12 hrs. At 150 kV, A is about 700-800, at 120 kV, A is some 10-20.

2. After-shutdown-conditioning at 120 kV with average rate 1 spark/hr did not help (though it was hundreds of times the pre-shutdown rate)

3. 20 hours of conditioning at 150 kV resulted in spark rate reduction by a factor of about 50 (about 100 for all but A49H) .

4. Ramping voltage down to 0 and back to 150 kV did not affect the sparking rate. No strong effect of polarity on the sparking rate was observed.

5.  B11V1 and , especially, A47H1M are found to be significantly different from other separators (higher sparking rates, etc).

6. (thus, no good explanation left of why the sparking rates are 10-20 times higher than before shutdown except some screw-ups with few separators, e.g. B11V and A47H).