February 16, 2005

Timing Generator Fanout (TGF) Diagnostic Signals

Sent to the Filter Card

Features:

- Capable of sending a 53Mhz clock synchronized to beam clock.

- Capable of sending a pulse train (7 pulses) at a 53Mhz rate again synchronized to beam clock.

- The pulse train can be adjusted anywhere within a one turn of the beam with a resolution of ½ bucket. The delay is set by adjusting the Sync(7) output delay.

- The above diagnostic signals can be routed to any/all channels of any/all Filter Cards to the:

  - Echotek digitizer

  - BPM sensor

  - Or both the Echotek digitizer and the BPM sensor

TGF Generated 53Mhz Clock		  	Filter Card Output to Echotek

TGF Generated Pulse Train			Filter Card Output to Echotek

TGF Delay = 0					TGF Delay = 40

| Table 7 | FilterCard Control Register BIT DEFINITIONS | I/O Address 0x100 |
| --- | --- | --- |
| DATA | DESCRIPTION |  |
| Bit-0 | FilterCard Start/Done Card 0 | Note 1 |
| Bit-1 | FilterCard Start/Done Card 1 | Note 1 |
| Bit-2 | FilterCard Start/Done Card 2 | Note 1 |
| Bit-3 | FilterCard Start/Done Card 3 | Note 1 |
| Bit-4 | FilterCard Start/Done Card 4 | Note 1 |
| Bit-5 | FilterCard Start/Done Card 5 | Note 1 |
| Bit-6 | FilterCard Start/Done Card 6 | Note 1 |
| Bit-7 | FilterCard Start/Done Card 7 | Note 1 |
| Bit-8 | FilterCard R/W | Note 2 |
| Bit-9 | FilterCard Enable Diagnostic Signal |  |
| Bit-10 | Diagnostic Signal Type | Note 3 |
| Bit-11 | RelayState0 |  |
| Bit-12 | RelayState1 |  |
| Bit-13 | RelayState2 |  |
| Bit-14 |  |  |
| Bit-15 | FilterCard Global Reset |  |

| Table 8 | FilterCard Data Register |  |  |
| --- | --- | --- | --- |
|  | Table 8 |  |  |
| Ch # | MSB Data LSB | Source | Destination |
| 1 | xx xx xx xx xx xx xx 00 | BPM | Digitizer |
| 1 | xx xx xx xx xx xx xx 01 | Diagnostic | BPM |
| 1 | xx xx xx xx xx xx xx 10 | Diagnostic | BPM & Digitizer |
| 1 | xx xx xx xx xx xx xx 11 | Diagnostic | Digitizer |
| 2 | xx xx xx xx xx xx 00 xx | BPM | Digitizer |
| 2 | xx xx xx xx xx xx 01 xx | Diagnostic | BPM |
| 2 | xx xx xx xx xx xx 10 xx | Diagnostic | BPM & Digitizer |
| 2 | xx xx xx xx xx xx 11 xx | Diagnostic | Digitizer |
| 3 | xx xx xx xx xx 00 xx xx | BPM | Digitizer |
| 3 | xx xx xx xx xx 01 xx xx | Diagnostic | BPM |
| 3 | xx xx xx xx xx 10 xx xx | Diagnostic | BPM & Digitizer |
| 3 | xx xx xx xx xx 11 xx xx | Diagnostic | Digitizer |
| 4 | xx xx xx xx 00 xx xx xx | BPM | Digitizer |
| 4 | xx xx xx xx 01 xx xx xx | Diagnostic | BPM |
| 4 | xx xx xx xx 10 xx xx xx | Diagnostic | BPM & Digitizer |
| 4 | xx xx xx xx 11 xx xx xx | Diagnostic | Digitizer |
| 5 | xx xx xx 00 xx xx xx xx | BPM | Digitizer |
| 5 | xx xx xx 01 xx xx xx xx | Diagnostic | BPM |
| 5 | xx xx xx 10 xx xx xx xx | Diagnostic | BPM & Digitizer |
| 5 | xx xx xx 11 xx xx xx xx | Diagnostic | Digitizer |
| 6 | xx xx 00 xx xx xx xx xx | BPM | Digitizer |
| 6 | xx xx 01 xx xx xx xx xx | Diagnostic | BPM |
| 6 | xx xx 10 xx xx xx xx xx | Diagnostic | BPM & Digitizer |
| 6 | xx xx 11 xx xx xx xx xx | Diagnostic | Digitizer |
| 7 | xx 00 xx xx xx xx xx xx | BPM | Digitizer |
| 7 | xx 01 xx xx xx xx xx xx | Diagnostic | BPM |
| 7 | xx 10 xx xx xx xx xx xx | Diagnostic | BPM & Digitizer |
| 7 | xx 11 xx xx xx xx xx xx | Diagnostic | Digitizer |
| 8 | 00 xx xx xx xx xx xx xx | BPM | Digitizer |
| 8 | 01 xx xx xx xx xx xx xx | Diagnostic | BPM |
| 8 | 10 xx xx xx xx xx xx xx | Diagnostic | BPM & Digitizer |
| 8 | 11 xx xx xx xx xx xx xx | Diagnostic | Digitizer |