Longitudinal Beam-Beam Effects in Tevatron

V.Shiltsev, A.Tollestrup

Fermi National Accelerator Laboratory, PO Box 500, Batavia, IL 60510, USA

Abstract

For the first time we observe effects of longitudinal electromagnetic head-on interactions of high intensity proton and antiproton beams. The interaction leads to proton longitudinal emittance  growth which is undetectable in standard HEP stores, but can be as big as 10% of the IBS rate if a longitudinal instability occurs. We present observations of the phenomenon in the Tevatron, analyze the data and propose an explanation.

PACS numbers: 29.27.bd

- Store #4111

- Other stores

- Discussion

- Conclusions

a) proton long emm growth rate in store #4111 DID depend on

intensity of antiprotons p-bunches collided with at

CDF and D0 ("Alvins' Effect")

b) the effect is 1/10 of the IBS dS^2/dt ~ N_p/emm^1.5/S

and is prop to dS^2/dt ~ N_a (max about 0.03 ns^2/hr)

c) store #4111 was "double remarkable": 36x24 and huge

1.4 deg phase oscillations due to long turbulence

d) in most of other stores (67 since Mar'05) IBS

dominated and "Long-Beam-Beam" led to slower growth

dS^2/dt ~1/N_a

e) Still, in some 7-10 stores, the "Alvin Effect" occured,

not as prominent as in #4111; most of those stores had

large phase oscillations

f) the effect might be as proposed by Petr Ivanov, etal(1991)

We are grateful to Aimin Xiao and Jean-Paul Carneiro

for preparation of the raw data files.

- References

[1] V.Danilov, et.al, Proc. 1991 IEE PAC, p. 526