Fermilab/AD/TEV

Beams-doc-xxxx-v1

September 6, 2005

Version 1

Main Injector Beam Position Monitor Upgrade

Software Specifications for

Data Acquisition

Margaret Votava, Luciano Piccoli, Steven Foulkes

Fermilab, Computing Division, CEPA

Brian Hendricks

Fermilab, Accelerator Division, Accelerator Controls Department

Abstract

This document contains the specifications for the Main Injector BPM upgrade data acquisition software. Expected operating modes and interactions with the BPM hardware are described. Data structures for communication with the online software via ACNET are defined.

# BPM Commands

There are two commands available at the online user level interface: Set_BPM_FILTER and Set_BPM_Mode. These commands are describe in more details in the Main Injector BPM upgrade requirements document (doc db#1786).

For every MI cycle there is a sequence of such commands associated. These commands must be known by the front-end software before the MI cycle is started. The following is a proposed structure for an ACNET device that can be used to transmit the commands associated to a MI cycle down to the front-end:

#define MIBPM_MAX_COMMANDS_PER_CYCLE 100

#define MIBPM_NAME_STATE_LEN 32

struct MIBPM_COMMAND {

int timeInCycle;     // Time when command is activated

int filterSetting;   // 53MHz or 2.5MHz

int particleType;    // Protons or Pbars

int attenuation;     // 0db, -6db, -12db, -18db, -24db, -30db, etc

int measurementType; // Closed Orbit, turn-by-turn, flash turn-by-turn

int trigger;         // MIBPM or RRBS value

int triggerType;     // MIBPM, RRBS or BES

}

struct MIBPM_CYCLE {

int resetEvent;      // TCLK reset event

int state;           // MI MDAT state that identifies the cycle

char stateName [MIBPM_STATE_NAME_LEN]; // Name for the state

MIBPM_COMMAND commands [MIBPM_MAX_COMMANDS_PER_CYCLE];

}

The list of commands for any cycle can be changed at any time by online users. However if the cycle is currently running the front-end can either 1) return an error when the user tries to set the new cycle information or 2) wait until the end of the cycle to change the cycle command table.

After receiving a list of commands the front-end will perform a basic check of the parameters. A more thoroughly check is expected to happen before the commands are sent to the front-ends. The front-end will provide means to read back the cycle command configuration, but no history of commands for any cycle will be kept by the front-end software.

# Text boxes

Crate Controller

User

Application

EchoTek

- Data request

- Command

- Data request

- Command

- Position data

- Position data

ACNET

BPM

UTI

Sequencer

T pages

CLIB

VAX  (1)

ACNET

MOOC

DAQ Front-end Applications

Front-End (N)

Sun (DAQ engines) (N)

DAQ Jobs

Windows/Linux (N)

Java Application

Ethernet/RMI

ACNET java

BPM UTI

java

Ethernet

Data at end of FIFO is dicarded

- Switch

activated

by

user

configur-

able event ($78)

- Switch

activated

by

TCLK $75

shot data

event

- Switch activated

every 2ms

- Switch deactivated on abort $47 or $4B

- Switch reactivated after 1st turn acquisition

Display

Frame

Buffer

Crate Controller

Timing Module

Front-end crate

- Switch activated

every 1sec

- Switch deactivated on abort $47 or $4B

-Switch reactivated after 1st turn acquisition

- Switch changed by change in Tevatron state device that listens to $4B and $5C events.

- Switch

activated

by

user

configur-

able event

128 pts

Data at end of FIFO is discarded

User

Data

Buffer

Fast

Time

Plot

Buffer

Switch activated every 2ms

TBT

Mode

All Closed Orbit Mode switches are interrupted by TBT mode.

128 pts

1024 pts

1024 pts

FIFO full generates error.  Pointer reset on TCLK $C2.

Data at end of FIFO is dicarded

ACNET

BPM

UTI

Sequencer

T pages

CLIB

VAX

ACNET

MOOC

DAQ Front-end Applications

Crate Controller

BPM Cards

DAQ Jobs

Filter Cards

Java Application

Ethernet/RMI

ACNET java

BPM UTI

java

Ethernet

Data Processing

Filter Cards

BPM Cards

Front-end crate

Crate Controller

Timing Module

BPM Cards

BLM Hardware (non VME)

Profile Frame Buffer

Slow

Abort

Buffer

Fast

Abort

Buffer

Closed Orbit Mode

Digital Filter

Mode Switch

- Position data

- Position data

- Data request

- Command

- Data request

- Command

TGF Filter Echotek

Online

Software

Crate Controller

Front-end crate

Timing Module

…

Repetition Period

VME Transfer

CollectionDone Int

Data Collections

TGF Trigger Outs

TGF Interrupt

TGF Turn Modulus

Turn Marker

Desired Number of Turns

VME Transfer

TriggerCounter Int

Data Collections

TGF Trigger Outs

TGF Interrupt

Bsync Start Event

Turn Marker

Data Processing

- Switch activated

every 1sec

- Switch deactivated on abort $47 or $4B

-Switch reactivated after 1st turn acquisition

- Switch changed by change in Tevatron state device that listens to $4B and $5C events.

- Switch

activated

by

user

configur-

able event

128 pts

Data at end of FIFO is discarded

User

Data

Buffer

Fast

Time

Plot

Buffer

Switch activated every 2ms

TBT

Mode

All Closed Orbit Mode switches are interrupted by TBT mode.

128 pts

1024 pts

1024 pts

FIFO full generates error.  Pointer reset on TCLK $C2.

Data at end of FIFO is dicarded

Data at end of FIFO is dicarded

- Switch

activated

by

user

configur-

able event ($78)

- Switch

activated

by

TCLK $75

shot data

event

- Switch activated

every 2ms

- Switch deactivated on abort $47 or $4B

- Switch reactivated after 1st turn acquisition

Display

Frame

Buffer

Profile Frame Buffer

Slow

Abort

Buffer

Fast

Abort

Buffer

Closed Orbit Mode

Digital Filter

Mode Switch

Filter Boards

PMC

UCD

ADC Boards

TGF

CPU