| Version | Echotek Configuration | Driver | MIBPM | Tentative Release Date |
| --- | --- | --- | --- | --- |
| 1 | Solve potential configuration problem with TGF for MI |  |  |
| 1.1 |  |  | Closed orbit only measurements at 500 Hz. Display and profile buffer support. Data access through front-end login only. Requires: Working closed orbit configuration! | Oct 17 |
| 1.2 |  |  | Closed orbit access through FTP. Requires: There are issues not yet solved from the TBPM software to get FTP > 15 Hz. | Oct 19 |
| 2 | Check turn-by-turn configuration. |  | System can change to turn-by-turn mode without reloading Echotek configuration. Requires: Changes on layer above driver (EchoTekPool class) for changing board configuration (e.g. Single/DMA, burst count, active channels). | Oct 25 |
| 2.1 |  |  | Provide means to take one turn-by-turn measurement and have the data through front-end login. Requires: Data from the echotek has to be processed and stored in the turn-by-turn buffer. | Nov 1 |
| 2.2 |  |  | Make tests proving that turn-by-turn data (12K turns) from 10 Echotek boards can be readout within 500 milliseconds window. Requires: Driver and EchoTekPool class read out support. | Nov 4 |
| 2.3 |  |  | ACNET access to turn-by-turn data (state 0). Requires: Implementation of routines for responding to ACNET requests (packing data according to specifications). Creation of turn-by-turn ACNET devices. | Nov 8 |
| Version | Echotek Configuration | Driver | MIBPM | Tentative Release Date |
| 2.4 |  |  | Ability to select 2.5 or 53 MHz data. Requires: Access to transition module through TGF. | Nov 10 |
| 3 |  |  | Change layer above driver to read out N turn-by-turn measurements and fill flash turn buffers. Single state supported (hardcoded sequence of events). Requires: Table for state sequences. State command structure (specifications doc). TGF state programming. | Nov 15 |
| 4 |  |  | Support for multiple states. Definition loaded at startup time or hardcoded. Requires: Buffer management – number of flash buffers assigned to a state depends on the number of injections (information coming from MDAT). | Nov 17 |
| 5 |  |  | State definitions are changeable through ACNET/I6. Requires: Link between ACNET variables and table of state sequences. Changes on I6 application. | Nov 21 |
| 6 |  |  | Implementation of the turn-by-turn (non-flash turn) Requires: Addition of ACNET device for controlling turn-by-turn configuration: delay and bucket number for each state. Check if turn-by-turn is enabled for the current state. | Nov 25 |
| 6.1 |  |  | ACNET access to turn-by-turn (non-flash turn). Possibly already implemented in version 2.3. Requires: Turn-by-turn ACNET devices. Data packing. | Nov 30 |