### Correcting the Accumulator Extraction Energy

- Make a plot of I:VDQ28 (MIRF 2.5 MHz phase detector) vs. time.  This can be done from a FTP or SDA’s plot viewer.

  - To get an FTP triggered at the right time, restore FTP file Pbar 9.

  - To view the SDA plot: open the view called MIRF_Phase_RR_SW.xml, select a transfer (or transfers) from case 7 (Transfer Pbars from Accum to MI for RR).  The resulting plot looks like the figure below:

NOTE:  The above figure shows a pure energy error.  There may be a phase error as well.  The phase error is the value of I:VDQ28 – baseline when beam arrives.  A phase error is corrected by adjusting A:R4MIPS.

- Estimate the phase excursion.

The phase excursion is how far the phase detector swings from the baseline on the first oscillation.   In the figure above the phase swing is about -76.

- Estimate the change to  A:RLLEXF required.

The change required is approximately -1 Hz per +15 of phase swing.  Therefore, the correction required above is:

- Before the markers on the longitudinal display have been frozen, change A:RLLEXF by the amount calculated in step 3.

- Change the MIRF capture frequency:

  - Open I6

  - Load state 20

  - Change the DATUM1 number in row 0 by 84  the number calculated in step 3.  The number to change is circled in the figure below.  After the change has been made, interrupt on *Send to Hardware.

- When the shot is done, update the value for A:RLLEXF in file 13 of the Pbar Annex sequencer.  If A:R4MIPS was changed, that should be updated in the same file.