High Intensity Neutrino Source ACNET Naming Convention

February 18, 2011

In order to facilitate parsing of names by programs and people and the use of templates when defining databases, we have developed a naming convention for all signals that will go into the controls system.   In ACNET there are two names associated with a database entry a long and a short name.  The short name is required because the ACNET protocol has only enough room to accommodate eight characters.  The first two characters designate the machine.   For HINS, this designation is H:

The convention for ACNET long names is:

H:SYS_SubSysX:device:Parameter

The subsystem should help to locate the device which should be what is doing the measurement… bpm, ion gauge, etc. The first letter representing a word should be capitalized.  For example, IG for ion gauge and Int for intensity.  The Xs are optional numbers which should correspond to the numbering convention given by P. Lucas.  For example:  H:BVAC_Kly1Cav1:TP1:I  would be the Current on turbo pump #1 connected to the beam vacuum of Klystron 1’s cavity #1.

The parameter is what is actually being measured … current, voltage, pressure, status, vertical position, etc.

The System name (SYS) will be one of the following:

BVAC		Beam Vacuum			MEBT 	M E Beam Transport

BETA.8(#)	Beta .8 module #		MOD		Modulator

BETA1(#)	Beta 1 module	 #		RFQ		RFQ

BLD		Building			RTL		Rm Temp Linac

CRYO		Cryogenics			RTTC		Rm Temp Test Cav

DMP		Beam Dump			SSR1(#)	Single Spoke Resonator 1

SSR2(#)	Single Spoke Resonator 2

IS 		Ion Source			TC		Test cryostat

IVAC		Insulating Vacuum		TSR(#)	Triple Spoke Resonator

KLY(#)	Klystron #			WTR		Water

LRF 		Low Level RF

SubSystems include one or more combinations of with an optional identifying number:

Bdy		Body				Kly		Klystron

BlckHeat	Black Heat			Mag		Magnet

Cav		Cavity 				RedHeat	Red Heat

Chp		Chopper			RFSw		RF Switch

Circ		Circulator			SCav		SC Cavity

Clctr		Collector			Shtr		Shutter

Col		Collimator			Sol		Solenoid

Cplr		Coupler			Tank		Tank

FerLd		Ferrite Load			Tn		Tuner

HMag		Horizontal Magnet		V		Vertical

HRM		Hot Link Rack Monitor 	WG		Wave Guide

Htr		Heater				Wtr		Water

IQPM		IQ Phase Modulator		Xfmr		Transformer

Device names can include the following abbreviations and may have additional descriptions and/or numbers.   The device should tell you what is doing the measurement:

AFM		Air Flow Meter			Mtr		Meter

BLM		Beam Loss Monitor			Mon		Monitor

BPM		Beam Position Monitor		PG		Pirani Gauge

BV		Beam Valve				PS		Power Supply

CC		Cold Cathode				PsSw		Pressure Switch

CT		Current Transductor

Dr		Door 					RFSw		RF Switch

FM		Flow Meter				RTD		Resistive Temp Dev

HS		Humidity Sensor			Sw		Switch

IG		Ion guage				Tc		Thermocouple

IP		Ion Pump				Tor		Torroid

Int		Interlock				TP		Turbo Pump

Mag		Magnet				 VV		Vacuum Valve

Parameter names can include combinations of these types of things:

Flow		Flow					PW		Pulse width

Fwd 		Forward				Pwr		Power

HP		Horizontal Position			Ps 		Pressure

Hum		Humidity				Ref		Reflected

I		Current (amps)			St		Status

Int		Intensity				T		Temperature

In		Input 					Tm		Time

Out		Output					V		Volts

P		Position				VA		Volt Amps

Ph		Phase					VP		Vertical Position