Fermilab/AD/MI

Date 1 Sept 2005

Version 1.2

Main Injector Beam Position Monitor System (MI BPM)

VME Chassis Specification

Bob Forster

# Introduction

The following is to be considered the minimum specification to be applied to each
”MI BPM Project VME Chassis".

# Quantity

The total number of chassis to be ordered is 11.

# General Requirements

Each chassis is a 19” rack mount VME64x powered enclosure with:

- 6U by 160 mm front vertical orientation 21-slot card cage with top and bottom front inject/eject extrusions.

21-slot monolithic standard VME64x J1/J2 (no J0) backplane with

  - 5 row, 160 pin DIN connectors with  5 mm pin lengths in all J1 slots 
with  no rear P1 shrouds installed.

  - 5 row, 160 pin DIN connectors with 17 mm pin lengths in all J2 slots 
with the rear P2 shrouds installed.

  - On-Board Termination, automatic Bus Grant/IACK jumpering in all slots.

  - Install top and bottom transition card guides mating with the rear of the
backplane slots.

  - The backplane is mounted left-justified in the chassis, so the lowest numbered slots are leftmost when facing the front of the chassis.

- A full 21-slot width backplane stiffener.

- A full 21-Slot width +3.3V/+5V/Ground backplane power busbar set.

- Real-time monitoring and remote control (minimally over Ethernet) of system power, system cooling and individually monitored fan speeds.  To permit control of system power, the status monitor/control system must be independently powered.  Password protected user programming of default alarms and limits parameters and must be off-the-shelf available through the Ethernet port.

- A front panel chassis mounted alpha-numeric LED (or better) display must be provided as a local visual system status monitor interface.

DC fans with tachometer outputs must be used, arranged to provide a bottom front input to rear output air path as follows:

  - Solid top and bottom chassis panels allow placement of immediately
adjacent hardware without affecting internal chassis airflow patterns.

  - Fan(s) draw ambient room air in thru a filter near the bottom of the front panel of the chassis.

  - Fan(s) push air up, bottom to top, across the inserted modules in a fairly laminar airflow pattern.

  - (Other) Fan(s) exhaust air from the top of the back panel of the chassis, achieving a push/pull effect, bottom/front to top/rear.

  - Each fan speed is monitored and controlled by a system status monitor (refer to Requirement 5 above).

- At least three Temperature Sensors.  Given the minimum set of three, they shall be placed (or be placeable) as follows:

  - Two mounted in the frame above the card cage, and

  - One mounted in the exhaust air path,

all connected to, and report through the system status monitor (refer to Requirement 5 above).

- Autoranging Input Power Supply, providing at least 60A of +3.3V, 115A of +5V, 
10A of +12V, and 4A of -12V when powered by 60Hz,110VAC.

- Front panel mounted Main Power and System Reset switches, with front panel main power ON indicator LED.

- Chassis mounted metal carrying handles.

- Fully assembled, wired, tested, with minimum length 6 foot 110VAC power cord for and ready to use.

# Special Requirement

If a closed rear panel is provided on the chassis (preferable in a push/pull air cooled system), then one hole for a vertically oriented DB25 connector must be made in the panel behind card slot 2 or slot 3, near the bottom of the transition card area.  Clearance holes for standard mounting screws must be included as well.

# Although not required, it will be counted as an advantage if :

- The card cage were recessed on the order of 2" from the front of the chassis.

- Users could establish local communications with the chassis monitor using a front panel ethernet or USB2 port.

- Power supplies and/or fan trays are swappable without dismounting the entire card cage assembly.

# Delivery Schedule

One chassis shall be delivered first for approval, the rest within 4 weeks of approval.

# Acceptance Criteria

Delivered chassis must meet manufacturer specifications.  Incoming acceptance testing at Fermilab will be performed by the PREP Equipment Pool staff.

# Examples of Similar Models Recently Purchased by Fermilab

DAWN Part Number 11-1010638-13

Weiner Part Numbers : 0B02.0025

# Change Log

| Version | Issue Date | Concurrence | Description of Change |
| --- | --- | --- | --- |
| 1.0 | July 18, 2005 | RGF | Original. |
| 1.1 | July 22, 2005 | RGF | Slight Editorial Changes. |
| 1.2 | Aug 29, 2005 | RGF | Add Rear DB25 Connector. |

# Concurrence

The following persons concur with this document.

Steve Wolbers, Project Manager	(date)

Bob Webber, Project Manager	(date)

Vince Pavlicek			(date)

Manfred Wendt			(date)