HINS Klystron Operation

5/01/08

Bruce Hanna & Jim Steimel

Version 6.0

I. Check that the LCW is on and that flows are reasonable. These can be checked on the Water System Parameter Page.

A. Flows as of 4/8/07:

1. Klystron Body Flow --- 5.4 gal per min (minimum value = 5.3 gal/min)

2. Klystron Collector Flow --- 42 gal per min (minimum value = 39.6

gal/min)

3. Electromagnet Flow --- 4 gal per min (minimum value = 2.6 gal/min)

4. Ferrite Load 1 Flow (actually 6” coaxial line load flow) --- 13.8 gal per min (minimum value = 9.2 gal/min)

5. Circulator Flow --- 4.5 gal per min (minimum value = 4.4 gal/min)

II. Check the Waveguide status

A. Will the klystron need to be operated at power levels greater that 500kW?  If so, follow the “Configuration Control of HINS Waveguide Switch for Protection of 6” Coaxial Line and Load during High Power Operation” procedure.

B. Is the Waveguide Switch, located next to the waveguide to coax coupler, in the correct position?

C. Does the 800W klystron driver amplifier have 22dB of attenuation on its output?  If not, the Waveguide Switch should be locked in the test area position.

D. Is the Waveguide Shutter, located next to the RF Cage, in the correct position?

E. Is the RF Cage interlock made up (for test area operation)?

F. 3” coaxial switch position:

1. For operation to the cage the switch must be in the

dummy load position (position 2 at the switch).

2. Check that the LCW is valved in at the coax loads.

3. Check that there is >5 psi of air pressure in the coaxial line; gauge is above the relay rack next to the console.

G. Is the cave secure? (For test cave operations)

1. If running to the cave check that the RF loads have their LCW valved in and that the coax line has >5 psi of air pressure in it.

H.Is the safety system made up?

III. Turn on the Filaments

A. Turn on the Black Heat

1. Is the black heat on? If so voltage will be about 86.5 volts. If not follow

the next steps

2. Reset the modulator to clear all PLC trips

a. can be done at the modulator VME crate or through the controls

system

3. In back of the filament supply set the Black Heat Pot to 0.

4. Set the front panel switch on the supply to Black Heat (down position).

5. Turn the Supply front breaker on (breaker is on the right side labeled

Heater Power Enable)

a. if the light does not come on check the Ion pump latches named

PD_KLY1:Kly1IP:Sw:L and PD_KLY1:Kly1:IP:IL ; both

should be 0

b. Ion pump value ; PD_KLY1:Kly1:IP:I should be about 9.7 volts

6. Knob the pot in the back of the supply until the filament voltage reads

85 Volts

a. Increase the knob slowly; take about 5 minutes to get to the final

value.

b. Monitor the Klystron vacuum either watching the supply at the

top of the relay rack or plot PD_KLY1:Kly1:IP:I, the filament

supply trips off if the IP voltage goes below 6.7 volts ( the mod

HV trips if the IP voltage goes below 7.14 volts)

c. The black heat will take 15 minutes to time out and the voltage

must be above 85 volts to start timing

d. You can monitor the time from PD_KLY1:BlkHeat:Timer:Tm

e. When the Black Heat is timed out

PD_KLY1:BlkHeatTmOut:Timer:L will go from 0 to 1.

B. Turn on the Red Heat by flipping the front panel switch to the Red Heat

Position.

1. The voltage should go up to 124 volts. Initially the current will go to

about 2.9 amps but will quickly go to 2.45 amps.

2. Red Heat takes 60 minutes to time out

a. time out begins when the current is between 2.1 and 2.55 amps

b. Elapsed time can be monitored by looking at the parameter

PD_KLY1:RedHeat:Timer:Tm.

c. When the time out is finished the parameter

PD_KLY1:RedHeat::Sw:St will change from 0 to 1.

IV. Turn on the Solenoids.(Note; filaments do not need to be timed out to do this)

A. Flip all three of the 208V/10A breakers on

B. Currents and voltages for the Solenoids (all supplies should be in I-mode):

1. Solenoid 1: 16V/17A

2. Solenoid 2 : 232V/14A

3. Solenoid 3 : 59V/14A

V. At RR PD-R5 (timing rack) insure that EVC from GP-IP Clock Generator (slot 5 and 6 in VME crate) connects to “VAR Rate M” BNC connector on the TESLA Rep Rate Generator and that the Rate M dial setting is set to desired rate (settings of 3,4,5, and 6 correspond to 2 Hz, 1 Hz, 0.5 Hz, and 0.2 Hz respectively).  The modulator rep-rate limiter will not allow rep-rates faster than 2.5 Hz.

V. Modulator Turn on

A. Insure the rf is inhibited

1. Look at the top status light in slot 2 of the rf VME crate in RR PD-R4(

labeled rf-inh); it should be off.

2. From the console:

a. Double click on HINS EDM icon

b. On PD main page on the top left under “325 MHZ Klystron”

click on “Interlocks”

c. Under “System Control” column (first column)click on “RF

ON/OFF” to make it red and indicate off.

3. Set the RF attenuator in RR PD-R3 to a value greater than 11.

B. Modulator Turn On Procedure

1. Reset of modulator controls can be done from the console by:

a. From the HINS main page click “Modulator Controls” box.

b. Check that the modulator pulse is disabled.  The “Pulse Enable/Disable” radar button should be red.  If not, press the “Pulse Inhibit” button.

c. Reset box is in lower right hand side of the display.

1) if all trips clear the four of the six status boxes at the top right side of the display will turn green.  Press the red “Klystron Support” button on the control page.  The only red box under the “Current” column should be “Capacitor Bank Below Normal”.

2) all the light on channels 0-20 for the cards in slots 1,2

and 3 should be green in VME crate in RR PD_R2.

3. Check the modulator settings; “Charge Supply Reference” voltage should be 7.50 kV. The pulse length should be left where it is (4.000 mSecs default); if a different pulse length is needed contact experts.

4. Click the “On” box in the Modulator Control page

a. charging voltage can be read on the left top part of the

Modulator page and is called “Capacitor Voltage (cont)

5. If the charging voltage is increasing, press the “Pulse Enable” button.  Pulsing will not commence until a “Reset” is pressed.

6. Once the charging voltage is past the reference setting, press the “Reset” button.

C. Set the charging supply reference.

1. The charging supply reference will need to be adjusted if more than 1.1 MW of peak power is required from the klystron.  The chart shows the relationship between klystron output power and charging supply reference setting.

2. The charging supply reference needs to be increased slowly while the modulator is pulsing.  From 7.5 kV, increase the reference by no more than 0.25 kV steps.  Allow the modulator 3 or 4 pulses at the new setting before increasing the reference.  At 8.25 kV reference value, reduce the step size to 0.1 kV steps until the desired reference value is reached.

VI. Turn on the RF

A. Check timing

1. From the HINS Main Page, under “325 MHZ Klystron” click on

“Timing”

2. Values as of 4/23/08 with a 3.5 msec rf pulse are:

|  | Delays | Widths | Event | Description |
| --- | --- | --- | --- | --- |
| 0 | 700 | 10 | A7 | Modulator Trig |
| 1 | 3495 | 3500 | A7 | Fwd Pwr Interlk Gate |
| 2 | 3495 | 3500 | A7 | Rev Pwr Interlk Gate |
| 3 | 3425 | 10 | A7 | RF Interlk Digitizer Trig |
| 4 | 3495 | 3500 | A7 | RF Gate |
| 5 | 8320 | 700 | AC | LLRF Gate |
| 6 | 8000 | 10 | A7 | Spectrum Anal Trig |
| 7 | 3425 | 10 | A7 | Scope Trig |

Items in italics are not currently pertinent to klystron operation.

3. . From the HINS Main Page, under “325 MHZ Klystron” click on

“Timing 2”

4. Values as of 4/23/08 for a 3.5 msec rf pulse are:

|  | Delays | Widths | Event | Description |
| --- | --- | --- | --- | --- |
| 0 | 700 | 10 | A7 | A8 – Ion Source Trig |
| 1 | 700 | 10 | AC | A7 – RF Event Trig |
| 2 | 700 | 10 | A7 | A6 – Beam Event Trig |
| 3 | 3545 | 10 | A7 | RF Detector Sample Trig |
| 4 | 3495 | 3500 | A7 | S/H Trig 1 |
| 5 | 500 | 10 | AC | Spare |
| 6 | 0 | 800 | A7 | LLRF Prepulse |
| 7 | 3425 | 10 | A7 | Spare |

Items in italics are not currently pertinent to klystron operation.

B. Check the RF interlocks

1. Pull up the Interlocks subpage from the HINS main page; all “Process”

lines should be green (ignore the red status lines below)

2. Reset if needed

C. Insure the frequency of the RF Generator is set to 325.0 MHz

D. Set the rf level

1. Check the attenuator value on the output of the driver amplifier.  If the

value is 22dB, the klystron power is limited to 500kW.

2.  If the value is only 12dB:

a) If the rf has been off for more than 4 hours you need to start out at 500 kW for 5 min and increment up by 500 kW every 5 minutes.

b) With the Agilent Signal Generator set to +15 dBm and the attenuator  in RR PD-R3 set to 20 (to start) the following plot shows attenuation vs Forward Power for charging supply reference settings of 7.5 kV and 8.5 kV.

3.  For 22dB attenuation on the drive amplifier.  Translate the plot by 10dB to determine klystron output power vs. attenuator setting.

E. From the “Klystron Interlocks” page click on “RF OFF” to turn on the rf

VII. Check that operations is ok

A. Signals from the modulator scope in RR PD-R2 (time base = 400 usec/div):

1.Klystron Current from CH 8 of slot 7 (1V/div)

2.Klystron voltage from CH 8 of slot 8 (2V/div)

3.Load Current from CH 7 of slot 9 (1V/div)

4. Primary current from JR5,cable 6 of slot 5(2V/div)

5. DVM2 should connect to CH 1 of slot 10 and indicates the charging

voltage

B. From the HINS main control page, click on the “RF Distribution” button.  Examine the different power levels at the different locations.

1. If no or very little RF power is detected, check that there are no interlocks in alarm.  Also verify that the “RF Detector Sample Trig” timing channel is set to trigger during the RF gate.

2. Verify that RF is directed to the proper load/s.

VIII. Turn off procedure

A. Inhibit the rf pulse by clicking on the RF On button on the Interlock Page.

1. see section VI for details on how to get to the Interlock page

B. Inhibit the modulator from pulsing

1. Depress the “Pulse Inhibit” button on the Modulator Controls Page.

C. Turn the Modulator off from the Modulator page on the Control System

D. If you will be running the system again in a few hours leave the Red Heat on. If you will not need the system for a few days put the filaments in Black Heat. If the system will not run for 4 or more days turn off the Red Heat, let the system stay there for a few minutes and then slowly, over the course of 3 minutes, knob the black heat to zero and then throw the front breaker.