| LHC-CT-ES-0004 rev 0.1 AB-OP 780566 2006-10-02 |
| --- |
| Functional Requirements |
| TUNE Application – HIGH LEVEL REquirements |
| Abstract The required elements for the Baseband Tune Measurement application are listed, described and explained here. |
| Prepared by : M. Lamont, AB/OP R. Steinhagen, AB/BI J. Patrick, Fermilab D. Nicklaus, Fermilab J. Annala, Fermilab D. Still, Fermilab | Checked by : J-J. Gras, AB/BI L. Jensen, AB/BI E. Hatziangeli, AB/CO H. Schmickler, AB/CO J. Wenninger, AB/OP S. Gysin, Fermilab E. McCrory, Fermilab D. McGinnis, Fermilab | Approved by: R. Jones, AB/BI R. Bailey, AB/OP |
| History of Changes |
| Rev. No. | Date | Pages | Description of Changes |
| 0.1 0.2 0.3 0.4 | 16-April-2007 23-April-2007 26-April-2007 01-June-2007 | 8 8 9 8 | First draft Second draft Third draft Fourth draft |

Table of Contents

1.	Introduction	4

1.1	About this document	4

2.	Application Overview	5

2.1	Objectives	5

2.2	Roles and Responsibilities	5

3.	Functional Requirements	5

3.1	FuNCtionality	5

3.1.1	basic considerations	5

3.1.2	basic measurement and display capabilities	6

3.1.3	tune calculation	7

3.1.4	Data archiving and retrieval	7

3.2	Scope, Performance and Concurrency	8

4.	Discussion	8

5.	References	8

# Introduction

The betatron tune values of each LHC beam are measured by the Base-Band Tune system (BBQ). Pickups in the LHC tunnel provide beam position information. Front-end electronics based on Direct Diode Detection (3D) [1] produces a baseband signal that is presented to a VME based Data Acquisition Board (DAB). The DAB digitizes the input signal and computes Fast Fourier Transforms in real time, and can compute the tune by searching within a prescribed window of each FFT.

Beam excitation for the tune measurement is provided by dedicated tune kickers, or transverse dampers, or dedicated stripline kickers. Control of the latter two is via the DAB.

The application interface to the hardware is through a FESA front-end. The front-end acquires data from the DAB, and can modify configuration parameters for the tune measurement and beam excitation functions it controls. This is through the FESA class BQBBQLHC.

There are two complete systems, each consisting of horizontal and vertical pickups for each of the two beams. The first is used to provide traditional information including position and FFT measurements as well as the measured tune to the control room in response to beam excitation of finite duration. The second is a dedicated Phase Locked Loop (PLL) system. This system measures and tracks the tune generally in response to low level continuous excitation. As variations occur, the PLL system sends tune and coupling measurements to the orbit feedback controller for its use in computing corrections to stabilize the beam. All electronics, DAB firmware, and FESA software are the same for both systems. Data from both these systems will be acquired and displayed by a single application.

## About this document

The functional requirements for the Base-Band Tune Application are listed and described here. It is anticipated that this software application will be used by AB/OP and others in the CERN Control Centre during the commissioning and operation of the LHC.

This application will be written by the LAFS team at Fermilab. Fermilab personnel will be present at CERN as needed during the writing, commissioning and operation of this application. The FESA interface to the hardware is provided by the AB/BI/SW group.

First, we present an overview of the application; the objectives, the roles and responsibilities. Then we present the formal requirements.

The priorities of the requirements are listed as either “Critical” or “Expected.” The former means that the application absolutely must have this feature. The latter means that the application should have it, bit it will not be necessary in the initial version(s) of the application.

# Application Overview

## Objectives

The tune application provides the operator interface for measuring the tune of the LHC beams. Excitation parameters are configured and a measurement initiated. The application acquires FFT and tune data from the front-end, computes tunes, displays the data, and may optionally store and retrieve information. The same application reads and displays data from the PLL system. This application is intended to provide tune measurement functionality needed for routine operation of the LHC. It will also be used to measure the chromaticity via RF modulation techniques. Separate expert applications will exist that provide access to additional features of the system.

## Roles and Responsibilities

The BBQ FESA front-end interfaces with the DAB, which in turn interfaces to the BBQ electronics, the damper and strip-line exciters, and the feedback system. Configuration of the tune kicker is through this application but via a separate front-end. There is interaction with the timing system to synchronize firing the tune kicker with data acquisition. Interaction with the timing system may also be required for synchronization of tune measurements with injection and with RF manipulation for chromaticity determination.

# Functional Requirements

The functionality and the scope, performance and concurrency of the tune application are discussed and presented in this section.

## FuNCtionality

The functionality of the tune application is listed here.  It is divided into 5 sections, based on the general capabilities required.

### basic considerations

The tune application will be written using the standard LSA framework. It is possible the required data rate will necessitate making use of a faster direct communication protocol between the front-end and application. Here a JAPC/CMW call would be made to the front-end to configure a direct data path to the application. Data would be sent over this path following the protocol used for the orbit feedback system.

| Num | Title | Description | Priority |
| --- | --- | --- | --- |
| 1.10 | Common | The tune application shall be written in the standard LSA architecture. | Critical |
| 1.20 | Look and Feel | The tune application shall have the standard LSA look and feel. | Critical |
| 1.30 | Communication | The application shall follow standard JAPC/CMW and real-time feedback communication protocols. | Critical |
| 1.40 | Security | The application shall use Role-Based Access Control for authentication and authorization | Critical |

Table 3-1, General requirements.

### basic measurement and display capabilities

The tune application is responsible for performing tune measurements. Excitation and other parameters are configured, the measurement is initiated, and data are read and displayed. The following modes of operation are possible:

Tune-FFT system:

- Monitoring of spectra with no excitation

- Measurement from single kick excitation by tune-kicker

- Measurement from chirp excitation via transverse damper

Tune-PLL system:

- Monitoring of spectra with no excitation

- Measurement from continuous excitation via transverse damper

- Measurement from continuous excitation via stripline

| Num | Title | Description | Priority |
| --- | --- | --- | --- |
| 2.05 | Excitation Control | The tune application shall allow the operator to select the beam excitation method from none/tune kick/damper/stripline | Critical |
| 2.10 | Excitation Control | The tune application shall allow the operator to set parameters associated with the selected excitation method including the strength and duration. | Critical |
| 2.15 | Front-end, DAB, and PLL Control | The tune application shall not allow setting of BBQ front-end, DAB or PLL parameters. It will be assumed that the defaults are suitable for normal operations. | Expected |
| 2.20 | Data | The tune application shall acquire FFT data from the FFT system, and tune and coupling results from the PLL system, for each beam. | Critical |
| 2.25 | Data Display | The tune application shall display the most recently measured tune and coupling values, and excitation parameters. | Critical |
| 2.30 | Time Display | The tune application shall plot the measured tunes as a function of time. | Critical |
| 2.35 | Resonance Line | The tune application shall display the measured tune as a function of time on a resonance line plot. | Expected |
| 2.40 | FFT Display | The tune application shall be able to plot single FFT spectra with the tune peak noted. | Critical |
| 2.45 | FFT Data Display | The tune application shall plot the FFT spectrum as a function of time as a contour or waterfall plot. It should be possible to select a slice from this plot for detailed display. | Expected |
| 2.50 | 3-D display | The tune application shall provide a full 3-D display of the FFT versus time. | Expected |
| 2.55 | Chromaticity | The tune application shall be able to initiate an RF modulation sequence and compute the chromaticity from the resulting tune measurements. | Expected |

Table 3-2, Measurement and Display Capability Requirements.

### tune calculation

The tune application shall be able to recalculate the tune from an FFT with modified peak search parameters. This serves as a cross check on the computation performed in the DAB.

| Num | Title | Description | Priority |
| --- | --- | --- | --- |
| 3.10 | Calculation | The tune application shall be able to recalculate the tune from the FFT using possibly modified search parameters | Critical |
| 3.20 | Coupling Calculation | The tune application shall calculate the coupling by examining data from both planes when the beam is excited in one plane | Expected |
| 3.30 | Chromaticity | The tune application shall be able to initiate an RF modulation sequence and compute the chromaticity from the resulting tune measurements. | Expected |

Table 3-3, Tune Calculation requirements.

### Data archiving and retrieval

It should be possible to store and retrieve FFT and tune data. The tune application should be able to log tune values it has computed, and be able to read files generated by the post-mortem system. It does not itself produce post-mortem files.

| Num | Title | Description | Priority |
| --- | --- | --- | --- |
| 4.10 | Data Storage | The tune application shall be able to archive blocks of FFT data in some standard format under operator control. | Critical |
| 4.20 | History | The tune application shall be able to read and display the archived data. It shall be possible to apply different peak search parameters to the data and redisplay it. | Critical |
| 4.30 | Logging | The tune application shall log calculated tunes to the logging system. | Critical |
| 4.40 | Post Mortem | The tune application should be able to read and display tune data the Post-Mortem system | Expected |

Table 3-4, Data Archiving and Retrieval requirements.

## Scope, Performance and Concurrency

| Num | Title | Description | Priority |
| --- | --- | --- | --- |
| 5.10 | Scope | The scope of the tune application shall be limited to the BBQ hardware and beam excitation controllers attached to the BQBBQLHC front-end, and the interaction with the user to manipulate these items. It shall not be required to interact directly with other application software. | Expected |
| 5.20 | Performance | The tune application shall be able to display the data that are produced by the front-end in real time. | Expected |
| 5.30 | Concurrency | More than one instance of the tune application may run simultaneously. But it is acceptable for one of these instances to initiate a “lock” on control of the beam excitation hardware. | Expected |

Table 3-5, Scope, performance and concurrency.

# Discussion

# References

  - LHC-Project-Report-853 “The Principle and First Results of Betatron Tune Measurement by Direct Diode Detection”.

  - LHC-B-ES-0009 (EDMS 463763) “On the Measurement of Tunes, Coupling, and Detunings with Momentum and Amplitude in the LHC”.

# Text boxes

CERN

CH-1211 Geneva 23
Switzerland

the
Large
Hadron
Collider
project