Dark Current Kicker with Pulsed Magnet
C.Y. Tan
J. Steimel

---
Goal
To see whether power requirements are smaller with a pulsed magnet.
  - Use Tevatron D48 pulsed magnet kicker as basis for calculation.
  - Use same beam pipe aperture of 2.5” OD.
  - D48 is a ferrite loaded picture frame magnet.

---
Picture Frame Magnet
Length of kicker is assumed to be 25 cm.
Aperture is 2.5”.

---
Results
For 20 mrad kick we need
  - 37 A current
  - Impedance is 6.25 (assuming 60kV)
  - Peak power is 8.6 kW
  - Average power is 650 W. (assuming pulse on is 25ns and 3MHz rep rate).
Filling time is 25 ns

---
Comparison with stripline kicker
Peak power is 360 kW.
Average power is 2 kW.
Fill time is 2 ns.
Ratios:
  - Peak power stripline/Peak power magnet = 42
  - Ave power stripline/Ave power magnet = 3
  - Fill time stripline/Fill time magnet = 1/12.5
From power considerations, it seems that pulsed magnet is the way to go.

---
Advantages
Power advantages is factor of 3 for averaged power and 42 for peak power.
We have pulsed magnet experts.
Everything is external to the beam pipe.

---
Possible problems
Vacuum because of ceramic beam pipe.
  - A0 gun vacuum is 10-9 torr.
  - c.f. Tevatron ceramic beam pipe vacuum. Note much longer than what we will have at NML. (About 10 m worth of ceramic beam pipe vs 30 cm)

---
F17 Kicker Vacuum Recovery
2.5 days
2e-8 torr
15 days
Magnet replacement