Comparing the Dark Current Kicker and the ILC Damping Ring Kicker Specifications
C.Y. Tan
J. Steimel

---
The Specifications
FID Technologies Pulser meets most of the dark current kicker requirements except for jitter. Cost is > $100k.
Mark Palmer's +/- 1kV version $67k.
+/- 10kV version $250k
Reliability?

---
Kicker Design
Many labs looking into kicker design:
  - SLAC (Krasnykh), ATF (Stefano), Frascati, KEK.
Known difficulties:
  - Feedthru's unreliable at these voltages.
  - Bandwidth ~ 1GHz.

---
What do we want to do?
Build a “Damping Ring Kicker” test kicker at NML?
  - Build a kicker that is capable of taking +/- 10kV peak and 1GHz bw.
  - Modify a design from one/all of the labs.
    - Length is about right 30cm.
Concentrate on building a prototype kicker on the bench rather than the pulser.
  - Test and install at NML. Build it and they will come?