# Conversions Between the 1970 and 2007 Booster Correctors

Version 1.2

Craig Drennan

July 19, 2007

## Introduction

This note describes the conversion between the 1970 Booster corrector elements and the new correctors we will be installing in 2007 and 2008.  Estimates are made of the ratio of the current needed in the new magnets to the the amount of current in the old magnets that produces fields of the same strength.

The references available for making this determination are given below.  Also, measurements of the field strength of the older corrector magnets were performed at the magnet test facility.  There is an open request for other or better references.

- R. E. Juhala, “Booster Correcting Magnets”, Fermi Note FN-206, February 23, 1970. (copy available at Fermilab Beams-doc-1881-v5, 2006, http://beamdocs.fnal.gov/ )

- E.J. Prebys, et al., “Booster Corrector System Specification”, Fermilab Beams-doc-1881-v5, 2006, http://beamdocs.fnal.gov/ .

The Amp to field transfer functions for the 1970 correctors is taken from Table 1 of Reference 1.  The numbers for the new correctors, and information about the old sextupoles, come out of Reference 2.

**Note:  The Inner Dipole is the Horizontal Dipole and the Outer Dipole is the Vertical Dipole.

## Dipole Comparison

Old Horizontal Dipole Transfer Function From FN-206

Old Horizontal Dipole Transfer Function From TD Measurements

New Horizontal Dipole Transfer Function

Old Vertical Dipole Transfer Function From FN-206

Old Vertical Dipole Transfer Function From TD Measurements

New Vertical Dipole Transfer Function

## Quadrupole Comparison

Old Normal Quadrupole Transfer Function From FN-206

Old Normal Quadrupole Transfer Function From TD Measurements

New Normal Quadrupole Transfer Function

Old Skew Quadrupole Transfer Function From FN-206

Old Skew Quadrupole Transfer Function From TD Measurements

New Skew Quadrupole Transfer Function

## Sextupole Comparison

The comparison is based on information from reference 2.  Note that the arrangement of sextupole magnets in the accelerator will be different than before.  The scale factor derived here takes into account that for a given plane (horizontal or vertical) the new system will you 24 magnets where the old system used 12 in the horizontal plane and 9 in the vertical plane.

Also, We assume that the scale factor for both the Normal and Skew sextupoles are the same.

Old Horizontal Sextupole Transfer Function

New Horizontal Sextupole Transfer Function

Old Vertical Sextupole Transfer Function

New Vertical Sextupole Transfer Function

## Summary and Scale Factors

From FN-206.

| Element | Old Amps / (Field) | New Amps / (Field) | Scale Factor Amps New / Amps Old |
| --- | --- | --- | --- |
| Horizontal Dipole | 1080 | 2711 | 2.51 |
| Vertical Dipole | 1867 | 2693 | 1.44 |
| Normal Quad | 45.91 | 400.0 | 8.71 |
| Skew Quad | 112.5 | 250.0 | 2.22 |
| Horz. Sextupoles | 5.59 | 1.128 | 0.202 |
| Vert. Sextupoles | 2.963 | 1.128 | 0.381 |

From TD Measurements

| Element | Old Amps / (Field) | New Amps / (Field) | Scale Factor Amps New / Amps Old |
| --- | --- | --- | --- |
| Horizontal Dipole | 1075 | 2711 | 2.52 |
| Vertical Dipole | 1923 | 2693 | 1.40 |
| Normal Quad | 48.08 | 400.0 | 8.32 |
| Skew Quad | 117.6 | 250.0 | 2.13 |