Gap Cleaning in the MI using RF Barrier

W. Chou, D. Wildman, J. Griffin and K-Y. Ng (February 29, 2008)

- Goal: To clean the two gaps on each side of the slip-stacked proton batch used for pbar production (Figure 1, courtesy P. Adamson) so that the 120 GeV extraction losses at MI-52 could be reduced.

Figure 1: Illustration of the method of using RF barriers to clean the extraction gaps.

Figure 2: RF barriers generated by the MI barrier RF cavity.

- Method: To accelerate/decelerate the particles in the two gaps by means of the RF barrier. There are two routes for the gap particles to get lost before reaching 120 GeV:

  - Those knocked out of the RF separatrix would immediately get lost at 8 GeV when acceleration starts.

  - Those remaining inside the RF separatrix will fill up the RF bucket to form a “fat” bunch (i.e. with large longitudinal emittance).  Part of them would be lost at the beginning of the acceleration when the RF bucket starts to shrink. Another part would be lost during transition crossing.

Some residuals could still reach 120 GeV. But the number would be much smaller than what we have now.

- Calculations:

Beam energy: 		E = 8.938 GeV

Slip factor: 		( = 8.88 ( 10(3

RF voltage: 		V(rf) = 1.1 MV

RF frequency:		f(rf) = 52,811,400 Hz

Harmonic number: 	h = 588

Bucket half-height: 	ΔE(bucket) = 34.4 MeV

Bucket area: 		A(bucket) = 0.83 eV-s

Synchrotron tune:	((s) = 0.0102

Synchrotron period:	T(s) = 98 turns = 1.1 ms

Gap width:					D = 600 ns (30 buckets)

Barrier rise/fall time:				dt = 20 ns (( D

Barrier voltage:				V(barrier) = (16 kV

Barrier width:					L(barrier) = 500 ns

No. turns to move beam by ΔE(bucket): 	n = ΔE(bucket) / V(barrier)

= 2150 turns

= 24 ms

- Procedure:

- After the completion of slip stacking, turn on the RF barrier such that the positive voltage (acceleration) pulses in one gap and negative (deceleration) in another gap (Figure 1).

- Each pulse is 16 kV in height and ~500 ns in width.

- Keep the RF barrier on until acceleration starts and then turn it off. (This gives us ~50 ms, corresponding to ~70 MeV acceleration or deceleration, which should be enough to knock most of the gap particles out of the RF bucket.)

- Compare the losses at 120 GeV at MI-52 (521B and 522A) with and without the RF barrier.

This will be a relatively simple and quick experiment. We already have all required equipments (hardware and software) in place (Figure 2).