Ecloud Energy Distribution
C.Y. Tan
24 Sep 2009

---
Setup
Picture is from Bob's talk at Project-X Meeting
RFA1
RFA3
RFA2

---
Data taken on 16 Sep
RFA3 signal ~10x smaller than RFA1. Beam current is 12e12.
RFA1 signal about -150mV peak
Amps off
BPM signal
RFA1 amps off
RFA2,3 amps on

---
Interesting Structures
-200V on grid, amps on
-250V on grid, amps on

---
Energy Spectrum
RFA2,3 amplified.
Ignore 0-20eV?
Max energy around 40-50eV.
Definition of fraction:
Qtot = all the charge in the time slice 1 to 1.05 s at "0" volts
   Fraction = total Q in energy slice (e.g. 20 to 30V) in time slice 1 to 1.05s /(Width of energy slice * Qtot).

---
Data taken on 18Sep
Beam current 30e12, RFA3 only 2x smaller than RFA1
No amps, grid -20V
No amps,
grid -280V

---
Zoomed in data
Grid -450V, no amps.

---
Ecloud Energy Spectrums
Distribution around 1 to 1.05s, near max dip.

---
Zoomed in Energy Spectrum (Dip1)
0.934 to 0.941 s

---
Zoomed in Energy Spectrum (Dip2)
0.941 to 0.948 s

---
Conclusion
- Electron energy spectrum is independent of coating.
  - Electrons which get off the surface will be accelerated the same way by the beam.
- If I believe the measurement then the distributions show that
  - Coating does not change the work function!
  - Coating only reduces the number of electrons coming off the surface.
  - Unless there is a longitudinal redistribution of the electrons!