HINS 2.5 MeV Beam Pre-Commissioning Checklist

12/3/2009

## RFQ Commissioning Work

  - Check that resonant drift phenomenon has been fixed. (Done and fixed)

  - Study LLRF system operation on RFQ. (Done for now)

- Arrange for x-ray monitoring as RFQ power is increased (after mating to ion source).

- Re-condition RFQ for spark free operation with RF only.

  - Commission RFQ PLL and verify frequency tracking.

  - Commission mechanical tuner control.

## Mechanical Work

  - Remove extra diagnostics from ion source beam line. (Done)

  - Mate RFQ and ion source according to Henryk’s procedure. (Done)

  - Mate RFQ to diagnostic and dump line while vacuum in RFQ is down. (Done)

  - Perform alignment of RFQ, ion source, BPMs, and wire scanners while pumps are off.  (Done)

  - Start all vacuum pumps according to Henryk’s procedure. (Done)

  - Install replacement valve for MP7 water skid and recommission water temperature control loop. (Mechanical work complete.  Still verifying operation)

  - Complete repairs and upgrades of MS6 system.

## Low Level Electrical Work

- Install RFQ RF fanback distribution box and install cables.

- Calibrate front panel RF diagnostic signals and RF detectors.

- Install control cable for RFQ mechanical tuner.

## Interlocks

- Upgrade hardware of RF interlock chassis. (Started, status unknown)

- Test RF interlocks and examine RF amplitude issues.

- Fix beam dump flow switch. (Done)

- Install and test 2.5MeV line vacuum valve position sensor.

- Bypass RFQ water flow interlocks for water free operation.

- Re-test RFQ and 2.5 MeV line water interlocks.

- Modify and verify klystron modulator pulse rate limiter to disable all pulse rates above 1Hz.

## Controls

- Install pulse shifter box for 2.5 MeV beam on/off control.

- Make names and add new RF detectors to EPICS database with calibration coefficients.

- Edit RFQ screen to show correct values for vanes water return temperature.

- Edit water distribution screen to show updated distribution, values, and interlocks.

- Edit RF distribution screen to show updated distribution and detectors.

- Re-establish remote operation of RF signal generator.

## Instrumentation

  - Calibrate 2.5 MeV line BPM cables.

  - Set up hardware (oscilloscope) for BPM beam energy measurement.

  - Repair 2.5 MeV beam dump wire chamber.

  - Test toroid data acquisition system.

  - Check that wire chamber data analysis software can provide beam density data.

  - Test wire chamber data acquisition system.

## Documentation

- HINS Test Facility at Meson System Overview of Hazards (Draft Complete)

- HINS 2.5 MeV Beam Commissioning Plan (Draft Complete)

- Fermilab HINS Program 2.5 MeV Beam – Design, Operations, and Safety Assessment (Draft Complete)

- HINS Aluminum Coil Beam Absorber Heating Analysis (Draft Complete)

## Inspection

- Arrange for inspection and approval of 2.5 MeV beam line and documentation.

- Arrange for x-ray monitoring as RFQ power is increased and beam intensity is increased.