Pre-injector Upgrade Updates
(26 May – 09 Jun 2010)
C.Y. Tan
09 Jun 2010

---
Source Status

---
LEBT Status

---
MEBT Status

---
RFQ Status
- Waiting for output emittances and Twiss params.
- PS for RFQ is here. Installed upstairs.

---
RFQ PA
RFQ PA from ANL is in the linac gallery.

---
Test Stand
- Room has been cleaned up.
  - After beam line layout (progress?)
    - Water – Bob Slazak
    - Electrical – Jim Ranson
- Need to test LEBT before RFQ connection
  - Wires, toroids at the end of the LEBT, same position as the RFQ.

---
Safety
When can the beam line layout in test area be done?

---
Controls
Mike Kucera will need to be involved.

---
RFQ reminders
- Schempp is vendor
  - Make sure that the vanes are cleaned! See ISIS email.
    - Some cleaning details supplied by ISIS.
  - Review and verify on site mechanical design and construction (already in contract).
- Add current transformers at beginning and end of RFQ. (Save space in MEBT).
  - Once vendor is finalized, we have to design “ends” of the vacuum structure.