Pre-injector Upgrade Updates
(09 Jun – 30 Jun 2010)
C.Y. Tan
30 Jun 2010

---
Source Status

---
LEBT Status

---
MEBT Status

---
RFQ Status
- RFQ input power will be on the left w.r.t. the beam direction. Tuners will be on the other side. (16 June 2010)
- Coax cables need to be ordered for PA to RFQ.
- Waiting for output emittances and Twiss params. Have contacted Schemmp.

---
Test Stand
- Room has been cleaned up.
  - After beam line layout (progress?)
    - Water – Bob Slazak
    - Electrical – Jim Ranson
- Need to test LEBT before RFQ connection
  - Wires, toroids at the end of the LEBT, same position as the RFQ.

---
Safety
When can the beam line layout in test area be done?

---
Controls
Mike Kucera will need to be involved.

---
RFQ reminders
- Schempp is vendor
  - Make sure that the vanes are cleaned! See ISIS email.
    - Some cleaning details supplied by ISIS.
  - Review and verify on site mechanical design and construction (already in contract).