Pre-injector Upgrade Updates
(13 Jul – 18 Aug 2010)
C.Y. Tan
18 Aug 2010

---
Source Status

---
Pulser
Volts (*103)
Waiting for safety approval.

---
LEBT Status

---
Solenoid Drawings

---
Talk to Sasha about end flanges

---
MEBT Status

---
Buncher

---
MEBT Quad (preliminary)
Parameter	Units	Value
Quadrupole gradient	T/m	39.25; 31.11;16.85
Pole tip radius	mm	20
Quadrupole effective length	mm	45
Quadrupole integrated gradient	T	1.77; 1.4; 0.76
Dipole corrector integrated field	T-m	0.006
Copper conductor dimensions	mm	5.0 x 5.0, ø3.0
Copper area	mm2	17.64
Quadrupole number of coil turns		4
Dipole number of turns		2
Quadrupole peak current at 1.77 T int. gradient	A	650
Dipole peak current at 0.006 T-m int. field	A	650
Current pulse form		60 Hz half sine wave
Repetition rate	Hz	15
R.M.S. current factor		0.0884
Quadrupole and dipole r.m.s. current	A	57.5
Current density	A/mm2	3.25
Quadrupole and Dipole inductances	µH	83; 2.3
Quadrupole and Dipole DC resistances	Ω	0.7; 0.13
Quadrupole and Dipole Inductive voltages	V	20.3; 0.6
Quadrupole and Dipole power losses	kW	2.5; 0.5
Number of water circuits		2
Water pressure drop	atm	5.0
Water flow	l/min	3.0
Water temperature rise	°C	14

---
RFQ Status
- RFQ input power will be on the left w.r.t. the beam direction. Tuners will be on the other side. (16 June 2010)
- Coax cables need to be ordered for PA to RFQ.
- Simulation shows 80% capture at end of DTL1 with RFQ parameters.
- We should ask Schempp for progress report.

---
Trace3D Simulation
For the DTL model that we have, 80% capture requires this emittance at the entrance of the DTL.
Asssume 60mA beam output from RFQ.

---
Trace3D/Parmila Simulation
Interesting difference between Parmila and Trace3D at the end of the half quad.

---
End of Tank 1, 80% capture.

---
Test Stand
- Room has been cleaned up.
  - After beam line layout (progress?)
    - Water – Bob Slazak
    - Electrical – Jim Ranson
- Need to test LEBT before RFQ connection
  - Wires, toroids at the end of the LEBT, same position as the RFQ.

---
Safety
When can the beam line layout in test area be done?

---
Controls
Mike Kucera will need to be involved.

---
RFQ reminders
- Schempp is vendor
  - Make sure that the vanes are cleaned! See ISIS email.
    - Some cleaning details supplied by ISIS.
  - Review and verify on site mechanical design and construction (already in contract).