Pre-injector Upgrade Updates
(01 Sep – 15 Sep 2010)
C.Y. Tan
15 Sep 2010

---
Solenoid Parameters
Parameter	Unit	Value
Solenoid peak field	T	0.45
Integral (Bz2 )dz	T2 -m	0.0154
Current	A	500
Number of turns		78
Ampere-turns	kA	39
Inductance	mH	3.7
Conductor	mm	10.4 x 10.4, dia. 5.82
Voltage	V	7.5
Power loss	kW	3.75
Water pressure drop	MPa	0.5
Number of water circuits		1
Water flow	l/min	2.5
Water temperature rise	°C	22

---
Quad Params
Parameter	Unit	Value
Quadrupole gradient	T/m	39.25; 31.11;16.85
Pole tip radius	mm	20
Quadrupole effective length	mm	45
Quadrupole integrated gradient	T	1.77; 1.4; 0.76
Dipole corrector integrated field	T-m	0.006
Copper conductor dimensions	mm	5.0 x 5.0, ø3.0
Copper area	mm2	17.64
Quadrupole number of coil turns		8
Dipole number of turns		2
Quadrupole peak current at 1.77 T int. gradient	A	650
Dipole peak current at 0.006 T-m int. field	A	650
Current pulse form		60 Hz half sine wave
Repetition rate	Hz	15
R.M.S. current factor		0.0884
Quadrupole and dipole r.m.s. current	A	57.5
Current density	A/mm2	3.25
Quadrupole and Dipole inductances	µH	166; 5.2
Quadrupole and Dipole DC resistances	Ω	0.7; 0.13
Quadrupole and dipole DC voltages	V	460; 85
Quadrupole and Dipole Inductive voltages	V	20.3; 0.6
Quadrupole and Dipole power losses	kW	2.5; 0.5
Number of water circuits		2
Water pressure drop	atm	5.0
Water flow	l/min	3.0
Water temperature rise	°C	14

---
Solenoid DC PS Requirements
Parameter	Requirement
Ripple	< +/- 0.25A @ 500A
Noise	< 7.5 @ 500A
Regulation	< 1 s*
Long term stability	< 0.25A change in 6 months
%mu "A"/sqrt{"Hz"}
Ripple requirement: Trace3D calculation < 1% envelope mismatch
Noise: Assume gaussian white noise. Assume 3 for gaussian PDF to give < 1% envelope mismatch.
* Must reach current setting < 1s

---
Quadrupole PS requirements
Parameter	Value
Stability for 100s	+/- 0.2% @ 500A
Ramp rate	15 Hz
Rise time	~ 4ms*
Fall time	~4 ms*
Maximum voltage	< 2kV
Stability	+/- 0.2% @ 500A change in 6 months
2nd quad is the most sensitive. 1% reduction in capture for 0.2% change. 2nd quad is weaker and runs at 550A.
*Rise and fall time should be determined by the stability of the current at flattop for 100 s.
Picture assumes ½ sine wave at 60Hz.

---
Source Status

---
LEBT Status

---
MEBT Status

---
RFQ Status
- Coax cables need to be ordered for PA to RFQ.
- PA being assembled.
- Schempp (25 Aug 2010)
  - Parts are being procured.
  - Rectangular box rather than round tube because it's a better design.
  - Some pictures of the RFQ (next slide)

---
RFQ
RFQ
750keV RFQ.
60mA beam current
1.3m long.
Rod design.
Alwin Schempp designer
Expected delivery, early 2011

---
Test Stand
- Room has been cleaned up.
  - After beam line layout (progress?)
    - Water – Bob Slazak
    - Electrical – Jim Ranson
- Need to test LEBT before RFQ connection
  - Wires, toroids at the end of the LEBT, same position as the RFQ.

---
Safety
When can the beam line layout in test area be done?

---
Controls
Mike Kucera will need to be involved.

---
RFQ reminders
- Schempp is vendor
  - Make sure that the vanes are cleaned! See ISIS email.
    - Some cleaning details supplied by ISIS.
  - Review and verify on site mechanical design and construction (already in contract).