Pre-injector Upgrade Updates
(10 Nov – 01 Dec 2010)
C.Y. Tan
01 Dec 2010

---
Source Status

---
Chopper Signals
Magenta: Faraday cup
Cyan: toroid
Yellow: Extractor voltage
Green: chopper pulser
16 averages
Chopper letting beam through
Arc current off

---
Scraping from space charge blow up
Labels are Arc currents not beam current
20A
15A
5A

---
LEBT Status

---
MEBT Status
FNAL style
BNL style

---
MEBT Quads (BNL)
- Spoke to Masahiro on 15 Nov
  - 45mm will be tested before end of the year.
  - Similar 70mm quads installed in EBIS
    - All hollow conductors
    - 5Hz, 100-200us pulse, 70T/m (~800A)
    - Temperature rise is minimal for flow rate of 1 litre/s.

---
RFQ Status
- Schempp
  - Tan has reproduced Schempps Twiss params and emittances!
- PA assembly
  - Waiting for new engineer, coming on 01/01/11

---
Test Stand
- Room has been cleaned up.
  - Beam line layout in progress
    - Water – Bob Slazak
    - Electrical – Jim Ranson
- Need to test LEBT before RFQ connection
  - Wires, toroids at the end of the LEBT, same position as the RFQ.
- Design diagnostic line.
- Drawings from Schempp are sufficient to build table.

---
Test Area

---
Instrumentation
- Toroids clamp on
  - 1.5” over 3” flange toroids (7810)
    - sensitivity 0.1V/A. c.f. 1V/A
    - Rise time 50ns (same as non clamp on, 2x slower than present)
    - Length 1.25”
  - 6” toroids (7655)
    - 0.1V/A
    - Rise time 100 ns.
    - Length 1.5” (2.5x or 3x shorter than non clamp on)
Waiting for Bill!!!!!!
Present

---
Safety
When can the beam line layout in test area be done?

---
RFQ reminders
- Schempp is vendor
  - Make sure that the vanes are cleaned! See ISIS email.
    - Some cleaning details supplied by ISIS.
  - Review and verify on site mechanical design and construction (already in contract).

---
Controls
In flux
Status?