## Slide 1: Introduction to Longitudinal Phase Space Tomography
Duncan Scott

## Slide 2: Introduction
Integral Transform techniques have been in existence since 1917
  Radon transforms
Iterative, ‘algebraic’ techniques have been developed since the 1970s
  Iterative methods are used to reconstruct a beam distribution
    They are very simple
    Require little input information
    Non-linear rotations can be accounted for
  Algebraic Reconstruction Techniques Concepts
    Forward and Back Projections
    Weight Matrix
      Tracking Maps
NB the following is qualatitive and for illustration purposes (i.e. minus signs could be wrong).

## Slide 3: Forward Projections
Example 2-D density distribution
  bunch charge density
  Discretized on a grid

## Slide 4: Forward Projections (FP)
2-D density distribution
  bunch charge density
Generate Projections, histogram

## Slide 5: Forward Projections (FP)
2-D density distribution
  bunch charge density
Generate Projections, histogram
Do at different angles

## Slide 6: Mountain Range Plots (Sinogram)
Many projections at different angles give mountain range plot, or sinogram
  This is the raw data used to reconstruct the initial density distribution
Original Distribution
Mountain Range Plot
Sinogram

## Slide 7: Back Projection (BP)
The contents of a particular projection are evenly shared along all the cells that could have contributed to each bin

## Slide 8: Weight Matrix
At arbitrary angles the back/forward projected values can be weighted
  e.g. the area the bin intersects with
  This will be used in a different way when we consider particles rotating in longitudinal phase space

## Slide 9: Iterative Reconstruction
First iteration is an arbitrary guess of the answer
  e.g. a grid of zeros
Reconstruction grid can be of any dimension as long as the weight matrix is calculated correctly
Initial projection data can be quiet crude
  15 bins at 10 angles sinogram

## Slide 10: Iterative Reconstruction
FP =0
Forward project the guess for a particular angle and bin

## Slide 11: Iterative Reconstruction
FP=0
measurement = 3
Forward project the guess for a particular angle and bin
The raw data tells us the answer should be 3

## Slide 12: Iterative Reconstruction
FP=0
measurement = 3
∆cell = 3/15 = 0.2
Weight matrix gives all 1s
Forward project the guess for a particular angle and bin
The raw data tells us the answer should be 3
Back project the difference evenly over contributing cells to give a correction grid

## Slide 13: Iterative Reconstruction
+
=
Guess
Correction
New
Guess
Forward project the guess for a particular angle and bin
The raw data tells us the answer should be 3
Back project the difference evenly over contributing cells to give a correction grid
Combine the correction grid and the original guess to give the next iteration

## Slide 14: Iterative Reconstruction
Forward project the guess for a particular angle and bin
The raw data tells us the answer should be 3
Back project the difference evenly over contributing cells to give a correction grid
Combine the correction grid and the original guess to give the next iteration
Repeat for different projection and Bin
Different shades
due to weight matrix

## Slide 15: Iterative Reconstruction
Repeat many times and the original image is reconstructed

## Slide 16: Convergence - Discrepency
The difference between the measured and reconstructed projections can be used as a merit function for the algorithm
There are numerous, rigorous, demonstrations that iterative algorithms will converge
K. Tanabe, “Projection method for solving a singular system,” Numer. Math. vol. 17, pp. 203-214, 1971.

## Slide 17: Beam Reconstruction
The above method, with some modifications, can be used to reconstruct the longitudinal phase space of a bunch, given a series of projections from Wall Current Monitors
Example raw data from WCM, bunch rotating, aim to reconstruct at injection

## Slide 18: Beam Reconstruction
The reconstruction grid and projection bins are aligned
The weight matrix contains 1s and 0s
  The intersection with the separatrix can slightly change this
53 MHz,
1MV RF Bucket
Projection
(WCM Signal)
Bins aligned with reconstruction grid

## Slide 19: Beam Reconstruction
The reconstruction grid and projection bins are aligned
The weight matrix contains 1s and 0s
  The intersection with the separatrix can slightly change this
The beam is rotating with variable speed
  Account for this by using Tracking Maps to modify the weight matrix
53 MHz,
1MV RF Bucket
Projection
(WCM Signal)
Bins aligned with reconstruction grid

## Slide 20: Tracking Maps
Non-Linear Rotation is accounted for by tracking
Start by Back Projecting a profile

## Slide 21: Tracking Maps
Non-Linear Rotation is accounted for by tracking
Start by Back Projecting a profile
Concentrate on one cell
But first a very simple example….

## Slide 22: Map Matrix Example
Particle moves from {1,4} to {2,2}

## Slide 23: Map Matrix Example
Particle moves from {1,4} to {2,2}
Express grid as a vector
M is the Map

## Slide 24: Map Matrix Example
Particle moves from {1,4} to {2,2}
Express grid as a vector
M is the Map

## Slide 25: Map Matrix Example
Particle moves from {1,4} to {2,2}
Express grid as a vector
M is the Map
  4th column ‘moves’ particles from 4th component of vector

## Slide 26: Map Matrix Example
Particle moves from {1,4} to {2,2}
Express grid as a vector
M is the Map
  4th column ‘moves’ particles from 4th component of vector
  Rows determine final position, i.e. 6th

## Slide 27: Tracking Maps (cont.)
Non-Linear Rotation is accounted for by tracking
Start by Back Projecting a profile
Concentrate on one cell
We want to know where the particles in this cell were at injection

## Slide 28: Tracking Maps (cont.)
Non-Linear Rotation is accounted for by tracking
Start by Back Projecting a profile
Concentrate on one cell
We want to know where the particles in this cell were at injection
  Therefore, track backwards

## Slide 29: Tracking Maps (cont.)
Non-Linear Rotation is accounted for by tracking
Start by Back Projecting a profile
Concentrate on one cell
We want to know where the particles in this cell were at injection
  Therefore, track backwards
After tracking count the number of particles in each cell

## Slide 30: Tracking Maps (cont.)
Non-Linear Rotation is accounted for by tracking
Start by Back Projecting a profile
Concentrate on one cell
We want to know where the particles in this cell were at injection
  Therefore, track backwards
After tracking count the number of particles in each cell
Doing this for each cell and turn generates a series of maps telling us:
what fraction of particles starting in cell X propagate to each other cell in the grid

## Slide 31: Example Reconstruction
Back Project 1st profile to give the initial Guess of the answer

## Slide 32: Example Reconstruction
Back Project 1st profile to give the initial Guess of the answer
Forward map the Guess a random number of turns

## Slide 33: Example Reconstruction
Back Project 1st profile to give the initial Guess of the answer
Forward map the Guess a random number of turns
Project forward- mapped Guess and compare with measurement
Projection of
Forward Mapped Guess
Measured
Answer
Difference between
Guess and
measurement, ∆projection

## Slide 34: Example Reconstruction
Back Project 1st profile to give the initial Guess of the answer
Forward map the Guess a random number of turns
Project forward mapped Guess and compare with measurement
Back-project ∆projection to create correction grid, ∆grid

## Slide 35: Example Reconstruction
Back Project 1st profile to give the initial Guess of the answer
Forward map the Guess a random number of turns
Project forward mapped Guess and compare with measurement
Back project ∆projection to create correction grid, ∆grid
Backward map ∆grid to injection

## Slide 36: Example Reconstruction
Back Project 1st profile to give the initial Guess of the answer
Forward map the Guess a random number of turns
Project forward mapped Guess and compare with measurement
Back project ∆projection to create correction grid, ∆grid
Backward map ∆grid to injection
Combine Guess and ∆grid to give new guess and repeat
+
=

## Slide 37: Example Reconstruction
Repeat to reconstruct original beam

## Slide 38: Conclusions
Iterative techniques are simple but effective
  Compare projections of a Guess to data
  Use the comparison to make corrections to Guess
  Repeat until difference in projections is suitably small
Maps can be generated using simple or complicated particle tracking and saved
Using saved maps should enable reconstructions to be done “online”
Combined all these elements into ACNET Application
Version 1 goal:
  Reconstruct 1 entire batch every 30 seconds
Also get information on single and coupled bunch modes, (beam loading…?) and … ?