## Slide 1
35 years of H- ions at Fermilab

## Slide 3
Outline:
How we got here
Where we are
Where we are headed

## Slide 4
Figure: V.Dudnikov

## Slide 5
4.6eV:Mo
1.6eV:Cs on Mo
2.1eV:Cs
Metals have an abundance of loosely bound electrons, for molybdenum it takes 4.6eV to removed an electron.
Cesium has a work function of 2.1eV, but can lower the surface work function of molybdenum to 1.6eV with a 0.6 monolayer.
Since the work function exceeds the electron affinity of hydrogen atoms, a majority of hydrogen particles leave the surface as neutrals. However a few will pick up an excess electron when leaving the surface.
Some of these H- ions will make their way though the plasma to the anode and be extracted.
Surface production of ions
Zhang: Ion Sources

## Slide 6
Magnetron sources
Plasma parameters
e-
e-
Anode (+)
Cathode (-)
Cs
H+
H2+
H-
e-
~1 mm
B
nH2 ~ 1016 cm-3
ne ~ 1013-1014 cm-3
Te ~ 1eV / 15 eV
Mo
In gas discharge plasma positive hydrogen and cesium ions are formed
These ions are accelerated toward the cathode
Some of the ions that strike the surface have enough energy to “bounce” off the surface, and some small number of those leave the surface as H- ions.
Figure: Martin Stockli
Cs+
H2
Cs

## Slide 7
Prototype magnetron H- ion source bought by FNAL for $40k from Brookhaven in the late 70’s
This source was designed for fusion research
Low current DC source
Large gas volume (important later on)
Used Cs pellets to enhance H- production

## Slide 8
Source Body
Hydrogen inlet
Anode
Cathode connection
Cathode
Anode cover plate (extraction aperture)
3in

## Slide 9
BNL source was installed in bell jar and tested at 15Hz
Interesting side note early test were done using cesium chromate and titanium powder to make cesium tablets that were inserted into the cathode

## Slide 10
Chuck Schmidt chose the new source volume based on source pressure.
The fill time of the BNL source was 8.3ms and it did not reach high enough pressure for plasma to form at 15Hz reprate.

## Slide 11
Original source drawings done on CW Schmidt’s kitchen table in 1976
Clever design by Chuck Schmidt reduced internal volume by a factor of 10 !

## Slide 12
Chuck’s source that was used in the Cockcroft-Walton accelerators:
Compact size

## Slide 13
Mo cathode
Anode
extractor
Anode cover plate
Extraction aperture
1mm x 0.1mm
Chuck Schmidt’s original design.
Based on the BNL source
Appropriate for pulsed operation.

## Slide 15
Parameter | Value
Arc current | 180A
Arc Voltage | 130V
Beam current | 50mA
Power efficiency | 2mA/kW
Source lifetime | 3 months
The original magnetron used a flat cathode which will become very important later on !

## Slide 16
H-
Cockcroft-Walton
The source was mounted pointing down with a 90deg bend magnet.
There was a cold box that trapped Cs before it entered the accelerating column.
Co-extracted electrons swept away by the bend magnet

## Slide 17
Cockcroft- Walton continued
750keV accelerating column
100kV between each electrode
Dome contains ion source electronics and vacuum pumping

## Slide 18
The 1st H- ions accelerated down Linac
Like all good accelerator experiments, it took less than 1 shift to prove that it works !

## Slide 19
The original cathode was used for years. Then it was decided to grove the cathode on one side to help focus the beam at the anode extraction slit. This was a huge improvement. Later, the cathodes were grooved all the way around thinking that it would reduce “noise” in the extracted beam current which was thought to be the result of too low of a plasma volume.

## Slide 20
Average power now: 156V x 35A x15 (1/s) x 60(ms) = 4.9W
Arc current went from 180A to 35A with cathode focusing!
This is where things remained until the installation of the new ion source and RFQ……

## Slide 21
Where we are now…

## Slide 22
2 sources
The ion source is based on a design by Jim Alessi of BNL

## Slide 23
Einzel lens chopper
Ion source HV electronics

## Slide 24
Equipment bellow deck
Solenoid supplies
Solenoid & Quad supplies
Extractor pulsers
Supply controls
Trim supplies

## Slide 25
Different extraction scheme
Cockcroft-Walton
New source with RFQ
DC accelerating voltage
Extractor pulsed
Source pulsed to -35kV
Extractor at ground
Higher voltage across extraction gap ( )

## Slide 26
BNL Style Source
Figures: Jim Alessi BNL
Spherical focusing dimple cathode !

## Slide 27
Parameter | Value
Arc current | 15A
Arc Voltage | 150V
Beam current | 100mA
Power efficiency | 67mA/kW
Source lifetime | 9 months!
BNL style source, huge improvement!
Increase in power efficiency comes from:
Spherical dimpled cathode
35kV extraction

## Slide 28
New FNAL magnetron
10 inch source cube
Technicians involved with design
Round aperture

## Slide 29
New FNAL source design
anode cover plate
extraction cone
extraction gap .090in
gas valve
Cs tube
cathode connections
ceramic extractor standoffs
~11in

## Slide 30
Some studies done on new magnetron
Perveance, able to achieve 1A/cm2 @35kV
Figure: M. Stockli
anode
extractor

## Slide 31
Vertical 0.25 p mm mrad normalized ls
Horizontal 0.15 p mm mrad normalized 1s
LEBT emittance with nominal RFQ settings

## Slide 32
Evolution of magnetron cathodes

## Slide 33
Extractor sparking, one of our greatest challenges !
There have been 6 main issues that have lead to high spark rates:
Materials used
Magnetic Field
Source pressure
Extraction gap pressure
Cs control
Source electronics

## Slide 34
Materials
Materials play a big role, once the damage is done there is nothing left to do other than pull the source and fix it.
Original extractor cone tip made out of molybdenum
Energy of spark would cause damage that would lead to the need to pull the source and fix
BNL uses tungsten for cone tips. They sent us one to try out. Big improvement in eliminating the damage from sparking
Original inner anode cover plate made out of titanium
Severe case of erosion increased the aperture from 0.125in to 0.25in !
Once again BNL (“ahead of the curve”) sent us a molybdenum cover plate which has clearly solved the erosion problem
0.125in
0.25in

## Slide 35
Magnetic field
Magnetic field plays a big role in both confinement and sweeping away co-extracted electrons
Magnetrons prefer 1kG in the plasma region for proper confinement.
Original magnets were marginal to start with and ended up too low (~700G) when warmed up.
Redesigned the magnets and yoke with the help of Jim Volk
Original design: 4 SmCo disks
Final design: 2 SmCo rectangular magnets with higher field, thicker yoke

## Slide 36
# of electrons inside source
0 Gauss
500 Gauss
1k Gauss
1.5k Gauss
Simulation by
CY Tan
For all simulations:
Extractor cone = 0V
Cathode = -35.2kV

## Slide 37
Source Pressure
Cathode (-)
Anode (+)
H-
e-
H+,H2+
If source pressure is too high, one possibility is that the path length for the fragile H- ions is so long that the probability is high that some number of them will loose their electron on the way to the extraction aperture, leaving an excess of electrons to be extracted. Leading to sparking.
1mm

## Slide 38
Source Pressure
Source pressure
Extractor Voltage
Anode (+)
Extractor (gnd)
Another possibility is low average cube pressure. When the pressure is too low in the extraction gap and we are operating in a different regime of the Paschen curve.
0.09in

## Slide 39
Cesium Control
Mo: 4.6eV
Cs on Mo: 1.6eV
Cs 2.1eV
If the cesium layer is too thick/thin:
Work function increases
H- production decreases
Number of free electrons increases
Cs boiler temp (yellow)
Extractor Voltage
Cs boiler temp (green)
Example of too much Cs
Example of too little Cs

## Slide 40
Examples of excess cesium in the source

## Slide 41
Source electronics
HRM resets due to sparking
Cathode looses about 20C due to the arc being off during the resets
Source body looses about 2C
HRM in the HV rack hangs up during heavy sparking. During resets the HRM is off for a few seconds which means that the arc is not on during that time. This allows the cathode and source body to cool off since the only heating is from the arc power: (150V)(15A)(15Hz)(230ms)= 7.8W average power

## Slide 42
What we are working on:
Solid State extractor pulsers
New gas valves
2 stage extraction
Removing HRM from HV rack
current regulated arc modulator
Better Cs boiler (no glass, heat tape)
Tungsten dimpled cathode

## Slide 43
Current extractor pulser
Vacuum tube based
150ms rise time
Tube lifetime 3 months
Long arc PW needed (230ms)
Source duty factor 0.3%
150ms
DTI Solid State Switches
9.6ms rise time
50kV, 50A switches
Source duty factor 0.12% a decrease of 40% !
Should allow even longer lifetimes

## Slide 44
Gas Valves
The current gas valves are Veco PV-10 piezoelectric valves. They are fast and reliable for the most part and have been in use since day one.
Piezeo disk
Viton wafer provides seal
Calibration is done by adjusting the tension on the retainer
End up with a hysteresis curve like these. The valves start to open around 20V and are fully open by 100V

## Slide 45
10% / 5degC
Gas Valves
However, these valves have a terrible temperature dependence !
Veco PV-10 data sheet
Even a change as small as 1C changes the arc current by about 1.5A and a change is source pressure of 1x 10^-6 Torr !
This is a big change that can lead to sparking and big changes in beam current!
~1C
~1A

## Slide 46
Gas Valves
We are currently testing a solenoid type valve that should have not temperature dependence.

## Slide 47
Source
35kV
+
_
~8kV
pulsed
+
_
2 stage extraction scheme
-27kV
-8kV
-35kV – (-27kV) – (-8kV) = 0
27kV
We only 27kV across extraction gap
Less voltage should reduce sparking
No need to pulse HV rack (it would set at 35kV DC)
Currently testing on test stand

## Slide 48
HRM removal
Plan to remove HRM and install it in a ground controls rack.
Communication via fiber transceivers will be installed
Will be a big help in reducing the affect of sparking
Will reduce overall spark rate due to asynchronous rebooting of HRM
Thanks to Mike Kucera for pursuing this option !

## Slide 49
Cs boiler
W cathode dimple
Cs on W H- production peak is broader
We us 5g ampules of Cs.
Sometimes Cs gets trapped in the broken glass
Need to get rid of heat tape and go to heater like BNL
Tungsten dimple

## Slide 50
All of this is cool, but the coolest thing about working on sources is: You don’t have to commit a crime to be on the cover of the Chicago Tribune !

## Slide 51
Thanks for your attention !