## Slide 1: PIP and PIP-II Status and Plans
Sergei Nagaitsev
Fermilab PAC meeting
24 July 2014

## Slide 2: Fermilab after the Tevatron
Fermilab operates the largest accelerator complex in the U.S., 2nd largest in the world (even after termination of the Tevatron)
Also part of operations:
  Proton Improvement Plan (PIP)
  Muon Campus projects
  Test facilities (magnets, SRF cavities)
Projects: Muon g-2, Mu2e, LBNF, MicroBooNE, LCLS-II (at SLAC), PIP-II
Programs: MAP, LARP, ILC
Research
Commercialization of our accelerator technologies.

## Slide 3: Accelerator Operations
Fermilab operates a total of 16 km of accelerators and beamlines
A 400-MeV proton linear accelerator (0.15 km)
An 8-GeV Booster synchrotron (0.5 km)
An 8-GeV accumulator ring (3.3 km)
A 120-GeV synchrotron (3.3 km)
A Muon Campus Delivery ring (0.5 km)
Soon: Muon g-2 ring
Transfer lines and fixed target beam lines (8 km)
Two high power target stations, several low-power targets
And maintains
130 buildings, structures, service bldgs,…

## Slide 4: Fermilab Accelerator Complex
Linac: NTF, MTA
BNB: MicroBooNE
NuMI: MINOS+, MINERvA, NOvA
Fixed Target: SeaQuest, Test Beam Facility, M-Center
Muon: g-2, Mu2e (future)
Also, test and R&D facilities:
ASTA
PXIE
CMTF
Various cryo test stands

## Slide 5: Present NuMI performance (protons on target)
FY14 performance metric: 3.2e20 POT

## Slide 6: Recycler is now part of operations

## Slide 7: Fermilab Booster
Booster is a resonant machine running at 15 Hz
RF is pulsed, limited to ~7.5 Hz
  at higher frequencies the cavities spark
  at higher frequencies the tuners overheat
  Refurbishment plan to achieve 15 Hz is part of PIP
There is an RF pre-pulse associated with beam cycles
  It means that the beam pulse rate is less than 7.5 Hz

## Slide 8: Proton Improvement Plan (PIP)
The PIP campaign has several goals:
  Increased reliability of the Linac/Booster complex
  Control of beam losses
  Increased proton flux (15 Hz)
Main challenge: keep beam losses constant while increasing the protons on target
  Beam loss limits are set at levels for personnel safety (ALARA) and equipment serviceability

## Slide 9: Booster RF cavities
July 1970 Flatbed semi delivering Booster RF cavity pair
Cavities built by GE

## Slide 10: Booster rf cavities
Booster has 22 slots for rf cavities
We can not run (4.3e12) beam with fewer than 17 cavities.
We have 19 cavities on hand
  At any given time: 17 are installed, 2 are out for repair
  each cavity requires 3 tuners. Tuners require 3 weeks to rebuild during the 10-week refurbishment process.
Cavity #20 is an old 1st prototype cavity. It was restored and equipped with new tuners, and ready for testing

## Slide 11: Booster PIP - Refurbishment of 40 year old cavities (facelift)
Cavity Removal
Cool-down
Remove Tuners
Rebuild - Cones & Tuners
Rebuild Stems/Flanges
Re-Assemble
Testing
Weeks
0
10
Cavity Removal - Stripping
Tuners Rebuild
Rebuild and Test

## Slide 12
Booster PIP - Cavity Refurbishment Timeline

## Slide 13: Refurbishment: “Fun” facts and beyond
All cavities in tunnel need to be refurbished before higher rep rate (15 Hz) is possible
After refurbishment is completed – higher flux will require time
After refurbishment is completed – the cavities will still be OLD
There is likely to be failures as cavities are run harder
Even if we have 20 cavities installed in the ring, this leaves us with no spares.
The plan is to procure 3 more cavities in FY16,17
  same type as present cavities
  larger bore
  install 2 in ring as hot spares

## Slide 14: PIP and PIP-II interaction
PIP original goals were:
  Achieve 15 Hz Booster operation with beam
  Operate Linac and Booster until 2025, then replace with Project X (8 GeV).
  Several reliability issues were ignored because of the 2025 end date.
PIP-II is not replacing the Booster, only the linac
  Need to reassess the PIP scope
  Need to set a new end-date for the Booster (2030?)
Started regular meeting to coordinate PIP and PIP-II

## Slide 15: PIP-II Physics Opportunities
LBNF
  1.2 MW of beam power on day one; 2.4 MW ultimately
  Flexible proton beam energy (60-120 GeV)
NuMI
  1.2 MW beam power in the interim
Mu2e
  30-50% increase in beam power immediately*
  Potential for ~25-100 kW at 800 MeV
    Current Mu2e configuration limits to 25-30 kW
SBN
  30-50% increase in beam power immediately*
* Possible extension of Booster operations to 20 Hz is under consideration, but not incorporated into these estimates
Notes: Per Bob B:
Shielding can be upgraded to accommodate ~25 kW
Instantaneous proton rate (measured over 1.7 usec) can go up about a factor of three (before problems with event pileup in the detector)

## Slide 16: PIP-II Goals
Proton Improvement Plan-II supports these long term physics research goals while providing a platform for the future
Design Criteria
  Deliver 1.2 MW of beam power at 120 GeV, with power approaching 1 MW at energies down to 60 GeV, at the start of LBNF operations
  Support the current 8 GeV program, including Mu2e, g-2, and the suite of short-baseline neutrino experiments
  Provide upgrade path for Mu2e
  Provide a platform for extension of beam power to LBNF to >2 MW
  Provide a platform for extension of capability to high duty factor/higher beam power operations
  At an affordable cost to DOE

## Slide 17: PIP/PIP-II Strategy
Increase Booster beam repetition rate to 15 Hz (PIP)
  700 kW to NOvA concurrent with 8 GeV program
Increase Booster/Main Injector per pulse intensity by 50%; decrease MI cycle time modestly
  Increase Booster injection energy
  to ~800 MeV
  Modest modifications to Booster/
  Recycler/MI
    To accommodate higher intensities
    and higher Booster injection energy

## Slide 18: PIP-II
We believe the most cost-effective means of achieving these goals is via an 800 MeV superconducting pulsed linac, extendible to support >2 MW operations to LBNF and upgradable to continuous wave (CW) operations
  Builds on significant existing infrastructure
  Capitalizes on major investment in superconducting rf technologies
  Eliminates significant operational risks inherent in existing linac
  Siting consistent with eventual replacement of the Booster as the source of protons for injection into Main Injector
Whitepaper available at
projectx-docdb.fnal.gov/cgi-bin/ShowDocument?docid=1232

## Slide 19: PIP-II Performance Goals
Performance Parameter | PIP | PIP-II | 
Linac Beam Energy | 400 | 800 | MeV
Linac Beam Current | 25 | 2 | mA
Linac Beam Pulse Length | 0.03 | 0.5 | msec
Linac Pulse Repetition Rate | 15 | 15 | Hz
Linac Beam Power to Booster | 4 | 13 | kW
Linac Beam Power Capability (@>10% Duty Factor) | 4 | ~200 | kW
Mu2e Upgrade Potential (800 MeV) | NA | >100 | kW
Booster Protons per Pulse | 4.2×1012 | 6.4×1012 | 
Booster Pulse Repetition Rate | 15 | 15 | Hz
Booster Beam Power @ 8 GeV | 80 | 120 | kW
Beam Power to 8 GeV Program (max) | 32 | 40 | kW
Main Injector Protons per Pulse | 4.9×1013 | 7.5×1013 | 
Main Injector Cycle Time @ 120 GeV | 1.33 | 1.2 | sec
LBNF Beam Power @ 120 GeV* | 0.7 | 1.2 | MW
LBNF Upgrade Potential @ 60-120 GeV | NA | >2 | MW
*LBNF beam power can be maintained to ~80 GeV, then scales with energy

## Slide 20: PIP-II Site Layout (provisional)

## Slide 21: PIP-II Status and Strategy
PIP-II is currently pre-CD-0
  Complete concept exists
    Documented in whitepaper; technical backup in PX RDR
  R&D program underway
    Front end (PXIE) and superconducting rf development
Strong endorsement from P5
  Recommendation 14: Upgrade the Fermilab proton accelerator complex to produce higher intensity beams. R&D for the Proton Improvement Plan II (PIP-II) should proceed immediately, followed by construction, to provide proton beams of >1 MW by the time of first operation of the new long-baseline neutrino facility.
    Applies in all budget scenarios considered.
Discussions with P5, Fermilab, and DOE/OHEP management have been in context of FY19 construction start
  Consistent R&D deliverables list established
  Preliminary discussions on potential international in-kind contributions
  Aligned with LCLS-II and LBNF activities
Goals for the next year
  Release PIP-II specific RDR
  Maintain PXIE and SRF development on established schedules
  Support DOE in the development of Mission Need Statement
  Establish PIP-II Office, within Accelerator Division

## Slide 22: PIP-II Collaboration
Collaboration MOUs for the RD&D phase (through CD-2) :
  National IIFC
  ANL ORNL/SNS BARC/Mumbai
  BNL PNNL IUAC/Delhi
  Cornell UTenn RRCAT/Indore
  Fermilab TJNAF VECC/Kolkata
  LBNL SLAC
  MSU ILC/ART
  NCSU
Ongoing collaboration/contacts with RAL/FETS (UK), ESS (Sweden), SPL (CERN), RISP (Korea), China/ADS
Annual Collaboration Meeting (June 3-4 at Fermilab)
https://indico.fnal.gov/conferenceDisplay.py?confId=8365

## Slide 23: PIP-II International Contributions
Discussions at agency and laboratory levels indicate that an 800 MeV SC linac could attract significant in-kind contributions from India/Europe/Asia
  SC accelerating structures
  RF sources
  Instrumentation
  Magnets/power supplies
Significant R&D collaboration for >5 years with India
  Discussions at DOE-DAE level on potential Indian in-kind contributions

## Slide 24: Flexible Platform for the Future
PIP-II Inherent Capability
  ~200 kW @ 800 MeV
  ×10 Mu2e sensitivity
2 MW to LBNF
Flexibility for future experiments
  Muons, Kaons @100’s kW
Compatible with muon acceleration
needs (Mark P talk)

## Slide 25: Summary
The Fermilab accelerator complex can be upgraded to establish LBNF as the leading long-baseline program in the world, with >1 MW at startup (2025)
The Proton Improvement Plan-II (PIP-II) is a complete, integrated, cost effective concept, that meets this goal, while
  leveraging U.S. superconducting rf investment,
  attracting international partners,
  providing a platform for the long-term future
PIP-II retains flexibility to eventually realize the full potential of the Fermilab complex
  LBNF >2 MW
  Mu2e sensitivity x10
  MW-class, high duty factor beams for rare processes experiments
We have received a positive recommendation from P5 and are working with Fermilab and OHEP management to move forward.

## Slide 26: Backup Slides

## Slide 27: PXIE @ CMTF
PXIE will address the address/measure the following:
  LEBT pre-chopping
  Vacuum management in the LEBT/RFQ region
  Validation of chopper performance
  Bunch extinction
  MEBT beam absorber
  MEBT vacuum management
  Operation of HWR in close proximity to 10 kW absorber
  Operation of SSR with beam, including resonance control
  Emittance preservation and beam halo formation through the front end
RFQ
MEBT
HWR
SSR1
HEBT
LEBT
40 m, ~25 MeV

## Slide 28: PXIE
RFQ
MEBT
HWR
SSR1
HEBT
LEBT
Collaborators
ANL: HWR
LBNL:LEBT, RFQ
SNS: LEBT
India (BARC): MEBT
30 keV
2.1 MeV
10 MeV
25 MeV

## Slide 29: SRF R&D
HWR
SSR1 SSR2
LB650
HB650

## Slide 30: SRF Development Status

## Slide 31: SRF R&D: Q0
Chart: 
| 4.10204171 | 4.1223678499999901 | 4.1207045099999888 | 4.1283258399999889 | 4.6427487300000001 | 4.8202409099999981 | 2.9004044099999997 | 2.0505828500000001 | 1.07215678 | 4.9301824600000002 | 5.9830811800000028 | 7.0031887800000003 | 7.908564859999994 | 9.0142927799999999 | 10.068958599999998 | 10.0728524 | 10.069451600000004 | 10.943803000000001 | 12.226071899999997 | 11.915780500000006 | 13.091423199999999 | 14.036556600000004 | 14.035236600000005 | 14.9128147 | 15.995047100000004 | 16.7
TB9ACC015 N doped | 32426520200 | 32632704300 | 32710516700 | 32834612200 | 32918723900 | 33444540800 | 31496372200 | 30077017400 | 27670617900 | 33385445800 | 34203935800 | 35160275000 | 35698594800 | 36192629700 | 37983903100 | 38126942900 | 38219676500 | 38859156600 | 40344910800 | 39858460900 | 40644362000 | 42530339500 | 42762934500 | 43336024900 | 43756612400 | 44000000000
TB9ACC012 N doped | 24814515500 | 26264851600 | 26091247000 | 25642462500 | 25011934400 | 23866195700 | 22752021800 | 24570105300 | 25116389500 | 26698181900 | 26893131300 | 27438102300 | 28084308800 | 28117802200 | 28580764300 | 28852215000 | 29368219200 | 29440085200 | 29919572700 | 29925300600 | 29809220400 | 29741982200 | 29900000000
TB9AES011 N doped | 28258212600 | 28481400100 | 26245050600 | 25030179000 | 27618889600 | 27623639200 | 28083525500 | 28094035400 | 28095714700 | 29381873300 | 29865487100 | 30221624800 | 30209165400 | 31070229600 | 31192684100 | 31454970600 | 31765331400 | 32255142700 | 32895657500 | 33640117900 | 34018122200 | 33861470700 | 33956410500 | 34043871100 | 34563330600 | 34787915600 | 35037050700 | 35314867200 | 35104923100 | 35168642700 | 35501498400
TB9ACC015 120C baked | 20887709600 | 21206814700 | 22388211500 | 22166250200 | 21342703800 | 22198197900 | 21537816200 | 21161914000 | 19784090600 | 21772836200 | 21748968800 | 20899132900 | 20160195400 | 19366794400 | 19502994000 | 19368704500 | 18546531100 | 17999381000 | 17205411300 | 17733409500 | 16800150700 | 16402967900 | 16006623300 | 16028423800
Q0
Eacc [MV/m]
Nitrogen-doped 9-cell cavities vs typical 120C bake (2K)

## Slide 32: PIP-II Linac Technology Map
Section | Freq | Energy (MeV) | Cav/mag/CM | Type
RFQ | 162.5 | 0.03-2.1 |  | 
HWR (opt=0.11) | 162.5 | 2.1-11 | 8/8/1 | HWR, solenoid
SSR1 (opt=0.22) | 325 | 11-38 | 16/8/ 2 | SSR, solenoid
SSR2 (opt=0.51) | 325 | 38-177 | 35/21/7 | SSR, solenoid
LB 650 (G=0.61) | 650 | 177-480 | 30/20/5 | 5-cell elliptical, doublet
HB 650 (G=0.9) | 650 | 480-800 | 24/10/4 | 5-cell elliptical, doublet
b=0.11
b=0.22
b=0.51
b=0.61
b=0.9
325 MHz
11-177 MeV
650 MHz
177-800 MeV
SC
162.5 MHz
0.03-11 MeV
LEBT
RFQ
MEBT
RT
IS
PXIE

## Slide 33: Proton Demand
g-2
Mu2e
8 GeV 
NOvA

## Slide 34: Cryogenic System
Required to support 5% cryogenic duty factor
  Configuration capable of 10-15% with more pumping
  160 – 240 kW beam power at 800 MeV

## Slide 35: Mu2e w/ PIP-II
Can operate PIP-II linac up to ~15% duty factor with cryogenic system as designed
RF system as designed can support 2 mA (averaged over 1 msec) at 15% duty factor
RFQ can supply 10 mA
MEBT chopper can provide arbitrary bunch patterns for separation at downstream end of linac.
Mu2e Operations:
  10% micro-duty factor (100 ns×1 MHz)
  13.5% macro-duty factor (9 ms×15 Hz)
  10%×13.5%×10mA×800 MeV = 108 kW

## Slide 36: Mu2e w/PIP-II
9 ms, 1 mA (Mu2e)
1 ms, 2 mA (Boo)
67 ms
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | . | . | .
1 ms
6 ns
100 ns, 10 mA
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | . | . | .