## Slide 1: Linac Laser Notcher READINESS Review
August 5th, 2014
Kevin Duel – Mechanical Support Engineer

## Slide 2: Outline
MEBT Modification and Installation

## Slide 3: Remove quads, corrector and beam pipe
Notes: Adjust quads in z to get better access to flange bolts.
Support 6” Conflat flange and use crane to remove quads.

## Slide 4: Quads, corrector, and beam pipe removed

## Slide 5: Swap out adjuster stand plates

## Slide 6: Cut off 6” Conflat and bellows and cut beam pipe to final length in machine shop
Clean beam pipe after machining

## Slide 7: Insert beam pipe through quad and weld on new bellows and KF50 flange
~3/4” from weld to magnet steel for welder
Notes: Push beam pipe upstream until downstream bellows contacts the quad steel.

## Slide 8: Insert beam pipe through quad and weld on new bellows and KF50 flange
~3/4” radially from weld to coils

## Slide 9: Assemble VC/OC onto RFQ, blank off KF50 port and leak check

## Slide 10: Install quads with new beam pipe, and make up KF50 flanges
New quad position is ~1/2” downstream of current position
~1/2” available to move quad further downstream
~1/8” between KF50 bolt head and quad coils in final position

## Slide 11: Install quads with new beam pipe, and make up KF50 flanges
¾” bolt length including bolt head
.4” clamp length
.22” thread engagement
~1” between coils and buncher
Notes: Will only have ~5/8”, might need to use studs and nuts instead

## Slide 12: Remaining work
Leak check
Alignment