## Slide 1: PIP Linac Laser Notcher Overview & Plans
David Johnson
Todd Johnson, Kevin Duel, Fred Mach
August 5, 2014
PIP Linac Laser Notcher System Installation Readiness Review
DRAFT

## Slide 2: Topics
Notcher System Description
What we are doing in September & why
Jean-Paul and Kevin Presentations
Laser System Status and Plans

## Slide 3: Requirements and Technique of Laser Notching of H-
Requirements
  All ions in bunch should see the same photon density
  The 201.25 MHz laser pulses must be phased with the RFQ
  The laser pulse length =/> bunch length ~1.5 to 2 ns
  Uniform temporal profile
  The burst of 201.25 MHz pulses must match the Booster inj rev. freq.
  The 450 kHz burst must have appropriate timing within the linac pulse
  The pulse energy should neutralize > 99% of ions in each bunch
Technique
  Utilize a CW seed laser and wave-guide modulator to create required laser pulse pattern (both 200 MHz and 450 kHz) at low pulse energies (pJ)
  Amplify pulse pattern using a three-stage fiber amplifier (nJ to uJ)
  Further amplify using a free-space solid state amplifier (mJ)
  Create a spatially uniform photon beam
  Insert laser pulse into a linear zig-zag interaction cavity where the laser reflections inside the cavity match the ion velocity
    to reduce required pulse energy by the number N of reflections in the cavity.

## Slide 4: Neutralization vs Pulse Energy
Design value

## Slide 5
Laser Notcher System
Optical Cavity
Vacuum can
Laser System
Optical
Pattern
Generator
Fiber
Amplifiers
Free
Space
Timing
Controls
Diagnostics
instrumentation
Optical
cavity
Vacuum
interface
Nd:YAG
DPSS
Amplifier
System
Beam
shaping
Transport
Laser
Dump
Mirror Test
Diagnostics
To be installed in the MEBT beam line
September Shutdown
ES&H
LASER SYSTEM & REMAINING COMPONENTS
IINSTALLED APRIL-MAY 2015 SHUTDOWN
Pre-amp
AWG
Modulator
Seed
Amplifier

## Slide 6: Optical cavity &vacuum flange

## Slide 7: Why are we installing the optical cavity now?
  Opportunity !
  We are interested in finding out how the dielectric mirrors behave in this location. We believe there should be no problem
    Vacuum level (residual gas) – install metal valve at downstream end of RFQ to allow for RGA.
    Aperture between the mirrors should be sufficiently large that no H- should impact the mirrors
    Electrons from the photoneutralization should exit downstream flange before striking beam pipe (result of simulations)
  Monitor the mirror reflectivity for any degradation with a low power 1064 nm laser and photo diodes-> interface into ACNET.
  We have designed the cavity/vacuum flange to be “easily” removable (flanged at both ends) and the optical cavity to be independent of the vacuum component.
  Kevin will detail the installation plans
  Next few slides show the flange and cavity geometry…

## Slide 8
TO MEBT
RFQ
Laser IN
Laser OUT
Vacuum Flange / Optical Cavity
~1.5” downstream
RFQ flange surface
~0.5” downstream
RFQ flange surface

## Slide 9
Optical Cavity can be easily removed
With 6 precision placed bolts
Rear View of VF/OC

## Slide 10
One Piece Vacuum Can (Flange)
Flange to MEBT
Sealing surface to RFQ
Input Viewport
Output Viewport

## Slide 11
Optical Cavity Structure
Fixed
mirror
Adjustable mirror
Adjustment screws (0.2mm pitch)
Exit port
Longitudinal Mirror adjustment

## Slide 12: Expected Beam Dimensions
Phase space simulation at end of RFQ (figure 4.40 of 750 KeV Upgrade Plan)
Trace 3D back calculation of beam size at exit of RFQ based upon emittance measurement at 178 kW power August 9, 2012 CY Tan.
Laser beam vertical profile (1/e2) ~ 5 mm.
Initial design assumed that the vertical laser beam dimension of 1 cm.
Beam measurements indicate vertical laser size could be reduced to 6 mm
Additional simulations to be shown by JPC

## Slide 13
Aperture
(looking from downstream)
Mirror cavity radius 1.49 cm
Beam tube Inner radius 1.83 cm
Expected (horizontal) half-size of H- << 0.5 cm
(X3 smaller than mirror cavity radius)

## Slide 14
2.3”
EOS
G [T/m]
Z=0
3.1” (0.0787m)
RFQ flange
.0251”
Stripping region
½”
coil
3s = 2.5 mm
2.0”
Data For Simulations of Electron Trajectory in Quad Fringe Field
0.105m
0.11 4 m
0.127 m
Center of doublet
Gradient in upstream quad

## Slide 15: Electron Trajectory Simulations
Electron Beam Trajectories for MEBT Quadrupole Doublet
V. Kashikhin, June 25, 2014
Electron Trajectories calculated by TOSCA3d code for electrons having 409 eV kinetic energy.
The beam of 9 electrons have sizes: +/- 3.6 mm, and +/-2 mm. The coordinate system is shifted -50mm in Z-axis. Coordinates -0.127,0.114,0.105m on the graphs are -0.177,-0.164,-0.155 m. It looks that all electrons go out of 31 mm cylinder surface radius. TPC =0,0,0 is for the beam parallel Z-axis, TPC=90,1,0 is for the beam rotated 1 deg. around X-axis, and TPC=0,1,0 is for the beam rotated 1 deg. around Y-axis

## Slide 16
Example of Electron Trajectories in Quad Fringe Field
Vladimir Kashikhin
Z= -127 mm
Z = -105 mm

## Slide 17
Readout to ACNET
Readout to ACNET
Monitor Photodiodes
and their ratio
(Datalog)
From: Todd Johnson
Optical Cavity Mirror Test

## Slide 18
Pre-Shutdown Schedule for Optical Cavity/ Vacuum Flange

## Slide 19
Part II Laser System

## Slide 20: Burst mode seed pulses to Fiber Amplifier followed by Free Space Amp
l1=1064nm
120 mW CW
SW=0.1 nm
10 GHz Mach-Zehnder
Modulator
Pulse Generator
Amplifier, Timing
PM Fiber
Lins ~5dB
Li~1.8dB
15 Hz
AOM
Generate 24 us burst at 15 hz
TRANSPORT BEAM SHAPING OPTICS & OPTICAL CAVITY
Fiber Pre-Amp
Fiber Amp 1
Fiber Amp 2
Free Space Amp
Output modulator/Input fiber pre-amp:
201.25MHz pulses (1.25 ns pulse), 458kHz burst
Clean up filter
Isolator
Line filter
Free
Space
Grumman CEO DPSS OEM
Diode + TC
controlled
*Notch 12 bunches -> 60 ns
10 notches/linac pulse
Pulsed at 15 Hz

## Slide 21: Optical Pattern Generator

## Slide 22: Optical Pattern Generator
Input: 100 mW CW
Output: 54 pJ (1.5 ns/200 MHz)
294 uW avg power at 450 kHz
Pulse on/off extinction 30 dB
Need stable source

## Slide 23: Seed Source
Requirements: center wavelength (1064.15 nm) , spectral width(0.1 to 0.3 nm), stability (< 1% p-p) , optical power (~200 mW)
Current seed source not stable @ 25oC operation point. Wavelength too high (could be adjusted by Peltier Cooler on FBG.
Current source more stable at 7oC (but don’t want to rely on this long term). Should work for initial tests of fiber system.
Plan on purchasing a new seed source (looking at options)
Diode at25o C
Peak amp shift ~6 dB
Diode at7o C
~5 dB amp shift

## Slide 24: Seed Source Output Stability
Look at output stability at 2 seed source temperatures
25oC sigma 191 uW p-p 1.025 mW (5.2%)
7oC sigma 52 uW p-p 0.6 mW (2.5%)

## Slide 25
Chart: Nd:YAG Gain Spectrum and Seed spectrum
Provides input to specification of seed center wavelength and spectral width

## Slide 26: Fiber Amplifiers

## Slide 27: Fiber Pre- Amplifier System
Input 54 pJ
294 mW
Gain 23 dB
Gain 17.2 dB
Output 100 pJ
590 mW
Output 385 nJ
2 W
PriTel
amp
filter
Gain Fiber 7.5 meters CorActive DCF-YB-6/128-PM ,
abs @975nm 2.6 dB/m, Core A 33 um2
Pump: center l 970.7 nm
(will shift higher due to heating)
up to 7.3W @8A

## Slide 28
Absorption Spectra for Yd doped Fiber

## Slide 29: SBS
SBS threshold (CW laser)
SBS in pulsed fiber amplifier
  Signal line width
  Pulse duration
  Repetition rate
Laser Pulse structure through CW section
We see detrimental effects due to both the pulse duration and repetition rate
= laser line width
= spectral width BGS (<100 MHz)
A = fiber core area
K = polarization factor (=1)
g = peak Brillion gain coefficient
L = effective fiber length
Notch (N pulses on 201.25 MHz)
Typically N ~ 12 16 pulses (60-80 ns)
Repetition rate ~ 450 kHz (Booster revolution frequency)
This is equivalent to 450 kHz repetition rate of 60-80 ns laser pulses
For 0.1 nm line width -> 26 GHz

## Slide 31: SBS Mitigation Plans
Raise the SBS threshold a factor of 7.5 by:
  utilizing a larger mode area gain fiber (x 3)
  Utilizing a gain fiber with a higher absorption
    Reduce length of gain fiber (x 2.5)
  Better matching pump wavelength to improve optical-optical efficiency
    Reduce pump power
  Potentially reduce un-doped delivery fiber

## Slide 32: Fiber Amplifier System
Input 363 nJ 1.96 W
Gain: 14.5 dB
Optical Engines
Micrograph of PCF fiber
Single mode, single polarization
Small NA (~0.03)
Large mode area
High peak power levels
High pump absorption (~10 dB/m)
High reliability
Output to include mode
stripper (to remove any pump
light) and optics to match
into first FS amp.

## Slide 33
Bundle to taper splice
PCF
Taper

## Slide 34: Free space amplifier

## Slide 35
Free Space Amplifier configuration 2.2
(Pulsed at 15 Hz)
HRM
HRM
Faraday
Isolator
8mm
Telescope to expand beam
(1/e2 diameter to 5.08 mm)
Input fiber
From fiber amplifier
HRM
Fiber port and optics
to generate
1/e2 diameter of 1.6 mm
Faraday
Isolator
4mm
HRM
RBA (2mm rod)
3.07”
HRM
REA (6.35 mm rod)
6.0”
l/2
Telescope to reduce beam
(1/e2 diameter to 1.6 mm)
Beam Stacker
532 nm alignment laser
HRM
HRM
000
045
090
135
Faraday
Isolator
4mm
8 uJ pulse/2 ns
4 kW peak
2 mJ pulse/2 ns
1 MW peak
BPM
Polarization orientation
Used by EOTech
Gain: ~ 23 dB (total for both modules)
Output: 2 mJ 10 kW (450 kHZ) 3.2 mW (15 Hz)

## Slide 37: Installation

## Slide 38
1
3
5
7
9
11
13
15
17
19
1.75” x 20U = 35”
LCD/Keyboard (1U)
4slot VME (2U)
Timing card/moto5500 controller/8ch D/A
PCI Expansion Chassis (2U)
PCI slots (AWG/clock /expansion)
OPG (2U)
LD- USB interface / MOD&BIAS - USB interface
PriTel fiber amplifiers (2U)
USB interface
RBA PS (1U)
Tdk-Lambda GEN50-30E
REA controller (2U)
RS-232 interface
RBA controller (2U)
RS-232 interface
Reserved (2U) for potential AOM
REA PS (1U)
Tdk-Lambda GEN100-24
REA PS (1U)
Tdk-Lambda GEN100-24
SPARE 1U
Rack mount computer (1U)
Laser Notcher Rack Layout ( July 2014)

## Slide 39: Es&h

## Slide 40: Laser Safety
We are in constant contact with Matt, Dave, and Ray every step of the design to assure personnel safety.
  Laser development lab
  Installation and operation of the laser system in Linac MEBT
    Interlocks
    Operational procedures
    Alignment procedures
  Installation of the mirror test laser system

## Slide 41: diagnostics

## Slide 42: Plans
Optical Cavity
  We should have all components for aligning the optical cavity by 1st or 2nd week in August. If all goes well (and no modifications are needed) should only take a couple of hours for alignment. Internal components will be ultrasonically cleaned and we will be wearing gloves for assembly.
  We should have the vacuum flange in hand during the 1st or 2nd week in August for installation of view ports and then vacuum certification.
OPG
  We are still in search of a new butterfly seed source with stable output and spectral width of ~0.1 to 0.3 nm and a central wavelength of 1064.3 +/- 0.2 nm
  We may need to add a Peltier Coolier to the FBG on the seed source to adjust the central wavelength of the seed to match the gain spectrum of Nd:YAG
Fiber pre-amp
  PriTel is actively working on constructing the power amplifier with LMA.
  We hope to
Fiber Amplifier (Optical Engines)

## Slide 43: Extra/old slides

## Slide 44: PRE-Shutdown Plans
Assume we start the shutdown 1st week in September.
Optical cavity & vacuum flange in shop being fabricated
All other components on order
Order components for mirror test
Receive optical cavity & components
Ultrasonically clean components (will work gloved after this)
Assemble optical cavity
Alignment of optical cavity in laser lab
Receive vacuum flange
Ultrasonically clean vacuum flange
Install viewports
Leak check
Assemble optical cavity into vacuum flange
Re-check alignment
Check alignment with mirror test components
Leak check full system
Ready for installation