## Slide 1: Enhancements of the Fermilab Booster to Reduce Losses and Extend Lifetime: The Proton Improvement Plan
Robert Zwaska
11 November 2014
HB2014

## Slide 2
  PIP is a critical Fermilab “project” to address desired increases in proton production to meet the present and near term experiments
  PIP’s scope is specific to the FNAL Proton Source
    Proton flux
    Machine reliability
    Machine long term viability
  Official start in FY12
This talk focuses on a few RF and injection/extraction issues
  More on beam dynamics issues in K. Seiya’s talk this afternoon
PIP Introduction
  Project Overview
  Notching
    Kickers
    Laser Neutralization
  200 MHz sources
    Modulator
    PA (tube or klystron)
  Booster Cavity Refurbishment

## Slide 3: Present Proton Production
Linac produces 400 MeV H-
  Bunched at 200 MHz
  35 mA for up to 40 us at up to 15 Hz
Booster produces 8 GeV protons (Booster neutrinos, muons, etc.)
  Bunched at 53 MHz
  Up to 5e12 (typically 4.3e12) in 1.5 us
  Ramps at 15 Hz
    Historically <<= 7 Hz with beam
Main Injector produces 120 GeV protons (NuMI)
  Bunched at 53 MHz
  Up to 5e13 (typically 3.7e13) Operates as quickly as 1.33 s
  With Recycler integration, designed for 700 kW
    Has run at 400 kW

## Slide 4: Linac Overview
Linac | 
Length (m) | 200
Pulse Frequency | 15 Hz
Kinetic Energy (MeV) | .750 - 4
Frequency (MHz) | 201 & 804
Current (operational) | 33 ma (Historical low)
Linac Lattice | LE ? HE - Photo
No of cavities | 5 DTLs, 7 SC, 3 small
LE Linac |  | 
Flat top | 350 | usec
Raise Fall time | 75 | usec
Average Axial Field | 1.5 | MV/m
Rep Rate | 15 | Hz
RF Peak Power | 3.5 | MW
Peak Current | 35 | mA
Beam width | 20 | usec
Power to the beam | 787.50 | KW
Average RF Power | 19.16 | KW
Peak Power | 3.50 | MW
High Energy Linac Gallery
High Energy Tunnel
7835
1
Tank 2
Tank 3
Tank 4
Tank 5
0
M1
M4
M6
750 keV
400 MeV
M2
M5
M7
M3
NTF
7835 Socket
Designed for high intensity single shot proton injection
Linac Overview

## Slide 5
Parameter | Value (units)
Energy | 35 – 750 (keV)
Frequency | 201.25 (MHz)
Length | 120 (cm)
Design current | 60 (mA)
Peak cavity power | ~ 140 (kW)
Radial aperture | 0.3 (cm)
Duty Factor | 0.12%
Pre-Injector Upgrade - RFQ
FNAL considered using RFQ in late 1980's
  BNL and FNAL worked with LBNL on a RFQ design
  200MHz built for BNL but FNAL cancelled order
FNAL initiated the Pre-injector upgrade in 2008
  Fermilab retired C-W in August 2012 after 43 years

## Slide 6
H- ions are stripped and multi-turn injected onto the Booster
Protons are accelerated from 400 MeV to 8 GeV in 33 msec
Fast cycling synchrotron
  Fast magnet ramping
  Frequency of 15 Hz
Single turn extraction
Booster | 
Circumference (m) | 474
Harmonic Number | 84
Kinetic Energy (GeV) | 0.4 - 8
Momentum (GeV/c) | 0.954 - 8.9
Revolution period (msec) | t(inj) 2.77 – t(ext) 1.57
Frequency (MHz) | 37.9 - 52.8
Batch size | 4.5 E12
Focussing period | FDooDFo (24 total)
Booster
Combined Function Magnets
No failures after initial phase…
but 8 spares have been refurbished as part of PIP…
Booster Overview

## Slide 7
Loss limited until 2010
then cycle rate limited
Where PIP started
Booster
loss profile

## Slide 8: Requested Proton Flux
g-2
Mu2e
8 GeV 
120 GeV 
NOvA Shutdown
(NOvA, LBNx)
Existing
Capability
15Hz pulse
15Hz beam

## Slide 9
The Proton Improvement Plan should enable Linac/Booster operation capable of
  Delivering 2.25E17 protons/hour (at 15 Hz) in 2016
while
  Maintaining Linac/Booster availability > 85%, and
  Maintaining residual activation at acceptable levels
and also ensuring a useful operating life of the proton source through 2025
The scope of the Proton Improvement Plan includes
  Upgrading (or replacing) components to increase the Booster repetition rate
  Replacing components that have (or will have) poor reliability
  Replacing components that are (or will soon become) obsolete
  Studying beam dynamics to diagnose performance limitations
  Implementing operational changes to reduce beam loss
Original Goals for the Proton Improvement Plan

## Slide 10: Scope change to PIP
Modifications to PIP objectives to reflect present laboratory planning.
Extend Booster operations to 2030
Linac operations till 2023
Consider transition to PIP II

## Slide 11: Beam and Losses through Cycle
Beam Intensity
Loss Monitors’ Responses
RF Capture
Transition
Extraction
700 MeV Notch

## Slide 12: PIP : Notching
Booster beam requires a notch to allow for the rise time of extraction kicker
  40-50 ns notch
Notch is created by kicking the beam @ 2 different cycle times
  400 / 700 MeV losses down to 5% / 9%
PIP phase approach
  Phase I: notch relocation & new absorber
  Phase II: kicker magnets & power system replacement
  Phase III: create notch in Linac
Absorber L13 (2013)

## Slide 13: Notcher & Absorber Controlling Beam Losses
The plot above shows the difference between two radiation activation surveys after running similar flux for a week. The new system has greatly reduced residual activation in several areas of Booster.
The new notcher system directs the beam to an absorber – old system was not designed for high flux and the kicked ‘notched’ beam into collimators -- uncontrolled
Rad Survey Data
Dec 2013
Notcher Absorber
Collimators
Activation decrease of ~1200mrem/hr

## Slide 14: Laser Notcher
Neutralize a portion of the Linac beam with a pulsed laser
  Remove the majority of the loss from the Booster entirely
Prototype of the laser front-end is operating
  Atypical laser
    Multiple timescales
    High-pulse power
    Moderate average power (few W)
Interaction region installed in Linac

## Slide 15: PIP – Accelerator Physics: Linac Laser Notch
Neutralize portion of the 750 keV beam using a pulsed laser
  Create laser pulse pattern for 200 MHz and 450 kHz
  Amplify pulse using a three-stage fiber amplifier
  Create spatial uniform photon beam
  Insert laser into a zig-zag interaction cavity
System internal review - Aug’14
APT Seminar – Mar’14
Final installation expected FY15
Laser port
beam
VC/OC installed Sep’14
200 MHz pulses
450 kHz “notch” spacing
Optical cavity
10-12 bunches
done
in-progress
installed

## Slide 16: PIP – Linac 200 MHz RF system: issues & risks
The 201.25 MHz RF power system has been a big concern for over a decade in regards long term operational reliability and viability
The issue of retaining the 201.25 MHz RF system is
  specialized maintenance required and extensive downtime generated by the tube modulator
    F1123 discontinued production for over 10 years
  short lifetime, high-cost & limited market of the final power amplifier
The risk of retaining the 201.25 MHz RF system is that
  power tubes could become unobtainable to support operations until 2025
  additional vacuum tubes could become obsolete in the modulator &
    F1123 no longer be rebuilt -> years of operation ~ 6 years
PIP plan to address these issues is
  build-up 4 year in-house inventory of the 7835
  develop a workable plan to replace the final amplifier in case tube line production is discontinued
  replace the high voltage modulator with present day technology

## Slide 17: PIP – Linac 200 MHz RF system: Modulator
Modulator provide pulsed power to the plate of the 7835 triode
  Plate modulation to provide tank field control
Modulator contribution to Linac downtime is ~57%
  Depending on the nature of the fault, each event may bring the system down from a few minutes up to tens of hours
  MTBF: ~ 10 hrs
    DC pwr sply – built directly to the frame
    Switch tubes no longer manufactured
      Rely on rebuilds to operate
    Outdated relays & interlocks
    Minimal diagnostic capability
gradient
voltage
current
FFPW
60kV
35 amp
DC PS
30kV
350 A
Modulator
F1123
3 triodes
FPA 7835
plate
10-35kV
100-350 A
0.6MW
3.5MW

## Slide 18: PIP – Linac 200 MHz RF system: Modulator
AD/EE design
best meets original specifications
lower cost than SLAC
in-house expertise
Modulator upgrade – 35 kV, Marx-topology modulator to drive triode
  Could even drive klystron with proper pulse transformer
SLAC “ILC-like” modulator (uses 3 kV cells)
  ILC Mark modulator (-120 kV/140Amp w/ 32 cells)
  modified ILC (35kV/350 Amp w/ 15 cells)
AD/EE designed using modulator specification
  designed with 1 kV cells, requiring 53 cells total
  built 9 cell modulator for testing (see pictures)
  building 25 cell modulator for further testing
  plan to build full 53 modulator prototype in FY15

## Slide 19: PIP – Linac 200 MHz RF system: PA
201.25 MHz final power amplifier
  Single vendor: Photonis USA (former Burle)
  National laboratories are the only users (FNAL,BNL,LANL*)
  Typical delivery time: 200 days
  Operation needs: 5 tubes
  Lifetime: ~ 8-10 months
*LANL upgraded one tank to diacrode Jul/2014
12k -15k
7.5k
There is no RF conditioning at the vendor site
  Typical 15 days/tube for 2 techs
  6 tubes conditioned annually
  Time consuming effort
  (4-5 months)

## Slide 20: PIP – Linac 200 MHz RF system: HLRF
Study conducted in 2012 discussed alternatives to the triodes
  Tetrodes (LANL design)
  Klystron-based 200 MHz RF
  “SNS-like” 400 MHz Linac
  Cost took in consideration series of criteria evaluated against over the expected lifetime of the Linac
    Criteria: supply chain, technical risk, M&S/labor construction, upgrade time, maintenance cost and program interruption time
After careful consideration,
the 201.25MHz klystron-based
RF power system was chosen as
a plausible replacement for the
7835 triode
A prototype is being designed and built at CPI

## Slide 21: PIP – Linac 200 MHz RF system: HLRF
Gain (dB)
Drive power Pin(kW)
51
45
40
0 100 200 300 400 500
5.5
2.5
0
Peak power (MW)
Courtesy:
5.0 MW
122 kV, 85.2 A
Pin 340 W
DTL
f0: 201.25 MHz
Saturated efficiency: > 48%
Perveance: 2.0 mA/V1.5
PRF: 15 Hz
Pulse length: 450 msec
Jcath : 1 A/cm2
Expected lifetime: > 200 hrs
Collector
5 cavity RF
circuit design
OC
IC
Gun
PIP to PIP-II adjustment:
task completes after successful acceptance-test
16’
6’

## Slide 22: Booster RF cavity
Designed in 1969 – several small modifications but largely original cavity
- 19 stations
- 2 gaps @ ~ 24 kV
- Tunable 24 – 53 MHz
- Power amplifier system already upgraded to solid-state in PIP

## Slide 23: Booster PIP - Refurbishment of 40 year old cavities
Cavity Removal
Cool-down
Remove Tuners
Rebuild - Cones & Tuners
Rebuild Stems/Flanges
Re-Assemble
Testing
(Weeks)
Cavity Removal - Stripping
Tuners Rebuild
Rebuild and Test

## Slide 24: Booster refurbishment
Goals: Completion of Refurbishment in FY15
  (19+1) cavities after refurbishment is complete
    (+1) comes from an originally rejected cavity
  22 cavities will be the final number
    2 cavities will come from the Proton Driver project after modifications to their aperture
  Reliable 15 Hz operations will require overhead
    Uncertain failure rate at 15 Hz operations
    At least 17 cavities for 4.5e12 protons per pulse
      longitudinal beam quality is decreased, higher losses through transition.
  Make 20 spare tuners (3 tuners per cavity)
    New tuners will be made by TD for refurbishment as well as for long term operations.
      Reduced repair time
      Lower worker exposure rate

## Slide 25: Booster RF cavity refurbishment status

## Slide 26: New tuners
Build new tuners to replace complete failures, accelerate refurbishment process, and reduce worker dose
New tuner has been in service for 10 weeks of running
Placed requisition for ferrites (enough for 20 tuners)
  worked with vendor (National) for 2+ years to get recipe for ferrites correct
  Delivery before end of year – ready to build immediately

## Slide 27: Booster RF station (Solid State upgrade completed in FY13)
Original Booster RF Station
Upgraded RF Station
with SSD + New Modulator
Ferrite Bias Supply
Modulator
Modulator
Control Rack
Ferrite Bias Supply
SSD
Controls

## Slide 28
Proton Improvement Plan Bill Pellico Bob Zwaska, Deputy Kenneth Domann, Project Controls Valeri Lebedev, Senior Physicist
Booster Keith Gollwitzer
200 MHz RF Power System Fernanda G. Garcia
High-Level RF J. Steimel
Linac Modulator Trevor Butler
7835 Procurement Fernanda G. Garcia
Instrumentation Craig Drennan
Utilities
Matthew Gardner
Power Distribution Ryan Crawford
RF John Reid
Anode Supply Ryan Crawford
Bias Supply Pat Sheahan
New Tuners Matt Slabaugh
New Cavities C.Y. Tan
Cavity 1013 Matt Slabaugh John Reid
Accelerator Physics Bob Zwaska
Booster Collimation Valeri Lebedev
Radiation Shielding Keith Gollwitzer
Alignment & Aperture Kiyomi Seiya
Booster Notcher Salah Chaurize
Low-Conductivity Water System David Hixson
Power Distribution Ryan Crawford
Vacuum System Dave Augustine
Solid State Upgrade John Reid
Power Amplifier Steve Kotz
Driver Module Tom Kubicki
Cavity Test Stand Pat Sheahan
Linac Notch Creation Dave Johnson
Simulations & Studies Valery Kapin
Accelerator Physics Valeri Lebedev
Vacuum System Dave Augustine
Modulator Rene Padilla
Installation Rene Padilla Steve Kotz
Instrumentation Craig Drennan
Dampers Nathan Eddy
Utilities Todd Sullivan
Booster Cogging Kiyomi Seiya
Beam Position Monitors Nathan Eddy
Simulation & Studies Bob Zwaska
Linac Fernanda G. Garcia
Cavity & Tuner Refurb. Matt Slabaugh
RFQ Injector C. Y. Tan
Beam Position Monitors Nathan Eddy
Low-Cond. Water System Matt Gardner

## Slide 29
Conclusion
PIP has been working for three years
  Many infrastructure upgrades already performed
  Notching improvements are straightforward path to higher throughput
    Control loss with improved notching in Booster
    Eliminate loss with laser notching in MEBT
  200 MHz RF: replace modulators, reduce risk on power amplifiers
  Booster cavities: refurbish all, gain overhead, replace many parts
Transition time coming for PIP:
  Increased proton demand to be realized with Recycler commissioning, new experiments
  Scope adjustments to anticipate a PIP-II Linac replacement

## Slide 30: Enhancements of the Fermilab Booster to Reduce Losses and Extend Lifetime: The Proton Improvement Plan
Robert Zwaska
11 November 2014
HB2014