Transmission line model of cavity with coupler
C.Y. Tan
30 Sep 2014

---
Goal
- Create semi-analytic model to see what's going on.
  - Voltage profile along the cavity.
  - How to add coupler.
  - What the reflection coefficient is at the coupler.
  - Does adding a “neck” help with impedance matching or voltage shaping? ←not done yet!
- Caveat Emptor! Results discussed here are all PRELIMINARY probably not right!
  - Subject to change without notice, apologies or regret!!!!

---
Transmission line model
Neglecting this part
Inspiration for neck
Too complicated! So work with even simpler model

---
Simple garnet loaded cavity

---
Results
I force the length of the garnet+non-garnet part = 3π/2 or 3λ/4 and find that:
Length of garnet =0.35 m
Length of non-garnet = 0.5 m
Gap capacitance = 18.76 pF

---
Results (cont'd)
- The cavity must be at least 3λ/4 because the garnet length even in MWS has more than π/2 phase change in it.
- The cavity can be any length that we want depending on the gap capacitance.
  - I found the gap capacitance to be ~20 pF, expect ~1 pF at 76 MHz
    - Source of the problem is that zf = 60*Sqrt[μr/εr]Log[ro/ri] and for μr=3.5 and εr=14, Sqrt[3.5/14] = 0.5 < 1. And so for the same βl, the inductance is smaller (Z = i z0 Tan[βl] for shorted coaxial line). From the geometry of the model zf = 17.17Ω and z=62.9Ω.
    - I need to understand this! Is this a problem of the way I've set up my model?
  - There is a reduction in length, in general, from the resonant length of a shorted transmission line (λ/4 or 3λ/4) due to the gap capacitor.
  - The length will affect Rs, so have to be careful. Q=π/4*(z/Rs) where z is the characteristic impedance.

---
Coupler
Location of coupler will be in the middle of the non-garnet part.
The centre conductor has radius 5” because of the tube anode constraints.
rci = 5”=0.127 m, rco=0.25 m and so zc=40.6Ω.
I chose the length of the coupler transmission line = 20 cm (← not the right way to do this, according to Joe)
Cc = 8 pF, Ct = 56 pF.

---
Getting the resonance
Found lf to be a little shorter compared to without coupler.
Lf = 0.335 m compared to 0.35 m previously.

---
Reflection coefficient
Doesn't work. Too much reflection for the entire range!
Talked to Joe Dey, he suggests that I need to find the point on the line that cancels the cavity impedance.

---
Stupidly connecting coupler introduces more problems
Do the simplest case where the cavity imaginary part of the impedance is zero at the coupling point. Then, I find that
Ooops! Coupler length is 3 m!!!!
Much more reasonable. So it is not sufficient to randomly select coupling point to be at the centre of the cavity!
Fine tune length of cavity so that at the coupling point, the imaginary part of the cavity impedance nearly cancels Zc. This could be the trick!

---
Clearly more work needs to be done!
- Figure out why Cg is so large. Model problems?
- Figure out the location of the coupler so that the impedance at the coupling point mostly cancels the impedance of the coupling capacitor.
- Make sure that the entire device does resonate with the coupler added
  - Make sure that the reflection coefficient is ok.
- Perhaps Ding's HFSS? Model will give a better result.