## Slide 1
March 17, 2015
C. Wiesner, M. Droba, O. Meusel, D. Noll,
O. Payir, U. Ratzinger, P. Schneider
IAP, Goethe-Universität Frankfurt am Main
Chopping and Transport of Low-Energy Ion Beams for FRANZ

## Slide 2: Outline
Introduction: Neutron Production
Overview: The FRANZ Facility
LEBT and Chopper System
  E×B Chopper Concept
  Numerical Simulations
  Experimental Results
3) Conclusion

## Slide 3: Introduction: Neutron Research
Material Science
Sensitivity for magnetic properties
High penetration depth in material
Sensitivity for different isotopes
Sensitivity to light elements (e.g. hydrogen)
Neutron imaging
Test radiation durability (detectors, fusion materials)
Cancer treatment (BNCT)
Neutron capture process relevant for ADS, nuclear astrophysics, …
Notes: Siehe „ Strategiepapier zur Neutronenforschung in Deutschland: 2015-2045“
Opportunities for material science

## Slide 4: Introduction: Nuclear Astrophysics
Stellar nucleosynthesis:
About 50% of the element abundances beyond iron are produced via the s-process.
s-process takes place in AGB stars.
Neutron temperature: kBT = 8 to 90 keV [Reifarth et al., 2014].
Modelling requires neutron capture cross-sections from 1 to 400 keV.

## Slide 5: Introduction: Neutron Production Facilities
Spallation Neutron Sources
Short Pulse
Synchrotrons or compressor rings
Pulse length: ~μs
Long Pulse
Linacs
Pulse length: ~ms
Continuous
Cyclotrons
 | Fission Reactors | Spallation Sources | Small-Scale Accel.-Driven Facilities
Typical production mechanism | fission of 235U | high energy protons (100s MeV to GeV) on heavy metal target. | protons/deuterons (several MeV) on Li or Be target.
Costs |  |  | 
Neutron flux | high (average) flux | High (peak) flux (ESS) | Moderate flux
Time structure | challenging | CW (SINQ), short pulse (SNS), long pulse (ESS) | CW to short pulsed
Neutron energy | MeV, moderated to thermal spectrum | Wn < Wp (emerging particles); (evaporating particles) | 
Angle distribution | isotropic | forward / isotropic | kinematic collimation
 | Fission Reactors | Spallation Sources | Small-Scale Accel.-Driven Facilities
Typical production mechanism | fission of 235U | high energy protons (100s MeV to GeV) on heavy metal target. | protons/deuterons (several MeV) on Li or Be target.
Costs |  |  | 
Neutron flux |  |  | 
Time structure | challenging | CW (SINQ), short pulse (SNS), long pulse (ESS) | CW to short pulsed
Neutron energy | MeV, moderated to thermal spectrum |  | 
Angle distribution | isotropic | forward / isotropic | kinematic collimation
Notes: FRM-II, München: >400 Mio Euro Kosten, 20MW Nennleistung. 8E14 n/s/cm^2
ILL, Grenoble: 55 MW Leistung
PIK, Gatchina, (St.Petersburg): 100 MW Therm. Leistung, neutron flux: 5e15 cm-2 s-1
TRIGA (66 weltweit): Leistung: 20kW bis 16 MW.
„TRIGA-Reaktoren können im Puls-Betrieb gefahren werden. Das heißt, dass der Reaktor ungeregelt bis in den prompt überkritischen Zustand angefahren wird. Der Neutronenfluss und damit die Wärmeleistung steigt sehr schnell an, bis der negative Temperaturkoeffizient der Reaktivität der Brennstäbe den Reaktor wieder unterkritisch macht.[1] Die Impulsdauer beträgt etwa 30 ms. Wegen der Restwärme in den Brennelementen muss der Reaktor dann bis zum nächsten Impuls abkühlen. Bei diesem Betrieb werden sehr hohe Impulsleistungen und Neutronenflussdichten erreicht, die im kontinuierlichen Betrieb nicht möglich wären.“
„TRIGA is no ordinary light water reactor because much of its "moderation" of neutrons is due to the hydrogen that is mixed in with the fuel itself. Therefore, as the fuel temperature increases when the control rods are suddenly removed, the neutrons inside the hydrogen-containing fuel rod become warmer than the neutrons outside in the cold water. These warmer neutrons inside the fuel cause less fissioning in the fuel and escape into the surrounding water. The end result is that the reactor automatically reduces power within a few thousandths of a second, faster than any engineered device can operate. In other words, the fuel rods themselves act as an automatic power regulator, shutting the reactor down without engineered devices. “
Der totale Neutronenfluss im Kern eines typischen Druckwasserreaktors liegt bei etwa 1013 cm−2s−1.
Die Spallations-Neutronenquelle SINQ erreicht 1014 cm−2s−1, der Forschungsreaktor FRM-II 8×1014 cm−2s−1.[4]
In einem Fusionsreaktor wird die Wand des Plasmagefäßes ebenfalls einem Neutronenfluss von etwa 1014 cm−2s−1 ausgesetzt sein[5].
„Reactor-based sources now produce 1015 n/(cm² s), and spallation sources generate greater than 1017 n/(cm² s).”
“nuclear fission produces neutrons with a mean energy of 2 MeV (200 TJ/kg, i.e. 20,000 km/s), which qualifies as "fast". However the range of neutrons from fission follows a Maxwell–Boltzmann distribution from 0 to about 14 MeV in the center of momentum frame of the disintegration, and the mode of the energy is only 0.75 MeV, meaning that fewer than half of fission neutrons qualify as "fast" even by the 1 MeV criterion.”
… Moderation..
Fast reactors use unmoderated fast neutrons to sustain the reaction

## Slide 6: Neutron Energy Spectrum
Arai and Crawford, p.18
Measured at FZ Karlsruhe for a primary proton energy of 1.991 MeV (flight path: 0.8m) [Beer et al., 2001].
Spectrum from Spallation Source (20 GeV protons on Pb target)
Measured at n-TOF, CERN (flight path: 200m) [Colonna et al., 2010].
n energy:
1…100 keV
Spectrum from small-scale facility
using the reaction.
Notes: Colonna: “Simulated and measured neutron fluence per proton pulse, available for measurements in the experimental area, at 200 m from the spallation target.“
The neutron fluence is defined as the neutron flux integrated over a certain time period.
n-tof: 5E4 n/s/cm^2 between 1… 100 keV (2007)

## Slide 7: Time-of-Flight (TOF) Method
TOF method allows to measure the neutron capture cross-sections as a function of the neutron energy.
Pulsed primary beam and fast (<1 ns) gamma calorimeter required.
Adequate neutron spectrum assures low background.
4p BaF2 detector at Frankfurt.
(n,g)
on sample
TOF [ns]
0
160
80 cm flight path
En = 1..200 keV
Other Reactions
Prompt Flash
En=128 keV
I [a.u]
En=200 keV
130
© R. Reifarth

## Slide 8: Frankfurt Neutron Source FRANZ
Physics Building, Goethe-Universität Frankfurt
FRANZ is currently under construction at Frankfurt University:
Deliver neutrons for nuclear astrophysics and material sciences
Accelerator test bench
Education of students in accelerator physics
Experimental Hall, IAP

## Slide 9: Frankfurt Neutron Source FRANZ
Deliver a high (peak) neutron flux,
produced via the 7Li(p,n)7Be reaction,
for the energy-dependent measurements of n-capture cross sections (using TOF).
with high intensities (50-200 mA),
at 2 MeV beam energy,
with a challenging time structure (1 ns, 257 kHz).
This requires a primary proton beam
Frankfurt Neutron Source FRANZ
Goal in Compressor Mode:
LEBT
Activation Mode:
2 mA, cw operation

## Slide 10: Frankfurt Neutron Source FRANZ
Arc-discharge driven ion source
Proton current: 50 mA (240 mA)
Current density: 480 mA/cm2
DC operation
Proton fraction > 90 %
Beam energy: 120 keV
εrms, norm < 0.08 mm∙ mrad
High-Current Ion Source
© K. Volk, W. Schweizer
Frankfurt Neutron Source FRANZ
LEBT
Notes: At the moment, the ion source is undergoing a detailed
test program at a dedicated ion source test stand. A proton
beam current density of 480 mA/cm2 was achieved during
dc operation using a total arc power of 9.7 kW. For an emission
opening radius of 4mm, a proton current of 240mA
was extracted at 50 keV beam energy. By manipulating the
plasma properties, the percentage of the undesired hydrogen
fractions, H+
2 and H+
3 , can be reduced to less than 10% [5].
First beam emittance measurements show an 89%-rms emittance
of ǫ rms, norm = 0.08mm·mrad at 52 keV energy and
at a normalized beam current of 85mA [6].

## Slide 11: Frankfurt Neutron Source FRANZ
CW operated
frf = 175 MHz
RFQ under construction
IH is being copper plated
RFQ test module tested with Prf ≈ 115 kW/m
2 MeV Linac Section
120 keV
700 keV
2 MeV
RFQ
IH
© M. Heilmann, U. Ratzinger, A. Schempp
Frankfurt Neutron Source FRANZ
2.4 m
LEBT
RFQ test module

## Slide 12: Frankfurt Neutron Source FRANZ
Mobley Type
Electric Kicker (f = 2.5 MHz)
Magnetic Guiding System
Rebuncher Cavities
Frankfurt Neutron Source FRANZ
Bunch Compressor
tp =1 ns,
257 kHz
tp > 50 ns,
257 kHz
DC
L. P. Chau et al., LINAC’10, MOP100
LEBT

## Slide 13: Frankfurt Neutron Source FRANZ
Frankfurt Neutron Source FRANZ
DC
LEBT Section
Sol1
Sol2
Sol3
Sol4
Chopper
tp =1 ns,
257 kHz
tp > 50 ns,
257 kHz
Mobley Type
Electric Kicker (f = 2.5 MHz)
Magnetic Guiding System
Rebuncher Cavities
Bunch Compressor
L. P. Chau et al., LINAC’10, MOP100
LEBT

## Slide 14: E×B Chopper: Motivation
Electric Deflection
Disadvantages: Risk of voltage breakdowns, especially at high beam intensities and especially for a high duty factor of the electric deflection field.
Disadvantages: High power consumption, especially at high repetition rates.
Magnetic Deflection
Requirements: Chopping a dc beam at
– low energy (120 keV)
– high intensity (50 mA)
– high repetition rate (257 kHz),
– producing a short beam pulse: 50 ns / 3.9 ms.
High duty cycle for electric field.
Combining static magnetic and pulsed electric deflection in an E×B (Wien-filter) field configuration.
Low duty cycle for
electric field.
Concept

## Slide 15
Dumped Beam
Pulsed
Beam
DC
Beam
Chopper Magnet
Sol3
Sol2
E×B Chopper: Concept
Separation Magnet
Shielding Tube
0.8 m

## Slide 16
B0 ≈ 60 mT
E×B Chopper: Concept
B0 ≈ 250 mT
Dumped Beam
DC
Beam
Chopper Magnet
Sol3
Sol2
Vdefl = 0 kV
Electric Deflector
Shielding Tube
Separation Magnet

## Slide 17
E×B Chopper: Concept
Pulsed Beam,
frep = 257 kHz,
t = 50 ns … 350 ns
DC
Beam
Chopper Magnet
Sol3
Sol2
B0 ≈ 60 mT
B0 ≈ 250 mT
Shielding Tube
Vdefl = 12 kV
Electric Deflector
Separation Magnet

## Slide 18: Beam Dynamics in Static E×B Fields
Magnetic
Dipole
Longitudinal Matching of Deflection Forces
Beam
z
y
(p, 120 keV)

## Slide 19: Beam Dynamics in Static E×B Fields
Beam
Magnetic
Dipole
Shortening
Tubes
Longitudinal Matching of Deflection Forces
z
y
(p, 120 keV)

## Slide 20: Beam Dynamics in Static E×B Fields
Beam
Magnetic
Dipole
Shortening
Tubes
Optimized
Pole Profile
Longitudinal Matching of Deflection Forces
z
y
(p, 120 keV)

## Slide 21: Beam Dynamics in Static E×B Fields
Particle Tracking, Protons, 120 keV.
Transverse Matching of Deflection Forces

## Slide 22: Beam Dynamics in Static E×B Fields
 Focusing Effect in x direction.
Beam
Acceleration
Deceleration
vl < v0 < vr
Velocity Change:
Felec
Fmag
̶
+
Effect 1: Wien-Focusing Effect.

## Slide 23: Beam Dynamics in Static E×B Fields
Effect 2: Given inhomogeneous field distribution.

## Slide 24: Beam Dynamics in Static E×B Fields
Superposition of both effects.

## Slide 25: Beam Dynamics in Static E×B Fields
Particle Tracking, Protons, 120 keV.

## Slide 26: Beam Dynamics in Static E×B Fields
Magnetic
Dipole Yoke
Shortening
Tubes
Longitudinally
Optimized
Pole Profile
Longitudinal Matching of Deflection Forces
z
y
Minimizing horizontal beam movement
Minimizing position offset
Transverse Matching of Deflection Forces
- Focusing in both transverse planes
- Preserving cylindrical symmetry
Compensation of
Velocity Change
Field
Homogenization
Beam
Optimized Pole Profile:
x
y
Field Simulations
using CST EMS.
Beam

## Slide 27: Beam Shaping Simulation
Input Data
Wb = 120 keV
Iproton = 50 mA
Matched Input Distribution
3d E-field of deflect. plates
3d B-field of chopper magnet
3d B-field of solenoids
Measured HV Pulse
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
By Daniel Noll.
Beam

## Slide 28: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Voltage Pulse

## Slide 29: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Voltage Pulse

## Slide 30: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Voltage Pulse

## Slide 31: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Voltage Pulse

## Slide 32: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Voltage Pulse

## Slide 33: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Voltage Pulse

## Slide 34: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Voltage Pulse

## Slide 35: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Voltage Pulse

## Slide 36: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Beam Pulse
Voltage Pulse

## Slide 37: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Beam Pulse
Voltage Pulse

## Slide 38: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Beam Pulse
Voltage Pulse

## Slide 39: Beam Shaping Simulation
p, 50 mA
H2+, 5 mA
H3+, 5 mA
Beam dynamics calculations using PIC-Code Bender.
Beam Pulse
Voltage Pulse

## Slide 40: Beam Shaping Simulation
Simulated Pulse Shape
at the RFQ Entrance
Results of
Numerical Simulations:
50 ns
Time requirements fulfilled.
50 ns flat top:
  Position offset below ±0.3 mm (necessary condition: longitudinal matching of deflection forces).
  Low emittance.
  Cylindrical symmetry preserved (necessary condition: transverse matching of deflection forces).
Low transmission for H2+ and H3+ ions (pulsed velocity filter).
Simulated without collimator system in front of the RFQ.

## Slide 41: Chopper Hardware Design
Electric Deflector
Magnetic Dipole
V0 = ±6 kV
frep= 257 kHz
lplate = 15 cm
hplate = 8 cm
Deflection Chamber
B0 = 130 mT
Icoil = 130 A
ldipole = 15 cm
hgap= 11 cm
Yoke
Exchangeable
Pole Plates
Coils
Deflection Chamber in Dipole
Beam

## Slide 42: Commissioning
HV Terminal: 150 kV
Concrete Shielding for linac and neutron target
LEBT Section and E×B chopper

## Slide 43: Measurements: DC Beam
Emittance measurement behind Solenoid 1
He+,
10 keV,
0.9 mA

## Slide 44: Measurements: DC Beam
Measured using
slit-grid device,
installed behind Sol1.
Simulated using Lintra code, assuming 85% space charge compensation.
He+,
10 keV,
0.9 mA

## Slide 45: Measurements: DC Beam
He+,
10 keV,
0.9 mA
Phase-space angle
Kurtosis

## Slide 46: FRANZ LEBT: Overview
Faraday Cup 1
HV Pulse
Generator
Beam Current
Transformer
E×B Chopper
Sol1
Sol2
Sol3
Sol4
Ion Source:
He+, 14 keV
Aperture: r = 50 mm
Faraday
Cup 2
L = 3.7 m

## Slide 47: Measurements: Repetition Rate
He+, 14 keV
raperture = 50 mm
Idipole = 40.0 A
Beam chopping at 257 kHz experimentally achieved.
Ratio of Pulsed to DC Beam Current of
95.2% ± 1.6%
achieved.
frep = 257 kHz

## Slide 48: Measurements: Pulse Shape
Gen. perveance K = 2.73e-3 (equivalent to 175 mA, p, 120 keV).
Rise Time:
120 ns ± 10 ns
Reliable chopping and transport was achieved even for high-perveance beams.
He+, 14 keV
raperture = 50 mm
Idipole = 40.0 A
50 ns
Notes: K equivalent to 21.9 mA, H-, 30keV

## Slide 49: Measurements: Variation of Wien Ratio
const.
sweep
He+, 14 keV
raperture = 50 mm
Idipole = 40.0 A

## Slide 50: Measurements: Variation of Wien Ratio
const.
sweep
He+, 14 keV
raperture = 50 mm
Idipole = 40.0 A

## Slide 51: Measurements: Variation of Wien Ratio
const.
sweep
He+, 14 keV
raperture = 50 mm
Idipole = 40.0 A

## Slide 52: Measurements: Variation of Wien Ratio
const.
sweep
He+, 14 keV
raperture = 50 mm
Idipole = 40.0 A

## Slide 53: Measurements: Variation of Wien Ratio
const.
sweep
He+, 14 keV
raperture = 50 mm
Idipole = 40.0 A

## Slide 54: Measurements: Variation of Wien Ratio
const.
sweep
He+, 14 keV
raperture = 50 mm
Idipole = 40.0 A

## Slide 55: Measurements: Variation of Wien Ratio
const.
sweep
He+, 14 keV
raperture = 50 mm
Idipole = 40.0 A

## Slide 56: Measurements: Variation of Wien Ratio
const.
sweep
He+, 14 keV
raperture = 50 mm
Idipole = 40.0 A

## Slide 57: Measurements: Variation of Wien Ratio
Highest flat-top charge achieved for the theoretically derived Wien condition.
Adequate matching of electric and magnetic deflection forces.
const.
sweep
He+, 14 keV
raperture = 50 mm
Idipole = 40.0 A

## Slide 58: LEBT: PXIE and FRANZ
 | PXIE | FRANZ – Commissioning | FRANZ - II
 | H- | He+ | p
Beam Energy | 30 keV | 14 keV | 120 keV
Beam Current | 5 (10) mA | < 3.5 mA | 50 (200) mA
Beta | 0.8% | 0.27% | 1.6%
Gen. Perveance | 6.25E-04 | 2.74E-03 | 7.81E-04
Chopping in (center of) LEBT | yes | yes | yes
Pulse Length | > ms | 100 ns to ms | 100 ns to ms
Rep. Rate | 1 to 60 Hz | 103 to 257 kHz | 103 to 257 kHz
Numbers of Solenoids | 3 | 4 | 4
Notes: Time structure complementary.

## Slide 59: Conclusion
  Accelerator-driven neutron source FRANZ currently under construction.
  E×B chopper and LEBT section have been commissioned with beam: ready for pulsed & dc operation.
  The LEBTs for FRANZ and PXIE allow…
    investigation of high-perveance beams…
    …with positive (FRANZ) and negative (PXIE) ions…
    …in dc or in pulsed mode…
    …using different neutralization schemes,…
    which is a promising basis for further cooperation.

## Slide 60
Thanks to…
FRANZ team: M. Heilmann, B. Klump, O. Meusel, H. Podlech, U. Ratzinger, A. Schempp, P. Schneider, M. Schwarz, W. Schweizer, K. Volk.
NNP group: A. Ates, M. Droba, S. Klaproth, O. Meusel, D. Noll, O. Payir, P. Schneider, H. Niebuhr, B. Scheible, K. Schulte, J. Wagner, K. Zerbe.

## Slide 61
Blue skies,…
…green rivers…
…and fascinating science.
Thank you for your attention!

## Slide 62
Backup

## Slide 63: Beam Measurements

## Slide 64: Measurements: DC Transmission
Helium Beam
Eb = 14 keV
Isol1 = 147 A
Isol2 = 70 A
Isol3 = 140 A
Isol4 = 183 A
Vrepell = -200V
Length: 3.5 m
Perveance K = 1.76 · 10 −3 (equiv. 113 mA, p, 120keV)
Test Ion Source
Notes: Check Divergenzwinkel Quelle klein/groß
Emittanz
Check Parameter Netzteil

## Slide 65: Measurements: Transmission of Chopped Beam

## Slide 66: Measurements: Noise Correction

## Slide 67: Measurements: Noise Correction

## Slide 68: High-Perveance Beams

## Slide 69: Measurements: Beam Energy Variation & TOF
TOF (p, 120keV) = 231.6 ns
Helium Beam
Eb = variable
Rep.Rate = 257 kHz
rslit = 50 mm
Isol1 = 176.6… 60.1 A
Isol2 = 0 A
Isol3 = 182…64.9 A
Isol4 = 0 A
Idipole = 35.0 A
Upulser = 44.1…19.2 V
dtof = 1.349 m
TOF

## Slide 71: Simulations

## Slide 72: Pulsed Beam Dynamics: Beam Shaping
Input Parameters
Wb =120 keV
Iproton = 50 mA
3d E-field calc. deflec. Plates
3d B-field calc. solenoids
3d B-field calc. Chopper magnet
3d B-field calc. septum magnet
Simulated Beam Pulse Behind Chopper
Using 2nd Non-Central Moments!

## Slide 73: Pulsed Beam Dynamics: Beam Shaping
Input Parameters
Wb =120 keV
Iproton = 50 mA
3d E-field calc. deflec. Plates
3d B-field calc. solenoids
3d B-field calc. Chopper magnet
3d B-field calc. septum magnet
Simulated Beam Pulse Behind Chopper

## Slide 74: Pulsed Beam Dynamics: Beam Shaping
Input Parameters
Wb =120 keV
Iproton = 50 mA
3d E-field calc. deflec. Plates
3d B-field calc. solenoids
3d B-field calc. Chopper magnet
3d B-field calc. septum magnet
Offsets Behind Chopper (no solenoids)

## Slide 75: Pulsed Beam Dynamics: Beam Shaping

## Slide 76: Pulsed Beam Dynamics: Beam Shaping
Sim. Beam Pulse Behind Chopper
Sim. Beam Pulse at RFQ Entrance
100 ns
70 ns
40 ns
110 ns

## Slide 77: Pulsed Beam Dynamics: Beam Shaping

## Slide 78: Simulations: Variation of Wien Ratio
Input Parameters
Wb =120 keV
Iproton = 50 mA
3d E-field calc. deflec. Plates
3d B-field calc. solenoids
3d B-field calc. Chopper magnet
3d B-field calc. septum magnet

## Slide 79: Effective Fields

## Slide 80: Pulsed Beam Dynamics: Beam Shaping
Variation of Aperture Radius

## Slide 81: DC Beam Transport
Electric Deflection Plates
Beam Matching in LEBT Section
Ion Source
p, 120 keV:
Transmission: 98%
100% Beam Envelope
Matching of Defl. Forces
Halo Collimation

## Slide 82: HV Pulse Generator

## Slide 83: HV Pulse Generator
Requirements:
frep =250 kHz
V0 = ± 5 kV
R = 47 kΩ
Ferrite Cores
MOSFETs
(Thomson-Board)
Diodes

## Slide 84: HV Pulse Generator

## Slide 85: Repeller Electrodes/ Shortening Tubes
In situ HV tests:
V = - 5 kV
Requirements: V = -0.5 kV
Material:
Magnetic Steel
Insulating Flanges
& Sleeves
155 mm
70.5 mm
Homogenous Beam,
Ib = 50 mA, rb = 10 mm
 Φb = 400 V
Beam Potential:
Electric Deflection Field:
 Electron Flux on Deflector Plates
Decompensation of Proton Beam
 Installation of Repeller Electrodes
 500 Vrepell required.

## Slide 86: Technical Design

## Slide 87: Chopper Dipole: Field Measurements

## Slide 88: LEBT Simulations

## Slide 89: DC Beam Transport
Transport Simulation (Lintra)
100% Proton Envelope
Ion Source
Halo Collimation
RFQ
Ion Source:
p: 50 mA
H2+: 5 mA
H3+: 5 mA
Total Transmission
p: 97.2%
H2+: 1.0%
H3+: 0.3%
Sol1
Sol2
Sol3
Wb = 120 keV,
IGUN Input Distribution

## Slide 90: DC Beam Transport
Ion Source Distributions

## Slide 91: DC Beam Transport

## Slide 92: DC Beam Transport

## Slide 93: DC Beam Transport: RFQ Matching

## Slide 94: DC Beam Transport

## Slide 95
Beam Separation System

## Slide 96: Beam Separation: Concept
Beam separation desirable for high beam power.
Three different „massless“ septa systems and one conventional system were developed and optimized.

## Slide 97: Beam Separation: Halfpipe Septum
Beam separation desirable for high beam power.
Three different „massless“ septa systems and one conventional system were developed and optimized.
Halfpipe Massless Septum proved to be the most promising.
C-Type
Magnetic Dipole
Coils
Shielding Tube
(Vacuflux 50)
x
y
On-Axis
Beam
Pre-Deflected Beam

## Slide 98: Beam Separation: Halfpipe Septum
C-Type
Magnetic Dipole
Coils
Shielding Tube
(Vacuflux 50)
x
y
On-Axis
Beam
Pre-Deflected Beam

## Slide 99: Beam Separation: Halfpipe Septum
C-Type
Magnetic Dipole
Coils
Shielding Tube
(Vacuflux 50)
x
y
B field on axis
reduced from
By = -31.6 mT to
By = -0.3 mT.

## Slide 100: Beam Separation: Beam Simulation
Emittance of 50 ns Flat Top
With Septum:
No Septum:
Sim. with
septum field
Sim. without
septum field