Summary of impedance, PA, and cathode resonator results with new AL800 μ measurements
C.Y. Tan
R. Madrak
02 Apr 2015

---
The new measurement

---
Summary of dimensions used in calculations
0.35 m
0.09625 m
0.112181 m
0.28875 m
l_f
Parameter	value	comments
Z1, Z2	61.299 Ω	Non-ferrite characteristic impedance
Zc	20.9269 Ω	Characteristic impedance of coupler
Parameter	value	comments
Cc	10 pF	Coupling capacitance
Ct	60 pF	Tube capacitance
Cg	3.4 pF	Gap capacitance
rfi	0.105 m	Inner radius of ferrite
rfo	0.170 m	Outer radius of ferrite

---
Equivalent circuit in ADS

---
Example ADS results at 76 MHz
At 76 MHz:
Shunt impedance = 81.6 kΩ
Ranode = 649 Ω
Q = 2345

---
The following are results from Mathematica (essentially gives same results at 76 and 108 MHz with ADS)
Shunt impedance at 76 MHz = 78.5 kΩ, Q = 2249
R/Q at 76 MHz = 35 Ω

---
Anode impedance
Zanode at this point
At 76 MHz = Ranode = 624 Ω

---
Voltage along the cavity
In terms of phase
In terms of position

---
Stepup ratio
This is highly dependent on the coupling capacitance that we have chosen. Can be changed later.
Assume stepup is 10 for now.

---
Y567 Grounded Grid Load line
The two points that were chosen are:
Right hand point (Vanode = 11 kV – assuming stepup of 10, 1 kV screen voltage, and Vcathode = 250 V cathode to grid bias)
Left hand point (Vanode = 1.025 kV – screen to grid bias,
I peak = 4 * I0 = 31 A)
I0 = takes into account the inefficiency of class B operation, Vgap = 100 kV and Rshunt = 78.5 kΩ.

---
Fourier components
Idc = 8.8 A, and thus DC input power Vanode = 11 kV => Pdc = 96 kW.
I@76 MHz = 14.2A gives Prf = 71.3 kW
Efficiency = 0.74
The load resistance (which I assume is the anode resistance) = 698 Ω
This number is consistent with the anode resistance calculated earlier = 624 Ω

---
Cathode side of the tube
To get the cathode resonator to resonate between 76 MHz to 106 MHz, the length of this transmission line has been reduced from 22.1 cm to < 3.3 cm.

---
Optimize to make VSWR more symmetric about frequency range
I reduced the length of L03 from 3.3 cm to 1.3 cm and reflections got a lot better across the frequency range. However, it is worse at 76 MHz. Although using gm=0.035, the power reflected is < 10%.
VSWR is now < 2 everywhere and reflected power < 12%.

---
Optimized results

---
Optimized results (cont'd)

---
Summary
- No power reflection calculation because we had a wrong idea about the tube resistance being fixed at 1.4 kΩ.
  - Mismatch of PA to cavity comes from the tube not working completely in class B.
- Power requirements ~96 kW are reasonable for 100 kV gap voltage.
- Modifying cathode resonator does not seem to be too difficult.
  - Essentially one part of the present cathode resonator needs to be reduced in length to nearly zero length.
  - Need to build a test station with 76 – 106 MHz to show that the Y567 tube can supply the required power.