Transition fixes
C.Y. Tan
21 May 2015

---
Fixing transition oscillations
- Recall at transition, there is no bucket and all particles essentially have the same revolution frequency independent of energy and the bunch is the shortest during the ramp.
  - Highest space charge effect.
- The longitudinal quadrupole oscillation arises from the beam from two phenomena
  - No space charge: The beam is very short at transition, in fact, at its shortest. This does not match the subsequent bucket that is formed after transition and thus there is a bunch length oscillations after transition.
  - With space charge: Space charge is “focusing” after transition. This is also known as the “negative mass” effect. (See later slide). Space charge is “defocusing” before transition. After transition, the bunch is over-focused and thus bunch length oscillations occur on top of bucket mis-match.
- Is there a transition problem from space charge????
  - I cannot reproduce YangXi's simulation results. (Chandra also cannot at this time)

---
Recall negative mass
When 2 charges are close together above transition, the early charge gets a positive energy kick and the later charge gets a negative energy kick. Since we are above transition, the early charge gets a longer orbital period and the late charge gets a shorter orbital period. Therefore, they get closer together! Thus “focusing”. Opposite happens below transition. See Edwards & Syphers pg 181.

---
Cures for quadrupole oscillations
- Bhat et al method (focus-free method) for fixing bucket mismatch
  - Flatten the voltage just before and after transition with 3rd harmonic. (We can also do this with 2nd harmonic as well).
    - This requires a phase shift of the RF so that the synchronous particle is in the middle of the voltage plateau.
    - Give all the particles the same energy kick.
  - The beam is “drifts” before and after transition but in the opposite directions because there is no focusing, i.e. beam is like free particles after energy offset is taken out.
- Y. Xi et al method for fixing space charge defocusing/focusing with “over-focusing” before transition
  - Over-focus the beam just before transition to counter the “defocusing” of beam from space charge at transition and this “over-focus” becomes “defocusing” after transition to counter the focusing of the space charge force.
  - Use more volts to get a steeper slope
    - She used 3rd harmonic to add more volts and slope to make it comparable to 45% more volts on fundamental.
    - We will use 2nd harmonic to add more volts and slope. At 100 kV, we can get comparable volts but not slope.
- Essentially, both methods rely on manipulating the focusing of the beam before and after transition.

---
Normal transition
We assume that the distribution is “matched” before transition.
Distribution does not match to the bucket after transition.

---
Comic of “focus free” method

---
How flat can the voltage be with 2nd harmonic at 100 kV
0.6% variation, bunch length is 153 deg.
0.6% variation, bunch length is 15.8 deg.
Note that flat, but could be good enough for very short bunches before transition.

---
Comic of “overfocus” method
Must have enough “slope” to compensate for the ΔE changes from space charge before and after transition.

---
“Overfocusing” method
What I want is increased slope instead of what Yang Xi did where she also increased voltage+slope. So how much more slope at the synchronous phase can I get with the same accelerating voltage of the main RF with the 2nd harmonic added?
Slope of 1.0Vrf at 60 deg phase = 0.5
1.0Vrf with 2nd harmonic slope = 0.76
1.45 Vrf slope @ 36.6 deg phase = 1.16 (to give the same accelerating voltage)
Increase in slope is 52% between 2nd harmonic and fundamental only.
(2nd harmonic + normal RF) is 34% smaller than 1.45 Vrf @ 36.6 deg
Note: in Yang Xi's writeup RF3rd-inj-TC.pdf she uses 28 deg as synchronous phase. I will used 60 deg instead.

---
Comparison with 3rd harmonic
1.0 Vrf + 0.15 V3rd harmonic.
Slope is “close” to 1.45 Vrf slope.
I don't think it is necessary to increase voltage to match 1.45 Vrf.

---
Hybrid Focusing
- Focus free method does not work very well with space charge dominated beam, not clear that at 100 kV we have enough “flat” region”.
- Over-focusing method, probably does not have enough slope at 100 kV.
- Consider combining both methods to see if this works better than using each one alone.
  - Start overfocusing to try to compensate as much as possible the space charge “defocusing” and “focusing” before transition
  - Then flatten RF voltage to allow the distribution to drift to get longer bunch before transition.
  - Wait for bunch to match bucket before turning off flat RF voltage.

---
Conclusion
- Work continues to see whether either of these two methods work.
- Goal is to create a new voltage ramp for our cavity rather than the one right now.
- Dark horse: 3rd harmonic cavity that may be available to us.
  - Note: My initial calculations show that it will not work as is. A new tuner will probably need to be built for this, plus, perhaps lowering the Q of the cavity.