## Slide 1: Magnetic Cogging and Extraction Lock New DDS System
Kiyomi Seiya, Craig Drennan
Workshop on Booster Performance and Enhancements
23 November 2015

## Slide 2: Outline
Cogging
Radial Cogging and Magnetic Cogging
Beam studies
Operation Status
Plan
  Synchronization to the LINAC Notch
  Bucket control during Phase lock
New DDS System
T. Boe
S. Chaurize
D. Dick
C. Drennan
W. Pellico
K. Seiya
T. Sullivan
K. Triplett
A. Waller

## Slide 3: Intensity and beam loss in the Booster cycle(Oct. 2014)
Extraction kicker gap (Notch)
Beam loss/cycle = 0.075 kJ  1125W
(525 W Administrative Limit)
Int. at Injection: 5.0E12 ppp
Int. at Extraction: 4.5E12 ppp
Efficiency: 90%
Energy: 400 MeV – 8GeV
RF freq. : 37.9 – 52.8MHz
RF
Intensity
Beam Energy Loss
Intensity

## Slide 4: Notch and Cogging
Gap
for the extraction kicker
MI/RR revolution
1st Booster batch
2nd Booster batch
Time
h=588
h=84
Notch(extraction kicker gap) – Booster extraction kicker – MI/RR injection kicker
Main Injector / Recycler
81 bunches + 3 empty buckets

## Slide 5: Beam at injection and extraction without Cogging
Notch
Notch
 81 bunches + 3 empty buckets
Adiabatic capture with 37MHz RF
 84 bunches
Time
1 Booster revolution
Injection from LINAC @ 400MeV
1st Booster batch
2nd
Lost 3 bunches
every Booster
extraction.
at extraction
at MI/RR injection
Intensity
Beam loss at extraction
at injection

## Slide 6: Total bucket count during Booster cycle
Booster:
15 Hz resonant circuit
RF frequency: 37.7 – 52.8MHz
Total rf bucket count = const.
Total rf bucket count = const. -- Notch is at same position at extraction

## Slide 7: Revolution frequency control with radial cogging
Path length (radial position) of the beam
@ 700 MeV
Radial position
Intensity
Creates notch at 700MeV.
Moves orbit before/after transition.

## Slide 8: Magnetic Cogging using 48 new dipole corrector magnets
Fixed with RPOS feedback
Changed by dipole corrector
Dipole corrector: 0.009[T-m] @ 24.4[A]
B field error ~1% can be compensated.
(Assuming 10[A] change )
Keeps beam on central orbit and save aperture.
Creates notch anytime after injection( even LINAC notch)
 reduce beam power loss by 40%.

## Slide 9: Field error and integration of difference of rf counts
Simulation
Measurement
B_main dipole field
Booster: 15Hz resonant circuit synchrotron synchronized to the 60Hz power line.
Number of MI/RR revolution

## Slide 10: New Booster VXI board (C.Drennan)
8 x digital inputs
8 x digital outputs
4 x ADC inputs
4 x DAC outputs
2x RF inputs
Replacement for the 15 years old present Booster VXI/DSP board

## Slide 11: Parameters and Plots on console (A. Waller)
Bucket error
32 turns average
32 turns average x Gain curve
4 array data from memory

## Slide 12: Block diagram of Cogging feedback
Integrated diff. bucket count has to be ‘0’ at the end of cycle.
BRF
Bdot
11 msec (MI/RR RF x 588)

## Slide 13: Simulation for the feedback and measurements
Integrated error w/o feedback (simulation)
With feedback (simulation)
With feedback (MEASUREMENTS)

## Slide 14: Orbit changes during Cogging operation
Corrector current
Orbit difference
Corrector current : +/- 1A
Orbit change < 1mm
2A
+/- 10 mm

## Slide 15: Notch at 700MeV to 400MeV
Reduced beam energy loss at the Notch creation by 40 % and the total cycle loss by 15%.

## Slide 16: Sync to the LINAC Notch
LINAC Notch– Booster extraction kicker – MI/RR injection kicker
The logic for the Cogging supposed to be modified.
No more beam energy loss from Notch creation in the Booster.
Laser notching cavity installed on the downstream RFQ flange.
Wall current monitor signal in the LINAC with 6 different optical pulse energies.

## Slide 17: Injection bucket error in Recycler
RR revolution
RR Intensity
Beam loss
@ RR Inj.

## Slide 18: Cogging and Phase Lock
h=588
h=84
Main Injector / Recycler
Main Injector / Recycler RF
Booster RF

## Slide 19: Phase Lock Loop at the end of the cycle
fMI – fBooster < 8kHz
RPOS feedback is turned off
PLL is turned on
when Df = fMI - fBooster = 0
End of the cycle
Df/32
Df
0 deg
90 deg
0 deg
180 deg
8 RF buckets
RPOS
PL reference curve
1msec/div
400msec/div

## Slide 20: PLL curve adjustments
Make communication between Cogging and Phase Lock system
Fix +/- 1 buckets error for the MI/RR injection
Could reduce the gap length from 3 to 2 buckets
4 RF buckets
5 RF buckets
6 RF buckets
PLL ON
Notch
For more info on the MI Phase Lock Controller go to: AD DocDB Beams-doc-4781-v2

## Slide 21: Summary and Plan
Summary
New beam extraction synchronization system called “Magnetic Cogging” was developed at the Fermilab Booster.
The system was successfully implemented to the operation in March 2015.
The gap creation used to be at 700 MeV with the RF Cogging and it was moved to 400MeV with Magnetic Cogging. The Magnetic cogging reduced beam energy loss at the Notch creation by 40 % and the total cycle loss by 15%.
Plan
Synchronize Cogging to LINAC Notch
Fix +/- 1 buckets error for the MI/RR injection

## Slide 22: A New LLRF Frequency Reference for Booster
Craig Drennan
Workshop on Booster Performance and Enhancements
23 November 2015

## Slide 23: Four Channel DDS Booster LLRF Reference
Yes, a better phase lock --- But, it is a complex install.

## Slide 24: Four Channel DDS Booster LLRF Reference
For more info go to Beams-doc-3891-v3 and https://www.youtube.com/watch?v=lAjt-3XEtaM
Benefits
More flexibility in producing the Bias Curve
Possibility for different curves for different Booster cycle types
Replaces difficult to maintain broadband analog RF phase shifters (paraphase, RPOS)
Can produce smoother MI phase lock.
Can provide more reproducible phase manipulations.
The acceleration phase lock and RPOS control loops, and injection, cogging and MI phase lock can have a more integrated control policy (or not).

## Slide 25: Four Channel DDS Booster LLRF Reference
There is a first draft for cabling the module in for testing in the Booster, and staging the implementation of the LLRF control functions.
For more info go to Beams-doc-3891-v3 and https://www.youtube.com/watch?v=lAjt-3XEtaM

## Slide 26: Booster DDS ACNET Controls (Brian Schupbach, Programmer)
DDS parameter read backs and settings available via ACNET MOOC functionality. Parameter page H53<66>
DDS board provides DAC outputs to ACNET MADC. The bias curve is currently available via snapshots.

## Slide 27
VME front-end facilitates TCP connection to Java GUI, B129
Inspect, edit, import, and export Freq, Bias, Para curves etc…