## Slide 1
Vladimir SHILTSEV (Fermilab*, USA)
Hadron Collider Physics Summer School
Fermilab, August 2016
* Operated by Fermi Research Alliance, LLC under Contract No. De-AC02-07CH11359 with the United States Department of Energy
Accelerator Physics and Technology: Lecture 2

## Slide 2: Research Machines: Just the Tip of the Iceberg

## Slide 3: Example: Spallation Neutron Source (Oak Ridge, TN)
A 1 GeV Linac loads 1.5E14 protons into a non-accelerating synchrotron ring.
These are fast extracted onto a Mercury target
This happens at 60 Hz -> 1.4 MW
Neutrons are used for biophysics, materials science, industry, etc…

## Slide 4: Light sources: too many to count
Put circulating electron beam through an “undulator” to create synchrotron radiation (typically X-ray)
Many applications in biophysics, materials science, industry.
New proposed machines will use very short bunches to create coherent light.

## Slide 5: Industrial accelerators
Radioisotope production
Medical treatment
Electron welding
Food sterilization
Catalyzed polymerization
Waste treatment

## Slide 6: Accelerator Technologies (“Show and Tell”)
Impregnated W cathode
RF cavity copper (warm)
RF cavity Nb (cold)
RF tube
Magnet: permanent SmCo
Magnet: superconducting NbTi
Vacuum pipe: FNAL Main Injector, LHC

## Slide 7: Examples of Accelerating RF Structures
Fermilab Drift Tube Linac (200MHz): oscillating field uniform along length
ILC prototype elipical cell “p-cavity” (1.3 GHz): field alternates with each cell
37->53MHz Fermilab Booster cavity
Biased ferrite frequency tuner

## Slide 8: State of the Art SC Magnets: 3 Decades
4.5 K He, NbTi
+ warm iron small He-plant
NbTi cable
cold iron
Al collar
NbTi cable
simple &
cheap
NbTi cable
2K He
two bores
4.5T
8.3T
3.5T
5.3T
1232 bending magnets 15 m long 
NbTi cables, 13 кА@1.9 К 10 GJ

## Slide 9
26 658.883 m
6.5 TeV x 2

## Slide 10: LHC Accelerator Operations
What are they doing there !?

## Slide 11
50 MeV
1.4 GeV
25 GeV
450 GeV
6500 GeV

## Slide 12: Bottom line: Integrated Luminosity
~20 fb-1 delivered to ATLAS & CMS
3 fb-1/very good week
Receipe : a) peak luminosity; b) max availability; c) short turnaround time

## Slide 13: Themes and Topics
“Level 0” Issues: Make machines run
  T1: Fix splices
  T2: Train magnets
  T3: Clean beampipes
“Level 1” Issues: Make them run reliably
  T4: Cryogenics trips, other issues
  T5: UFOs
  T6: Turnaround time, ramp
“Level 2” Issues: Performance (luminosity)
  T7: Proton’s life and death in LHC
  T8: Halo collimation
  T9: Upgrades

## Slide 14: T1: Splices… all began Sept 19 2008
A splice with bad thermal and electrical contact between the superconductor and the copper produced sufficient resistive heating to lead to thermal runaway.
This provoked the melting of the material surro-unding the splice, and subsequently an electric arc developed between two exposed cable ends.
This arc melted through the helium line in which the cable travels, releasing Helium into the insulation vacuum of the interconnect.
The rapid and voluminous expansion of the Helium caused a pressure wave that propagated along the insulation vacuum causing extensive damage

## Slide 15: Sample Joint X-Rays
Sample 3A left (26 mW)
Sample 3A right (43 mW)
Sample 3B (21 mW)
Pictures by J.-M. Dalin
Sample 2B (42 mW)
Sample 1 (61 mW)
Sample 2A right (43 mW)

## Slide 16
A 13kA splice has a resistance of about 300 pΩ, which can be measured with a precision ~20pΩ. The acceptance criteria is 10 nΩ. Any splice does not meet this criteria is replaced/repaired. The resistance acceptance criteria at the Cu - superconducting splice joints was 5 Ω. Any joint does not meet this criteria is replaced or repaired.

## Slide 17: T2: Train All the Magnets: Sep 2015 – April 2015

## Slide 18: T3: Electron Cloud & Need of Scrubbing
Primary sources of electrons in the LHC
  At Injection (450 GeV) gas ionization
  At 7 TeV Synchrotron Radiation
Consequences:
  - instabilities, emittance growth, desorption bad vacuum, beam loss
  - excessive energy deposition in the cold sectors
The critical energy of the photons at
7 TeV ~ 44 eV
72x 2.2E11ppb(25ns)
36x 3.5E11ppb(50ns)
Emax=239.5 eV
T =2.5 m

## Slide 19: What e-cloud can do to the Beam?
~33% Horizontal
~110% Vertical
Associated beam loss
Measured Emittance Growth
Injection Intensity
End of fill Intensity
Fill: 2249 (2011)
25 ns Bunch Spacing
Energy = 450 GeV
Time between Injection to End ~10 min
Dumped by BPM
1020 Bunches
Intensity
Bunch #

## Slide 20: Scrubbing @ 25 ns bunch spacing
So far it is the only cure in the LHC….Takes time to clean the surface and reduce SEY (secondary electron yield) from ~2.2 to ~1.5
Scrubbing “memory” kept while running with 25 ns beams - deconditioning was observed after few weeks of low e-cloud operation

## Slide 21: T4: Cryogenics , Trips
LHC: 8 cryoplants total 35 MW wall plug; 130 tons of LHe to keep 36,000 tons at 1.9K
Efficiency ~250 W wall plug power per Watt at 4.5 K
  CERN cryocapacity of 150 kW @4.5K and 20kW at 1.9K
Three Temperatures:
  50-70 T-shield
  4.6 K Heat Intercept
  4.6-20 K Beam Screen
  1.9K cold mass
Safety factor 1.6 (design)
Reality: ~none (1.1?)

## Slide 23: Cryo: Complex and Large Machinery

## Slide 24: 2015 LHC Machine availability
Statistics for 25 ns run from September 7 to November 3

## Slide 25: Availability: 11th June – 23rd July, 2016
Stable Beams 67%
From 32% to 67%
In one year!

## Slide 26: T5: UFOs
‘Unidentified Falling Objects’

## Slide 27
2016
2015
arc UFOs (cell >11): rates similar to end of 2015
  did not lose conditioning over the Xmas stop
UFOs: there are many of them, they are frequent ! UFO events observed quite often during operation at 6.5 TeV Conditioning is observed on the UFO rate in spite of the increasing number of bunches BLM thresholds being optimize to find a good compromise between availability and quench protection

## Slide 28: A Schematic of LHC Operational Cycle at half nominal energy
The fastest turnaround in 2012 was 2 hours 8 minutes. This was close to the theo- retical minimum for 4 TeV operation. The average for the year was around 5 hours 30 minutes.
Beam dump
Ramp down/precycle
Injection
Ramp
Squeeze
Collide
Stable beams
450 GeV
3.5 TeV
Beam loss during
squeeze
12-SPS batch Injection
T6: Turnaround times, ramps, etc

## Slide 29: T7: Turnaround @ 13 TeV - longer
Additional delays:
• Transfer and injection optimi-zation and general wrestling with the injection process (respecting tight demands on beam quality etc.).
• controls and data acquisition problems; kicker overheating; problems in the injectors; etc.
• access recovery, precycle faults
• Fills lost in the ramp and squeeze to beam induced problems (instabilities) or, feedback system faults

## Slide 30: T7: Proton’s Life in LHC
2100 bunches/beam x ~1.2e11/bunch = 2.5e14 /beam
11,000 revolutions/s x 12 hrs = 0.5 billion turns
  Only ~ 1 billion protons die in collisions per second
Transverse betatron oscillations ~60 times/revolution:
  Also called betatron oscillations
  Rms amplitude = beam size
  200-300 micron in arcs, 13 micron at IPs
  Angular divergence : ~2 microrad in arcs, 30 microrads at IPs
Longitudinal oscillations – slow – 23 Hz:
  Also called synchrotron oscillations
  Particles change positions in the bunch, rms bunch length ~8 cm
  Particle’s energies vary, too – rms 1 GeV (dE/E_rms=1.1e-4)
design 2800

## Slide 31: T7: Proton’s Death in LHC (Luminosity)
The relationship of the beam to the rate of observed physics processes is given by the “Luminosity”
Rate
Cross-section (“physics”)
“Luminosity”
Standard unit for Luminosity is cm-2s-1
Example: total p-p inelastic+elastic cross section at 13 TeV cme is ~110 mbarn (58 inel+ 12 ssd+40 el not seen)
~30 interactions per crossing (NB: pile up is only ~20! ) x
40,000,000 collision/sec= 1.1B protons leave each beam every second
Beam lifetime due to such “Burn up” T=N/(dN/dt)= 2.5e14 protons/(1.1e9/s) =63 hours

## Slide 32: Luminosity lifetime
Take into account two IPs (ATLAS, CMS and 3% LHCb) 1/64+1/64 hrs-1
Take into account beam gas 1/110hrs-1 and that Lumi~N^2  x2
2x(1/64+1/64 + 1/110) hrs-1
=8%/hr (12.5 hrs lifetime)

## Slide 33: Peak luminosity: design 1e34 reached!
1034
(8 yrs after start up, 6 yrs after 1st lumi)
  No of bunches ~2100 due to SPS beam dump
  6.5TeV -8% off design
  25 ns beam - nominal bunches ~1.2e11 p/bunch
LHCb and ALICE: levelled operation at
~3x1032 and ~2x1030 cm-2s-1 respectively
But: Lower emittance from injectors (2.9 vs 3.5 um)
Squeeze harder in ATLAS and CMS
  beta* = 40 cm
  cf. 80 cm in 2015, 55 cm design

## Slide 35
The LHC beam energy is 350 MJ. Already at injection the beam can damage a magnet.
The power of the LHC beams
T8: Halo Collimation
LHC particles are not 100% contained! They diffuse! – need control !

## Slide 36
Superconducting coil:
T = 1.9 K, quench limit ~ 15mJ/cm3
Proton beam: 145 MJ
(design: 362 MJ)
Factor 9.7 x 10 9
Aperture: r = 17/22 mm
LHC “Run 1” 2010-2013: No quench with circulating beam, with stored energies up to 70 times of previous state-of-the-art!

## Slide 37: LHC collimation system
LHC has complex and distributed collimation system of >100 collimators → several stages to protects LHC components as well as detectors
Collimation is designed to provide cleaning efficiencies > 99.99% → need good statistical accuracy at limiting loss locations; → simulate only halo particles that interact with collimators, not the core.

## Slide 38
The LHC collimator
BEAM
1.0m+0.2m tapering

## Slide 39: LHC Collimation System Layout
Two warm cleaning insertions, 3 collimation planes IR3: Momentum cleaning 1 primary (H) 4 secondary (H) 4 shower abs. (H,V) IR7: Betatron cleaning 3 primary (H,V,S) 11 secondary (H,V,S) 5 shower abs. (H,V)
Local cleaning at triplets 8 tertiary (2 per IP)
Passive absorbers for warm magnets
Physics debris absorbers
Transfer lines (13 collimators) Injection and dump protection (10)
Total of 108 collimators (100 movable).
Two jaws (4 motors) per collimator!
Momentum
cleaning
IR3
Betatron
cleaning
IR7

## Slide 40: Super-Effective Halo Cleaning in LHC
2015

## Slide 41: T9: Upgrades
The main objective of HiLumi-LHC Upgrade (2022-2024) is to install new hardware and guarantee beam parameters that will allow the LHC to reach the following targets:
  Prepare machine for operation beyond 2025 and up to 2035-37
  Devise beam parameters and operation scenarios for:
    enabling a total integrated luminosity of 3000 fb-1
    implying an integrated luminosity of 250-300 fb-1 per year,
    design for μ ∼ 140 (∼ 200)
    (peak luminosity of 5 (7) e34 cm-2 s-1)
  Design equipment for ‘ultimate’ performance of 7.5 1034 cm-2 s-1 and 4000 fb-1 => Ten times the luminosity reach of first 10 years of LHC operation

## Slide 42: LHC Luminosity Upgrade : Machine Goals

## Slide 43: HL-LHC Scale: Hardware and Cost
976MCHF (-142 +208)
~2,500 man-years

## Slide 45: Acknowledgements
  Materials and slides used here come from many sources, including the USPAS lectures, Eric Prebys, Mike Lamont, various conferences, workshops, LHC and LARP reviews, etc
  Thanks for Your Attention !
Questions !?

## Slide 46: Backup

## Slide 47: Radio Frequency Accelerating Cavities
SuperConducting
ILC RF Cryomodule
Normal Conducting (“Warm RF”) -
Muon Cooling RF Cell

## Slide 48: Accelerator Technology: Permanent Magnets
Sr-Fe + iron poles
B_max=1.45T
combined function
T-compensation
dB/B~0.01%

## Slide 49: Recycler Ring
E_kin=8 GeV fixed
Shares tunnel with 150 GeV fast cycling Main Injector
C=3.32km
344 Permanent magnets (344, 1.45T, Sr-Fe
combined function)
Stores and cools antiprotons
Build by the US Congressman
Recycler
Main
Injector
Bill Foster
Gerry
Jackson

## Slide 50: Accelerator Elements : Present
Tevatron
SC magnet
LHC SC magnets
VLHC Super- ferric magnet

## Slide 51: Quench : МRI magnet* (~1/30,000 of LHC)
*pulled off the web. We recover our Helium.
№1 how LHC was fixed
№2 LHC vacuum chamber

## Slide 52: Exit Run 1(2010 – 2012)
Foundations well proven at 4 TeV
  Magnets, vacuum, cryogenics, RF, powering, instrumentation, collimation, beam dumps etc.
Huge amount of experience gained
  Operations, optics, collimation…
Healthy respect for machine protection
Main bend power converters: tracking error between sector 12 & 23 in ramp to 1.1 TeV

## Slide 53: 2013 - 2015
13-14
Aug 14-Apr 15
2015
April ‘13 to Sep. ‘14
Dipole training campaign
1st B E A M
5th April
3rd June
First Stable Beams
10th April Beam at 6.5 TeV
28th October Physics with record number of bunches
Peak luminosity 5 x 1033 cm-2s-1
Struggle
IONS

## Slide 54
2015: re-commissioning year, relaxed parameters, some issues…
UFOs
8 UFO dumps within 2 weeks (Sep 20 to Oct 5)
Conditioning observed
Radiation to electronics
Mitigation measures (shielding, relocation…)
Non-rad hard components used in LS1 upgrade
Electron cloud
Anticipated
Significant head load to cryogenics

## Slide 55
Overcome a few problems
WEASEL
PS MAIN POWER SUPPLY
SPS BEAM DUMP
Limited to 96 bunches per injection
2076 bunches per beam cf. 2750

## Slide 56: Then enjoy some remarkable availability
6 weeks
Heartbeat
Things that can go wrong

## Slide 57: Stored energy per beam
Beam 1
2.2 mm gap
B1 collimators IP7

## Slide 58: Beam from injectors
Standard 25 ns scheme
PS circumference
BCMS (Batch Compression, Merging & Splitting)
Lower intensity, smaller bunches from PSB
Lower than nominal emittance taken a step further

## Slide 59: Dipole training 2/2
Campaign summary
All magnets have been trained to well over 7 TeV in SM18 before installation
Extensive re-training in situ was not expected
Training: frictional energy released during conductor motion