## Slide 1: Particle Accelerators at the Intensity and Energy Frontiers for High Energy Physics Research
Dr. Chandra Bhat
Fermi National Accelerator Laboratory, Illinois, USA
Jnana Bharathi, Bangalore University, India
November 30, 2016
Joint sponsors:
KAAS + IPS(BC) and Dept. of Physics, Bangalore University
Outline
Modern Accelerators – An introduction
Intensity Frontier Accelerators
Energy Frontier Accelerators

## Slide 2: Why we do need High Intensity & High Energy Particle Accelerators?
Curiosity Driven Fundamental Science Research
If Target is Hydrogen then available
Center of Mass Energy=
In pp collider, available
Center of Mass Energy=
At =100 GeV available Energy  14.1GeV
At =100 GeV available Energy =200 GeV
Target
Energy Frontier Colliders:
Intensity Frontier
Fixed Target Experiments:

## Slide 3: The Types of Accelerators for High Energy Physics Research
Linear Accelerators
Circular Accelerators
Combo
Most of the modern High Energy Physics Accelerators belong to the last category

## Slide 4: Concepts of Linear Accelerators
Two Conducting Parallel Plates
A Charged particle Gains an additional Energy of 1.5 eV
This is the Principle of Electro-Static Accelerators
Used for Nuclear
Physics Research
Examples: Cockcroft-Walton Accelerator,
Van de Graff (of BARC, Bombay)
Pelletron (IUAC(Delhi) and TIFR )
Van de Graaff
Cockcroft-Walton
4Vpeak

## Slide 5: Concepts of Linear Accelerators
RF Cavity
RF Source of
Appropriate Frequency
+V
-V

## Slide 6: Concepts of Linear Accelerators
+V
-V
RF Cavity
RF Source
Drift Tube
Superconducting Niobium RF Cavity
This idea led to
Alvarez Drift Tube LINAC
Beam

## Slide 7: Examples of Linear Accelerators
SLAC(length=3.2km)
50 GeV ee+ collider
DESY 1.5 GeV
Free-electron Laser
SNS: Front-end of 1 GeV LINAC

## Slide 8: Concepts Circular Accelerators
Cyclotron (1929)
N
S
Ds
Charged Particles
Side View
RF
RF
Viewed from the Top
E. Lawrence
Vacuum
(~1Torr
Examples: Cyclotron, Panjab University
VECC in Kolkota & 14 Others for
Medical Applications, in India

## Slide 9: Beyond Cyclotrons
As the speed of the particles approach speed of light the path length will not change in proportion to the gain in momentum. So, the conventional cyclotrons have limited scope for higher energy. Maximum energy one can achieve is about 30 MeV/nucleon
Sector Focused Cyclotrons
World’s Highest Energy Cyclotron at TRIUMF operates at 520 MeV

## Slide 10: Synchrotrons, Circular Accelerators for Relativistic Particles
Focusing &
Defocusing
Quadrupoles
Beam Injection Line
Beam
Extraction Line
Vacuum
Beam-pipe
F O D O
Cell
Beam
Envelope
Dipoles
RF
Source
RF
Cavity
Principle of Synchrotrons:
RF Phase Focusing
Examples: 2.5 GeV Synch Light
Source, RRCAT,
Indore

## Slide 11: Importance of RF system in Synchrotrons
Coasting Beam with Energy E0±E
Beam Pipe &
the Beam
RF Bucket
Boundary
Beam
Vrf

t
A contour of
constant Hamiltonian
Synchronous Particle
Phase-space Area of a Bunch is
Longitudinal Emittance
Measured in eVs
Closed Orbit
Beam
Storage Ring
RF Cavity


Bunched Beam
AC
rf= hrev
harmonic number h=1
Vrf
t
Sinusoidal
Vrf
t
Sinusoidal
AC
rf= hrev
harmonic number h=2
RF Buckets
Vrf
E
WCM Data
Beam Acceleration
Vrf
t
Sinusoidal
AC
rf= hrev
harmonic number h=2
Accelerating RF Buckets
and
Accelerating Beam Bunches
E
Accel. /turn=EAcc=V0sin 
WCM Data
t
RF
Buckets
E
WCM Data
Vrf
t
Sinusoidal
AC
rf= hrev
harmonic number h=2
Bunch Compression
E
WCM Data
Buckets of higher harmonic RF system

## Slide 12: What Else are Needed? Beam Diagnostics are key Tools

## Slide 13: An example of 3GeV RCS JPARC (Japan)
Material & Life
Science
Experimental
Facility
Main Ring
H from LINAC

## Slide 14: Intensity Frontier LaBs

## Slide 15: Fermilab, World’s Intensity Frontier Lab
Aerial
view of Fermilab
Site
MicroBooNE
NuMI:
MINOS+
MINERvA
NOvA
Muon:
g-2
Mu2e
MIPP
Test Beam
SeaQuest
M-Center
LBNF
Tevatron
Accelerators
are 4m-8m deep
underground!
Recycler
&
Main Injector
Booster
LINAC
Debuncher/
(Muon-ring)
Booster:
0.4-8 GeV Accelerator
Main Injector:
8 -120 GeV Accelerator
Recycler
Debuncher/
Muon-Ring

## Slide 16: Protons Start from a Hydrogen Bottle
This idea led to

## Slide 17: Radio-Frequency Quadrupoles (RFQ)
Fermilab pre-accelerator Region
Drift-tube LINAC
It is a very interesting device invented by
I.M. Kapchinsky and V.A. Tepliakov in 1970.
Schematic of RFQ
RFQ at Fermilab

## Slide 18: Drift-Tube LINAC 750KeV to 116 MeV
TM010
Alvarez Drift Tube LINAC
RF
Source
Beam
Inside this tank

## Slide 19: Side-Coupled Linear Accelerator for 116 MeV to 400 MeV
Each one of cavities are hand-tuned
Coupling
Cells
Schematic of Side Coupled RF structure

## Slide 20: Fermilab Booster 15Hz RCS Synchrotron
Built as an injector to the Fermilab Main Ring with 1-2E12p/cycle
R = 75 meters
Cycle Time = 1/15 sec
96 Combined Function Dipoles
Bend Magnets/cell = 4
Cell type: FOFDOOD (DOODFOF)
Harmonic number h=84
Transverse Tune X= Y 6.7
400 MeV
H- Injection
with 200 MHz
RF structure
8 GeV Extraction 53MHz RF structure
Two of 20 RF Cavities
Frequency Swing: 37 MHz-53 MHz
Two of 96 Dipole
magnets
Dampers to control Beam
Beam Diagnostic Device- IPM

## Slide 21: 8 GeV Recycler (Beam Stacker) 8-120GeV (150 GeV) Main Injector
Aerial view of the Main Injector
Main Injector Ring
Circumference=3300 m
Beam Delivery Rate =1pulse/1.3sec
Number of p/pulse=4.7E13@120GeV
Harmonic Number= 588
# of Dipoles=507 (L=240”-120”)
# of Quadrupoles=266 (L=116-17”)
# of Sextupoles= 108 (L=18”)
Transverse Tune X26.425 Y 25.415
Beam Power Target=700kW
Recycler Ring
 LBNF (Future)
Micro-BooNe
NuMI
g-2 & Mu2e
Switch Yard
Beam Abort
NuMI Beam line
20 Accelerating MI-RFs
RR RF Cavities for g-2
RR-collimator
MI/RR Tunnel
Quad
Dipoles
Sextupole

## Slide 22: PIP-II, MW Beam Power
IS
LEBT
RFQ
MEBT
=0.11
=0.22
=0.51
=0.61
=0.9
Room Temp.
Superconducting
162.5MHz, 0.3-11MeV
325MHz, 11-117MeV
650MHz, 117-800MeV
US & India
Collaboration

## Slide 23: Status of Intensity Frontier HEP Accelerators
Fermilab (US):
  Design Goal without PIP: 700kW beam power on target
  Current Status: Demonstrated 700 kW on Neutrino production target (possibly we may go up by ~30%)
  PIP-II: We are in the design stage of PIP-II, which will provide MW type of beam to the -Targets and many fixed target precision measurement experiments.

## Slide 24
FAST/IOTA
PXIE
R&D to Increase Beam Intensity
New Synchrotron Concept (FNAL)
1st Cryomodule tests complete
Photo-Cathode
Booster Cavity

## Slide 25: J-PARC Accelerator Facility
Michikazu Kinsho Nov. 2015
Built using more recent Accelerator Technology
3GeV Synch: 1010kW
50GeV (30GeV) Synch: Beam on -target 420kW

## Slide 26: Energy Frontier LaB

## Slide 27
Fermilab Tevatron
was Energy Frontier
Accelerator from
1985-2011
CERN World’s
Energy Frontier Lab
Lake Geneva
Jura Mountain
World’s
Energy Frontier Lab
P4: 400MHz
RF system
RF: 200 &
800MHz
RF: 2.8-10, 20, 40,
80 and 160MHz
ALICE
LHC-B
ATLAS(IP1)
CMS (IP5)
Crossing in
H-plane
Crossing in
V-plane
France
Switzerland
SPS
LHC Ring
PS
These Accelerators
are 5m-175m deep
underground!

## Slide 28
CERN Accelerators
28
LHC (Lum. upgrade) I worked on these
SPS (single bn. Instability) accelerators
PS (bn. Int. & e-cloud) during my sabbatical
at CERN
from 2010-2013
50 MeV
26 GeV
450 GeV
450 GeV
450-7000 GeV
LHC 7 TeV
SPS 450 GeV
PS 26 GeV
PSB 1.4 GeV
LINAC-2 50 MeV
1 bn/ring, 4bn
36,48,72 bpc
288 bpc
2808 bpc

## Slide 29: LHC PP/Heavy Ion collider (Schematic) Two beams
12
45
34
81
78
56
67
23
LHC SC Quad
LHC SC Dipoles magnets (1232)

## Slide 30: The Large Hadron Collider
A scientific & technological marvel!
~ 27 km circumference
>10,000 Magnets
Largest cryogenic system in the world
SC Magnets cooled by superfluid helium to 1.9oK (523oF below RT)
Total beam power at 7TeV: 362MJ/beam

## Slide 31: LHC from 2008-10 – Bright Startup
2008: Accelerator complete. Ring cold and under vacuum.
Sept. 10th 2008 by 14:59 hr
  First beam around the ring
Some times things will not go smoothly
Sept. 19th 2008 around noon: A DISASTER STRUCK while attempting 3-4 to 5.5TeV
2008–2009: 14 months of major repairs
LHC back on track by early 2010
However, uncertainties existed about the splice quality through out the 2010-2013 runs
  Because of this Risk
Decision: Limit the beam energy =4 TeV
  “This is HISTORY & we learned a lot”
SC splices at the joints
Complex connections
between two dipoles
Public display of the
Dipole magnet
~4km of the LHC Ring was badly damaged
2012: Discovery of Higgs Boson

## Slide 32: Current Status and HL-LHC
From 2013-2014 major repair to fix the problems
Since 2015, LHC is running at CM energy of 13TeV
Goal for HL-LHC(2018 and beyond): total =3000fb-1
  Lots of effort is going on; New high field magnets are being built
  Crab-cavity- a special types of RF cavities to use at interaction points are being built.
  Many more.
Goal: By the End of 2017
provide total =100-200fb-1
Instantaneous Luminosity
in units of (/cm2/sec)

## Slide 33
LHC (and HL-LHC) Schedule
Run 1
Run 2
Run 3
Run 4
7-8 TeV
13-14 TeV
<PU>≅ 21
<PU>≅ 40
<PU>≅ 60
<PU>≅ 140
25ns
bunch spacing
HL-LHC
Run 2: pp @ 13 TeV, 25 ns bunch spacing
Peak Luminosity goal ~ 1.3 x 1034 cm-2s-1
Integrated Luminosity goal ~100 -120 fb-1
Run 2+3: 300 fb-1
2015 Goal: ~10 fb-1

## Slide 34: Issues and Operational Complexity in High Energy Accelerators
Transition crossing in synchrotrons
When a beam propagates in an accelerator, it interacts with both the external fields and the self-generated electromagnetic fields which induce Beam Instabilities
  Space Charge Effect  Self Induced fields
  Microwave instability: transverse and longitudinal microwave instability
  Single bunch instability, multi-bunch instability
Beamloading  RF cavity impedances
Coherent Synchrotron Radiation (CSR) instability
Electron Cloud effects
So on …
Wake field
Initial Dist.
Final Dist.
Longitudinal Profiles
Quadrupole mode
Stable Unstable

## Slide 35: Buildup of Electron Cloud at the LHC & consequences
Primary Source of electrons in the LHC
  At Injection (450 MeV) gas ionization
  At 7 TeV Synchrotron Radiation
Possible consequences:
  - instabilities, emittance growth, desorption bad vacuum
  - excessive energy deposition in the cold sectors
The critical energy of the photons at
7 TeV ~ 44 eV
Evolution of e-cloud
e-cloud induced
beam instability
Mitigation:
Scrubbing,
2) Coating with low SEM materials,
3) Shape inner surface of beam pipe

## Slide 36: CERN, Then and Now

## Slide 37
I should not give up
How wonderful will
it be to go to A

## Slide 38: Dream Machine: International Linear Collider
ILC or International Linear Collider is an e+e- linear collider with the following main parameters
  Center of mass energy ~500 GeV
  Luminosity >1034 cm-2s-1
No synchrotron radiation, but long tunnel to accelerate to ~250 GeV/beam
  Excellent Higgs factory with many Higgs production and decay channels accessible

## Slide 39: Dream Machines: VLHC/VLEP, 100TeV collider
Pushpa Bhat
http://arxiv.org/pdf/1306.2369v1.pdf
SC Magnet Research is going on at Fermilab/CERN
SCRF Research is going on at Fermilab, CERN and elsewhere

## Slide 40: Dream Machine: FCC, 100TeV collider
80-100 km tunnel infrastructure in Geneva area
design driven by pp-collider requirements
with possibility of e+-e- (TLEP) and p-e (VLHeC)
CERN-hosted study performed in international collaboration
15 T  100 TeV in 100 km
20 T  100 TeV in 80 km
Frank Zimmermann

## Slide 41: Dream Machines: Muon Factory and Muon Collider
High
Intensity
Proton
Accelerator
High
Intensity
Proton
Accelerator

## Slide 42: Dream Big!
If you can dream it you can do it
–Walt Disney

## Slide 43: Backup Slides

## Slide 44: Muon-Collider

## Slide 45: (Future) Long Baseline Neutrino Facility
The next MegaScience International project at Fermilab
40 kT LAr detector at Sanford Lab, Multi-MW beam from Fermilab

## Slide 46: Luminosity Formula for a Collider
Beam Revolution Frequency
# of Bunches/beam
Transverse Beam sizes
For Beam-1 & Beam-2
* @ interaction point
(Lattice parameter)
Beam Transverse
Emittance
Instantaneous Luminosity
# of protons/bunch
for Beam-1 & Beam-2
Relativistic Factor
Correction term

## Slide 47: Luminosity
Luminosity relates the cross-section p and event rate
  For Fixed Target case depends on
    Flux of Incident beam
    # of target nuclei/unit area
L
L
Time variable
Kinematic factor
  In the case of the Collider
    the target is also moving. Assuming bunched beam, the L per bunch crossing is,
v1=1c
v2=2c
N1 and N2  number of particles /bunch
Lfix-Tgt=  T l 
x
s
y
Goal of the Accelerator is to maximize the Event Rate

## Slide 48: Collider Luminosity
Assume
  Head-on collision with magnitudes of velocities |v1|=|v2|
  Densities in all coordinates are uncorrelated:
    (x,y,s,s0)= x(x)*y (y)* s(s±s0) ; x Horizontal, y Vertical
  Density distribution function is Gaussian in each coordinate
  Transverse size: 1x 2x and 1y 2y, but bunch length 1s= 2s
  Then
; *x,y : Lattice beta-functions at interaction points &
x,y : Transverse Emittance of the beam
 2x,y =x,y *x,y
As the # of bunches increase the cross talk between in-coming and out-going bunches (beam-beam interactions) becomes an issue.
Solution: Crossing angle

## Slide 49: Collider Luminosity with Crossing Angle & other corrections; the case of LHC
Beam 2
Beam 1
= C
Instantaneous Luminosity with other Corrections:
For the LHC
(nb)Max= 2808 @25 ns bunch spacing,
N1=N2=1.15E11ppb, fo= 11.24kHz, *x= *y=0.55m,
c=285r, *x= *y=16.6m, s=7.5cm
W  Beam offset
S  Crossing angle
 Crossing angle and beam offset
H  Hour-glass factor from bunch length
LHead-on =1.2x1034cm-2s-1
LS =1.01x1034cm-2s-1
LS&H =1.00x1034cm-2s-1
Luminosity per Crossing
If N=N1=N2 L  N2 and linearly with nb .
L also depends on beam filling pattern
x