## Slide 1: Y567B PA test at 76 MHz
Robyn madrak
Booster 2nd Harmonic Cavity Meeting
19 Jan 2017

## Slide 2: PA test at 76 MHz
Previously, had tested PA at ~71.9 MHz (anode resonator frequency)
To test at 76 MHz, added a ring to increase the frequency, and a modified jumper for the 50 ohm load connection, in order to get the optimal impedance

## Slide 3: Original and Modified
ring
Position is adjustable, but not enough with ring to
get optimal impedance with straight tap, so tap has to loop around
tetrode
shroud
Blocking
Capacitor
(fruitbowl)
Anode
Resonator
Center conductor

## Slide 4: Procedure
As was done last time, several data points were taken at varying DC anode voltages
The drive power from the Tomco (new this time) was set to that which produced 300 mA screen current
The duty cycle was 50% which ~40 ms wide pulses
Measured quantities: Anode DC voltage and current, output (load) power, dissipated anode power, cathode and anode response, forward and reflected drive power, reflected drive power at cathode

## Slide 5: Output power and anode power
Chart: DC anode V (kV)
| 12 | 15 | 18 | 21
Pload, calorimetry | 43.7094 | 69.6367 | 103.1435 | 137.9654
Panode, calorimetry | 16.866 | 27.2185 | 41.4541 | 58.4229
Efficiency (right axis) | 0.72157 | 0.71898 | 0.71331 | 0.70251

## Slide 6: Drive power
Chart: anode V (kV)
| 12 | 15 | 18 | 21
Forward drive power | 1.6485 | 2.114 | 2.7296 | 3.3504
Fraction reflected - RIGHT AXIS | 0.061136 | 0.077321 | 0.11074 | 0.13437
Reflected power is low since drive and cathode resonator are well matched at 76 MHz

## Slide 7: Plans
A new cathode resonator has been designed which should be a better compromise for matching at both 76 and 106 MHz
  Matt will start working on getting this made
  We will want to test this (high power) at 76 and 106 MHz since the loading (and impedance) is different when the tube is on
The 106 MHz anode resonator is being fabricated
  As of last week it was in the shop.
  Next: welding
  Back to shop
  Out for plating
  Matt’s best guess: on the order of two months