## Slide 1: PEEK cooling tubes. Shroud with fingers.
2nd Harmonic cavity meeting
February 2, 2017
Gennady Romanov

## Slide 2: Kevin: PEEK Proposal
PEEK water tubes

## Slide 3: CST model of the tubes
Distilled water: ε=78.4, µ=1, tan δ = 0.005 (for 100 MHz and 25ºC).
PEEK material: ε=3.3, µ=1, tanδ = 0.003

## Slide 4: Fields
The electric field is very weak in the tube location.
The field component parallel to the tube dominates, so field enhancement on the ceramic and water boundaries is minimal
 |  | Thermal losses for V=100 kV and t = 3 ms, W |  |  |  | 
 | f, MHz | Copper | Alumina | Garnet | PEEK | Water
No tubes | 103.92 | 945 | 58 | 4369 | 0 | 0
Tubes | 103.92 | 945 | 60 | 4367 | 0.003 | 0.006
NB For garnet it was tan δ =0.001 instead of 0.000206
PEEK tubes look acceptable.
Loss tangent of distilled water must be confirmed.

## Slide 5: Kevin: New shroud shape to place finger contacts
Yellow – current CST shape
Proposed shape
Current CST shape
Chart: μ uniform
| 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4
Eigenmode, current shroud | 112.7903 | 106.9378 | 101.387 | 96.3 | 91.8056 | 87.7713 | 84.1713 | 80.9465 | 78.0438 | 75.4176 | 73.0294 | 70.8473 | 68.8443
Eigenmode, new shroud | 105.9332 | 104.0431 | 101.2331 | 98.7164 | 95.0769 | 88.7405 | 81.9674 | 75.8577
Tuning range is slightly smaller. Other parameters are not checked yet, but expected to be OK.
Concern: possible pressure on the ceramic window.