Booster Lattice Measurements
C.Y. Tan & K. Seiya
22 Mar 2017

---
Goals for the past two weeks
- Measure chromaticity for HEP lattice and pseudo-flat lattice.
- Measure dispersion.
- Perform a tune scan.
- Do a LOCO measurement.

---
Tune scan (08 Mar 2017)
Beam efficiency for both HEP and pseudo-flat lattice < 90% which is not very good. We may need to revisit this.
Although clearly, HEP lattice has very strong 1/2 integer horizontal resonance while for pseudo-flat, it is much weaker.
Vertical 1/2 integer looks a little stronger in pseudo flat lattice.
HEP
Pseudo flat

---
Pseudo lattice dispersion
RPOS
Bad BPMs
Note: I cannot measure absolute dispersion. Rescaled w.r.t. MADX Dx at rpos. However, I don’t know the exact calibration of rpos. Therefore, these plots can be different by a scale factor.
If I set this scale factor = 1, I have a displaced mean error at -0.07 m and standard deviation of the relative error 0.12 after removing 2 obvious outliers.
Dispersion relative error w.r.t. model about 10% w.r.t. model (perhaps).

---
β functions
Combined spread in relative error between model and measurement is 14% for βx and 9% for βy.
Note β relative errors dominated by low β’s.

---
Chromaticity
HEP
Flat
Beam intensity: 0.75e12 (3 turns in Booster)
Measured chromaticity @ 3.1 ms
HEP: Cx = -21.0, Cy = -4.8
Pseudo flat: Cx = -19.7, Cy=-4.4
Not much difference between the two lattices in terms of chromaticities.
Measured tune @ 3.1 ms
HEP: Qx = 0.748, Qy = 0.861
Pseudo flat: Qx = 0.753, Qy=0.862

---
Orbit Response
- Orbit response matches model very well if I have rpos between 0 to 0.5 its expected effect. (Weird).
  - Rpos effect set to zero
  - Rpos effect set to 1.0
- This effect was not seen in previous studies, e.g. 22 Nov 2016.
  - Beam intensity was higher ~ 1.2e12 compared to 0.75e12 on 13 Mar 2017.
  - This effect is being investigated.