## Slide 1: Booster Vrf by fsy Measurements at Extraction Energy (8 GeV) (data of 20170228-0318)
Chandra Bhat and Nathan Eddy
20170328
Goal:
Measure Vrf by the measuring the small angle synchrotron frequency, fsy of the beam in rf bucket at extraction.
or
frev = Revolution frequency of the beam
    = 0.994, Relativistic velocity
Es = 8.938 GeV (kE=400MeV)
= 0.223
h = 84, Harmonic number
fsy = Measured synchrotron frequency
Synchrotron Oscillations
±600
600

## Slide 2: Measurement Technique -1 ($1C)
Settings:
  Turn off the bunch rotation (B:BRRMP) for beam to Recycler ($1C).
  Turn off Acceleration feedback 3 ms of the cycle (standard procedure).
  f(RF) held constant for last 3ms of the cycle (standard procedure)
  Load RF voltage curve with constant B:APGT for at least 3 msec before the beam extraction.
Inject ~1E12ppBc on the beam to and accelerate the beam to the extraction energy.
Give a longitudinal kick (phase kick) to the beam at about 2.5 ms before beam extraction by turning OFF mode 50 and turning ON Nathan’s Vernier rf cavity.
Collect the WCM data for at least 3-synchrotron oscillations before the end of the cycle.
Notice that the rf frequency is changing during this last 3 ms, because it is locked to the RR.
B:APG
B:RFSUM
Constant
RF Voltage

## Slide 3: Damper Configuration Set Up (Nathan Eddy)

## Slide 4: Mountain Range
Time (nsec)
Turn Number

## Slide 5: Mountain Range Data for the last 1.6 ms
1.6ms
18.9nsec
18.9nsec
APG held at 4.74 V
APG held at 9.76 V
The position of the bunch centroid has two components
1. Oscillation of the bunch about the bucket centroid (fsy)
2. In absence of radial feedback bunch moves in accordance with B-field

## Slide 6: fsy from Fit to the Peak Position
F)+
1.6ms
1.6ms
18.9nsec
APGT=4.74
APGT=9.76
Back Ground (changing magnetic field)
Synchrotron Oscillations

## Slide 7: Measurement Technique -2 ($17) (20170318)
Settings:
  Turn off the bunch rotation (B:BRRMP) in the Booster on the study cycle ($17).
  B:RAGT =0 for the last 3 ms of the beam cycle
  f(RF) held constant for last 3ms of the cycle
  Load RF voltage curve with constant B:APGT for at least 3 msec before the beam extraction.
Inject ~1E12ppBc on the beam to and accelerate the beam and extract.
Give a longitudinal kick (phase kick) to the beam at about 2.5 ms before beam extraction by “turning OFF mode 50 and turning ON Nathan’s Vernier rf cavity” or “turning off mode-1 damper”.
Collect the WCM data for at least 3 synchrotron oscillations.
B:APG
B:RFSUM
Constant
RF Voltage
B:RPOS
R:RAG=0
for the last 3ms
1035kV

## Slide 8: Mountain Range Data for the last 1.6 ms
1.6ms
18.9nsec
18.9nsec
APG held at 6.38 V
APG held at 9.50 V
The position of the bunch centroid has two components
1. Oscillation of the bunch about the bucket centroid (fsy)
2. In absence of radial feedback and at fixed frequency bunch
moves in accordance with B-field

## Slide 9: fsy from Fit to the Peak Position
F)+
1.24ms
1.24ms
18.9nsec
APGT=6.38
APGT=9.50
Back Ground (changing magnetic field)
Synchrotron Oscillations

## Slide 10: Vrf from fsy at 8 GeV in the Booster
Vrf(kV)=0.87B:RFSUM

## Slide 11: B:RFSUM –SNP data
Offset in
B:RFSUM ??

## Slide 12: Vrf from fsy at 8 GeV in the Booster
Vrf(kV)=0.932B:RFSUM

## Slide 13: Error in the Measured Vrf(fsy) and Conclusions
300
±2%
fsy(Total Error)=
±2% (Systematic)
±.5% (Statistical)Ave
For example, with 20 RF cavities
B:RFSUM=1035kV
VRF(fsy) = 900 kV+40 kV (+ve error only)
(900/1036)  0.93
We have lower Vrf by about 13%
Conclusions:
We find that the Vrf seen by the beam is about 7% smaller than B:RFSUM. This needs to be taken into account in future efforts.

## Slide 14: Measured APG and B:RFSUM
B:APG
B:RFSUM