## Slide 1: European XFEL
Alignment Work and Geodetic Control Network Adjustment
Markus Schlösser
Fermilab, June 16th, 2017

## Slide 2: European XFEL, Aerial View
Facts and Figures
  Total length 3.4 kilometers, tunnel length ~ 6 kilometers
  Depth of tunnels is between 6 – 38 meters
  Injector is located on the DESY grounds (Hamburg), as well as the cryogenic facilities
  Main Linac Tunnel ~ 2km in urban area
  Experimental area is located in Schenefeld (Schleswig-Holstein)

## Slide 3: European XFEL
Facts and Figures
  11 participating countries (DK, FR, DE, HU, IT, PL, RU, SK, ES, SE, CH)
  Construction cost 1.22 billion Euro (Germany 58%, Russia 27%, others 1 – 3%), mainly as “in-kind”-contributions
  Start of civil construction: 2009
  Start of commissioning: 2016
  First User operation: 2017
  Superconducting accelerator, 101 accelerator modules
  Energy: 17.5 billion electron volts
  Repetition rate: 27000 flashes per second
  0.05 nm < l < 4.7 nm
  Pulse length < 100 femtoseconds
  Brilliance: peak 5·1033, average 1.6·1022 (g/s/mm2/mrad2/0.1% bandwith)

## Slide 4: Alignment work
Fiducialization
  Planning of monument placement on the components
  Definition of component center and axis orientation together with owner
    Mirror center point for MC
    Center of mechanical gap for QP
    Magnetic axis for HQ QP
    Flange axis for VP
    etc….
  Creation of coordinate system (origin is located in component center)
  Measurement of all fiducials in this coordinate system
  Two (independent) sets of measurements to improve reliability (NOT accuracy)
  Averaging data (with check for consistency of measurements)

## Slide 5: Fiducialization
Information about the inner geometry of a component is transferred to outside monuments that are accessible after installation
  By laser tracker measurement
  By photogrammetry
Axis measurement of undulator with touch probe or hall probe
Photogrammetric measurement of quadrupole and cryo module

## Slide 6: Fiducialization
approx. 2000 components for XFEL so far (still growing)
  101 cryo modules
  93 undulators
  ~ 600 warm magnets
  ~ 275 corrector magnets
  ~ 250 ion pumps
  mirror chambers / attenuators / beam shutters …
Most of them have been fiducialized by the DESY alignment group
Some are not fiducialized, because the accuracy requirement is low. Instead the relevant data has been extracted from construction drawings  this slows down the alignment process!

## Slide 7: Alignment work
Stake out
  Preparing nominal coordinates for every component support (boreholes)
  Stake out points
  Measure points staked out before (for documentation)
Coarse alignment
  Preparing nominal coordinates for every component
  Alignment to an accuracy of better than 1mm (required for beam pipe installation)
  Measurement of aligned components (for documentation)
Fine alignment
  Nominal coordinates are already available (same as for coarse alignment)
  Alignment to an accuracy of 0.5 – 0.2mm (depending on component type)
  Measurement of aligned components (for documentation)

## Slide 8: Stake out
Lattice file from physicists contains position (x,y,z) and orientation (q,j,c) for each component  this is imported into the alignment database
Together with relative coordinates for boreholes from construction drawings (treated as “fiducialization data” here) this gives the nominal stake out coordinates for all boreholes, data is combined directly in the database
SA3 | U68.2840.SA3 | UNDU | UNDULATO | U68 | 4.896000 | 0.000000 | 2817.309742 | 235.604721 | -5.650145 | -2.747355 | 2840.111170 | -0.000365 | 0.023007 | -0.000008
SA3 | CBX.2842.SA3 | MAGNET | HKIC | CBX | 0.025000 | 0.000000 | 2819.868942 | 238.163921 | -5.709019 | -2.748289 | 2842.669692 | -0.000365 | 0.023007 | -0.000008
SA3 | CBY.2842.SA3 | MAGNET | VKIC | CBY | 0.025000 | 0.000000 | 2819.893942 | 238.188921 | -5.709594 | -2.748298 | 2842.694686 | -0.000365 | 0.023007 | -0.000008
SA3 | ABSP.2842.SA3 | VACUUM | ABSORBER | ABSP | 0.050000 | 0.000000 | 2819.981442 | 238.276421 | -5.711607 | -2.748330 | 2842.782163 | -0.000365 | 0.023007 | -0.000008
SECTION | NAME1 | GROUP | CLASS | TYPE | LENGTH | TILT | S | ST | X | Y | Z | THETA | PHI | CHI
Components of same type often have the same type of support, therefore this is an efficient way to produce the coordinate for stake out
Q(x,y,z)
(dx,dy,dz)
Q(q,j,c)

## Slide 9: Coarse / Fine alignment
Data is (almost) produced automatically
  Lattice was already inserted into DB during stake out
  Fiducialization data is already present in DB
  Only information about individual magnets and their installation positions has to be supplied
No major difference between coarse and fine alignment from organizational point of view

## Slide 10: Alignment work
Geodetic Tunnel Network
  Planning
  Installation and measurement
  Network analysis and adjustment
SLRS (Straight Line Reference System)
  Installation
  Measurement
  Analysis (not fully automated yet)
  Integration in Tunnel Reference Network (not automated at all yet)
  New network analysis and adjustment

## Slide 11: Alignment work

## Slide 12: Alignment work

## Slide 13: Alignment work

## Slide 14: Geodetic Tunnel Reference Network - Layout
Tunnel reference network is based on “rings” of laser tracker targets, installed every ~10m in the tunnel.
rail for laser tracker car
Targets

## Slide 15: Geodetic Tunnel Reference Network - Measurement
Accelerator
  Accelerator
~10m
laser tracker instrument
observations
XFEL tunnel network
  11400 monuments in total (1700 LINAC, 4200 Photon tunnels, injector, shafts, ExpHall)
  ~210000 Observations (70000 Azimuths, Zenith Angles and Distances, plus some height differences from Levelling)
  PANDA would be able to adjust a network of this size, but …
  the network was never measured in one go, because of external constraints
    Installation was started, before all tunnels were built
    workload is too high to measure all tunnels again in a short time span
    LINAC tunnel and some photon tunnels are now closed due to commissioning / running accelerator

## Slide 16: Sequence of tunnel measurements
Different epochs have to be integrated into one homogenous network
After a year tunnels have deformed near the shafts, so the network can not be considered undisturbed in these areas
We don’t want to change coordinates in areas where the machine installation already started!
2012
2012
2013
2013
2013
2013
2013
2013
2013
2013
2014
2014
2013
2014
2014
2014
2014
2014
2014

## Slide 17: Adjustment of different tunnels / different epochs
XTL measured and adjusted in 2012
  Free network adjustment of laser tracker data, elimination of gross errors, adopt accuracy (when needed)
  Free network adjustment of levelling data, elimination of gross errors (if any)
  Combining lt and lev with levelling weight set to factor 100., because number of levelling observations is low compared to laser tracker
  Perform a best-fit to the nominal tunnel shape, this gives best accordance between CAD model and reality when installing the accelerator
XTD1 adjusted in 2012
  Same principle as above, but only check, if the network fits to the nominal tunnel
  Provisionally attach XTD1 network to XTL by quick and dirty connection measurement
2012
2012
2013
2013
2013

## Slide 18: Adjustment of different tunnels / different epochs
XTL, XTD2 and XS1 measured and adjusted in 2012/2013
  Free network (laser tracker)
  Free network (levelling)
  Combine both (levelling with high weight)
  Check, if the adjusted network fits to the nominal tunnel
  Correct the XTL network by new levelling campaign
  Attach the networks of XS1, XTD1 and XTD2 to the XTL by over-constrained network adjustment (some XTL monuments are non-moveable)
  Check, if the adjusted network still fits to the nominal shape of the tunnels
For all other networks similar approaches, however,
  Lots of guessing involved engineering experience needed
    Gross errors vs. wrong à priori accuracy
    External influences, like ventilation
    Movement of “fixed” points
  Very limited time for adjustment
  … some sleepless nights

## Slide 19: Movement of XTL between 05/2012 and 02/2013
Side view
-4mm
-8mm
Injector shaft
XS1 (Distribution shaft)
glacial drift area
Top view
0.8mm (max)
Glacial drift area could be identified, in this area more bentonite had to be used during tunnel construction
Significant vertical movement close to the shafts – soil disturbance due to construction
Minimal horizontal movement, seems to be related to vertical movement

## Slide 20: Simulation of XFEL network chunk (600m)
Undulator area (up to the first mirror) is extremely sensitive to misalignment
Accuracy requirement is 0.5mm per 600m in horizontal and height
Simulation: relative error (P=99%) is up to 4mm in horizontal
Refraction: systematic error could add up a factor of 5 with DT=2K
Solution: We need a refraction free measurement system  SLRS
SLRS is expensive, only installed in three critical areas
Simulation of free tunnel network L=600m, ellipses 50:1 black: point error ellipses red: relative error ellipses

## Slide 21: System setup
Dx, Dz
Dx, Dz
Dx, Dz
System Integration
  The SLRS (Straight Line Reference Surveyor) is a refraction free alignment system
  It uses a collimated laser beam within an ISO200 vacuum tube
  SLRS is used like a ruler put into the seemingly bent (refraction) tunnel network
  There is no direct connection between the SLRS and machine components
  SLRS provides correction parameters (dx, dz) for the geodetic network
  Calibrated targets are used to connect the SLRS measurements
    to the tunnel network

## Slide 22: System setup
Principle of the SLRS:
  A laser light source emits coherent light
  A fiber end, aperture and a plano convex lens are used to expand and collimate the beam
  Spheres put into the beam along the measuring section originate a poisson spot behind the center of the sphere which can be viewed with a CCD camera
  The center of the sphere and the center of its poisson spot in the image generate a straight line
  A lens system focuses the expanded beam to the dimensions of the CCD sensor
  Correlation algorithms are used to calculate the poisson centers in the image
Plano-convex lens
Targets
Plano-convex lenses
CCD Camera
Laser Point Source
Aperture
Johannes Prenting, IWAA 2016

## Slide 23: System setup
Actual setup:
      Aluminum pipes, 7.73m/3.87m long, 200mm diameter. Supports are placed every 3 to 4.5m with fixed point and floating point fixing.
      special housings for (laser, aperture, lenses) and (lenses & camera)
      Tee piece connector with bellows, every 24m, every 2nd is equipped with adapted measurement targets (aka target boxes)
      blue laser (wavelength = 405nm) allows for small targets and provides fine interference patterns
      revised plano convex lenses for minimal spherical aberration
      GigE-Camera with 2048x2048 pix. resolution
      Oerlikon/Leybold Trivac D 65 B Vacuum pumps
housing for laser, aperture, lens
camera housing
SLRS@SASE1, 482m
Tee piece connector & bellows
Johannes Prenting, IWAA 2016

## Slide 24: System setup, 1. SLRS, SASE1, XTD2, some impressions
camera housing
fiber end of laser light source
lens mount in pivot bearing
laser housing with central optics pipe
view at aperture and laser fiber from inside lens tube
installation of laser into laser housing
target box
Johannes Prenting, IWAA 2016

## Slide 25: How does it work?
The Poisson Spot
  By interference a poisson spot develops behind a sphere put into coherent light
  Each point at the spheres outline acts as a single lightsource
  The 2D sectional view shows how the centre of the image is formed by interference of lightwaves which travel the same distance „r“
  The next high intensity ring of the poisson image is formed by interference of lightwaves that travel distances „a“ and „b“ which are different by one wavelength.
  A low intensity ring is formed by interference of lightwaves that travel distances that are different by 1/2 wavelength.
sectional view of interferences behind a sphere put into coherent light
poisson image of a sphere
Johannes Prenting, IWAA 2016

## Slide 26: Commissioning of SLRS@SASE1: please, let there be light
Simulation vs. real thing
first image after complete installation and
adjustment from outside with lasertracker, 0823
image after complete installation and
first adjustment of laserlightsource, 0824
image after adjustment check @ of every single tee
piece with laser beam itself, 0831, no target installed
image after implementation of target
frame, fine aligning the laser
image after implementation of target
frame, fine alignment of laser done
image after implementation of target frame,
aligning target frame with camera image
simulated image of target box ‚9‘ @ 200m
image after implementation of target frame,
(box 9), varying the exposure
Johannes Prenting, IWAA 2016

## Slide 27: SLRS Status
All three SLRS are operational, measurements were done
Preliminary network adjustment has been done
Lasing was achieved at SASE1 with minimal movements of quadrupoles.
Distribution of SLRS systems in the XFEL
SASE1: 482m
SASE2: 530m
SASE3: 434m
Distribution of SLR-Systems in XFEL Tunnels
Tunnel network has to be re-measured while simultaneously collecting SLRS data
SLRS corrections are applied to the laser tracker and levelling network

## Slide 28: Simulation of XFEL network chunk (600m) – with SLRS
Accuracy requirement – 0.5mm per 600m in horizontal and height – is fulfilled
Simulation: relative error (P=99%) is up to 0.4mm in horizontal
Refraction: systematic error is greatly reduced due to vacuum tube (1mbar)
Simulation of free tunnel network without / with SLRS L=600m, ellipses 50:1 black: point error ellipses red: relative error ellipses

## Slide 29: SLRS & network adjustment
P1
Pi
Pn
x
x
x
n : number of SLRS measurements → n-2 constraints
x
x
P2
Pn-1
d2
di
dn-1
Functional Model of constraints:
distances between points and line are 0
Scheme of SLRS

## Slide 30: Gauss Markov Model
(Least Squares Model)
(“generalized” Least Squares Model)
(Least Squares Model with constraints)
  Vector of observations
  Vector of unknowns
Model with constraints is sufficient (Method of Lagrange multipliers).
n : number of SLRS measurements → n-2 constraints

## Slide 31: Gauss Markov Model
Derivatives needed for Matrix A2
All other derivatives are 0
Design matrix of constraints
Normal equations for Gauß Markov
Normal equations with constraints

## Slide 32: Adjustment strategy
Model with constraints would give the correct solution for coordinates and statistics, but software for this model was not ready in time
PANDA is not able to integrate constraints in a convenient way
Actual approach
  Free network solution (laser tracker and levelling) without SLRS
  Compare actual solution of SLRS points from free network with SLRS measurement, calculate corrections
  Apply corrections from SLRS to actual points from free network
  Introduce corrected points into new network adjustment as fixed points, thus making it a (over-)constrained network.
  Since the network was estimated as free network first, this step does not introduce any constraints but those coming from SLRS
The actual solution will be close to the correct solution, concerning the coordinates of all reference points
However, the stochastic model is wrong. This is not important for the actual work, but matters for possible analysis in the future, like deformation analysis.

## Slide 33: Result of SLRS measurement, SASE1-3
Corrections from SLRS are up to 3mm
Vertical corrections are smaller, because we have à priori levelling information
“wavelength” of disturbances is much smaller than expected  too few points!
Chart: horizontal corrections
SASE1 | 0 | 2.5087 | 1.0282 | 0.25904 | 1.1529 | -0.54129 | 0.11533 | 0.30368 | 0
SASE2 | 0 | -1.98 | -2.485 | 1.344 | 2.825 | 0.963 | 0.121 | 0.479 | 0
SASE3 | 0 | -0.64 | -0.498 | -1.279 | -0.573 | -1.243 | 0.264 | 0
Chart: vertical corrections
SASE1 | 0 | -1.7881 | -0.81869 | 0.75098 | -0.85602 | -0.096406 | 0.25557 | 0.081544 | 0
SASE2 | 0 | 0.027 | -1.048 | -0.219 | 0.459 | -0.926 | -0.273 | 0.392 | 0
SASE3 | 0 | 0.562 | 1.709 | 0.123 | 0.475 | 1.036 | -0.149 | 0

## Slide 34: Beam based alignment results
For SASE1 and SASE3 the beam went through the undulator section without steering it with the magnets, aperture of vacuum chamber is as low as ±4mm
For SASE1 a first beam based alignment of the intersections has been done
  Results show good accuracy for BPM
  Accuracy of quadrupoles is not as good as could be expected, several possible reasons (to be investigated)
    Beam based alignment is wrong (don’t know, ask the experts)
    Alignment is wrong (unlikely, because we are geodesists the BPM are close to the quadrupoles (~30cm))
    Measurement system of the movers has been misread
    Fiducialization of quadrupoles magnetic axes is inaccurate (in-kind-contribution)
    Quadrupole axis changes more than expected with different current (would influence the beam based alignment)
    …?
0
10
[mm]
horizontal
vertical
BPM
Quad
0
-4
4

## Slide 35: Thank you!
And now for the XFEL tunnel flight…