PLL for 2nd harmonic cavity
C.Y. Tan
31 Aug 2017

---
Why PLL?
- We need to keep the cavity resonance and the drive frequency in sync.
  - There is a bias current ramp and we have to make sure that the error between the cavity resonance and the drive frequency is tolerable.
  - “Tolerable” here means that we have enough power to drive the cavity to 100 kV even if we are off resonance.
  - Note: we probably won’t drive the cavity at resonance due to Robinson stability requirements. A programmed offset phase in the PLL loop can easily accommodate this requirement.
- Note: No beam loading taken into account at this stage.
  - Need fast PLL for beam loading if necessary.
  - Or other forms of beam loading compensation.

---
PLL block diagram

---
How PLL works with a grad student
Our grad student looks at the output of the phase detector and sees that the phase difference, Δθ, between the drive and the pickup is no longer zero. He then changes the solenoid bias to shift the resonance of the cavity so that Δθ goes to zero again.
If he turns the bias knob too quickly, he might overshoot. If too slowly he might never catch up. ← This is the gain of the loop.
This is how a PLL works.

---
Modeling
Bias solenoid modeled as LR circuit
Cavity phase response linearized about resonance.

---
Usual to analyze PLL in Laplace space
In “s” space analysis, I found that for the PLL to converge when there is a frequency ramp, I needed an integrator.

---
Normalized H Bode plots at 76 MHz
The H Bode plot does not look like a low pass filter because of the extra “s” in the numerator from the bias solenoid. However for low enough frequencies, everything converges. BW is limited to < 3 kHz.
This is ok since corrections are not expected to be larger than 1 kHz bw.

---
Time domain
Use Gennady’s CST results (22 Jun 2017) and fit to “charging” exponentials.

---
PLL parameters and requirements
- Open loop gain set to 5000
- Bias solenoid
  - Ls = 4.7 mH, Rs = 21.6 mΩ
- Given the shunt impedance Rc and Qc, I can calculate the required frequency tolerance from 76 MHz to 81 MHz and assuming max power of 100 kW

---
Results
Frequency step 100 kHz
Sudden changes in slope are bad: Frequency errors outside +/- 10 kHz.
Frequency ramp track error

---
Results of proposed ramp
Errors are within the required +/- 10 kHz

---
Conclusion
- We have a theoretical design that should be able to track and lock to the given 3 ms ramp to within the required tolerance
  - No noise in the system that will reduce the bw.
  - No beam loading yet!
    - Initial calculations show that this may be a concern.