## Slide 1: Parallel-Biased Replacement Booster Cavity
Mohamed Hassan
PIP Replacement Booster Cavity
Aug 15th 2017

## Slide 2: Large Bore Cavity Testing
With large bore the whole frequency range will move to lower range, tuning range decreases
First design goal is to adjust the sweep range with the new 3.25” bore radius

## Slide 3: Trials for 3.25” Bore
 | F1 [MHz] | F2 [MHz]
Taper close to current (-0.04) | 35.2 | 50.4
Taper is steeper (-0.1) | 36.1 | 51.3
Gap piece diameter | 36.4 | 51.9
Moving dielectric window 2” towards gap | 36.3 | 51.8
Center cast diameter | 37.6 | 52.8
Center cast diameter | 37.8 | 52.9

## Slide 4: Preliminary Design
3.25” Bore
Steeper Taper
8.5”
Meeting first goal (37.8 MHz to 52.9 MHz)

## Slide 5: Electric Field at 37.8 MHz (60 kV)
MV/m
MV/m

## Slide 6: After Blending Edges with 0.5” (60 kV)

## Slide 7: Preliminary Design2
3.25” Bore
Steeper Taper
9.284”
Longer Stem +0.5”

## Slide 8: Preliminary Design2 Tuner Changes
 | F1 [MHz] | F2 [MHz]
As Is | 36.8 | 52.1
One Stackpole Out (replaced by copper) | 38.2 | 53.2
4Tsh+10Sp | 37.3 | 52.6
3Tsh+11Sp | 37.7 | 52.9
2Tsh+12Sp | 38.1 | 53.3
1Tsh+13Sp | 38.4 | 53.7
All Sp | 38.7 | 54.0
13 SP | 39.2 | 54.5
3Tsh+10SP | 38.1 | 53.4

## Slide 9: Preliminary Design2 Max Field with 0.5” Rounding (60 kV)
All SP 38.7 MHz with 60 kV

## Slide 10: Energy and Heeating
 |  | mu=8.4 | mu=3 |  |  |  |  |  |  |  | 
 |  | f1 [MHz] | f2 [MHz] | Q1 | Q2 | E1 [mJ] | E2 [mJ] | Eav [mJ] | Ecycle [mJ] | Gap [kV] | BW[ MHz]
Ref Cavity |  | 37.3 | 53.5 | 286 | 1123 | 42.9 | 14.8 | 28.85 | 19.91 | 55 | 16.2
 |  | 38.7 | 54.0 | 337 | 1490 | 38.9 | 13.4 | 26.2 | 18.1 | 55 | 15.3
New All SP |  | 38.7 | 54.0 | 337 | 1490 | 46.3 | 15.9 | 31.1 | 21.5 | 60 | 15.3
New All SP |  | 37.3 | 53.5 |  |  | 43.7 | 13.0 | 28.35 | 19.56 | 55 | 15.3
New All SP |  | 37.3 | 53.5 |  |  | 52.1 | 15.4 | 33.75 | 23.29 | 60 | 15.3
Estimated

## Slide 11: Preliminary Design3
Longer Stem +1”
3.25” Bore
Steeper Taper
9.284”

## Slide 12: Preliminary Design3 Tuner Changes
 | F1 [MHz] | F2 [MHz]
Design2: 3Tsh+10SP | 38.1 | 53.4
Design3: 3Tsh+10SP | 37.8 | 53.1
 |  | mu=8.4 | mu=3 |  |  |  |  |  |  |  | 
 |  | f1 [MHz] | f2 [MHz] | Q1 | Q2 | E1 [mJ] | E2 [mJ] | Eav [mJ] | Ecycle [mJ] | Gap [kV] | BW[ MHz]
Ref Cavity |  | 37.3 | 53.5 | 286 | 1123 | 42.9 | 14.8 | 28.85 | 19.91 | 55 | 16.2
 |  | 38.7 | 54.0 | 337 | 1490 | 38.9 | 13.4 | 26.2 | 18.1 | 55 | 15.3
New All SP |  | 38.7 | 54.0 | 337 | 1490 | 46.3 | 15.9 | 31.1 | 21.5 | 60 | 15.3
Design3 3Tsh+10SP |  | 37.8 | 53.1 | 309 | 1327 | 49.27 | 16.89 | 33.08 | 22.83 | 60 | 15.3

## Slide 13: Design3 3Tsh+10SP

## Slide 14: Near Flat Tuner
Longer Stem +1”
3.25” Bore
Steeper Taper
9.284”
1.6”
 | F1 [MHz] | F2 [MHz]
Design2: 3Tsh+10SP | 38.1 | 53.4
Design3: 3Tsh+10SP | 37.8 | 53.1
Near Flat Tuner 3Tsh+10SP | 38.2 | 50.5

## Slide 15: Double Taper Tuner
Longer Stem +1”
3.25” Bore
Steeper Taper
9.284”
2.4”
 | F1 [MHz] | F2 [MHz]
Design2: 3Tsh+10SP | 38.1 | 53.4
Design3: 3Tsh+10SP | 37.8 | 53.1
Near Flat Tuner 3Tsh+10SP | 38.2 | 50.5
Double Taper Tuner 3Tsh+10SP | 38.9 | 52.3

## Slide 16
 | F1 [MHz] | F2 [MHz]
Design A: 3Tsh+10SP | 37.8 | 53.0
Design B: 5Tsh+9SP | 37.1 | 52.3
Steeper Taper -0.12, 4Tsh+9SP | 37.26 | 52.45
Steeper Taper -0.15, 4Tsh+9SP | 37.46 | 52.54
Design C: 5Tsh+8SP | 38.5 | 53.5
Longer Stem +1”
3.25” Bore
Steeper Taper
9.284”
Clamp
Gap
Corona

## Slide 17
-0.1
-0.12
-0.15

## Slide 18: Shorter Cavity with Existing Tuner
Upon shortening the total length of cavity by 6", frequency range is 37.6 to 53.6 MHz with the existing tuner (5 Toshiba, 9 Stackpole per each half tuner)
It is definitely a good option if the beam dynamics and mechanical design allows.
4” shorter 37.4 to 53.2 MHz

## Slide 19: Decisions
Cavity length can’t be changed
We settled on using Design A; 3Tsh, 10SP (1st Tsh ferrite ring will be replaced by copper filling).
3.25” Bore
Steeper Taper
9.284”
Clamp
Gap
Corona
Longer Stem +1”

## Slide 20: Preliminary Thermal Analysis
60 kV
Simplified averaging over the cycle
More accurate analysis is undergoing

## Slide 21: Accurate Cycle Averaging for the Current Booster Cavity
R/Q=V^2/(2wU)
Time [ms] | mu | Frequency [MHz] | Energy [mJ] | V [kV] | Q | R/Q | Vol Losses [kW] | Surf Losses [kW] | Ploss-55kV [kW] | Ratio
0 | 8.200 | 37.7 | 170.51 | 55 | 293 | 37.47 | 137.83 | 7.15 | 144.98 | 19.26
1 | 7.900 | 38.3 | 163.84 | 55 | 306 | 38.38 | 128.72 | 7.07 | 135.78 | 18.22
2 | 7.400 | 39.3 | 152.78 | 55 | 331 | 40.11 | 113.97 | 7.03 | 121.00 | 16.20
3 | 6.800 | 40.7 | 139.60 | 55 | 367 | 42.39 | 97.63 | 7.00 | 104.63 | 13.95
4 | 6.100 | 42.4 | 124.40 | 55 | 419 | 45.66 | 79.09 | 6.96 | 86.05 | 11.36
5 | 5.400 | 44.4 | 109.42 | 55 | 489 | 49.57 | 62.49 | 6.89 | 69.38 | 9.07
6 | 4.950 | 45.8 | 99.94 | 55 | 547 | 52.62 | 52.65 | 6.76 | 59.41 | 7.79
7 | 4.550 | 47.2 | 91.65 | 55 | 611 | 55.68 | 44.49 | 6.68 | 51.17 | 6.66
8 | 4.250 | 48.3 | 85.52 | 55 | 670 | 58.31 | 38.73 | 6.58 | 45.30 | 5.89
9 | 4.020 | 49.2 | 80.88 | 55 | 723 | 60.52 | 34.60 | 6.50 | 41.10 | 5.32
10 | 3.810 | 50.1 | 76.70 | 55 | 779 | 62.67 | 30.98 | 6.44 | 37.41 | 4.81
11 | 3.670 | 50.7 | 73.95 | 55 | 821 | 64.24 | 28.67 | 6.40 | 35.07 | 4.48
12 | 3.570 | 51.1 | 71.99 | 55 | 854 | 65.47 | 27.07 | 6.38 | 33.45 | 4.24
13 | 3.480 | 51.5 | 70.25 | 55 | 886 | 66.57 | 25.67 | 6.32 | 31.99 | 4.06
14 | 3.420 | 51.8 | 69.09 | 55 | 909 | 67.29 | 24.75 | 6.30 | 31.05 | 3.93
15 | 3.380 | 52.0 | 68.33 | 55 | 924 | 67.79 | 24.15 | 6.28 | 30.43 | 3.85
16 | 3.340 | 52.2 | 67.56 | 55 | 940 | 68.29 | 23.55 | 6.26 | 29.81 | 3.76
17 | 3.320 | 52.3 | 67.18 | 55 | 949 | 68.55 | 23.26 | 6.25 | 29.51 | 3.72
18 | 3.300 | 52.4 | 66.80 | 55 | 957 | 68.81 | 22.96 | 6.24 | 29.21 | 3.68
19 | 3.255 | 52.6 | 65.94 | 55 | 977 | 69.43 | 22.31 | 6.22 | 28.53 | 3.59
20 | 3.255 | 52.6 | 65.94 | 55 | 977 | 69.43 | 22.31 | 6.22 | 28.53 | 3.59
21 | 3.255 | 52.6 | 65.94 | 55 | 977 | 69.43 | 22.31 | 6.22 | 28.53 | 3.59
22 | 3.230 | 52.7 | 65.47 | 55 | 988 | 69.80 | 21.95 | 6.21 | 28.16 | 3.53
23 | 3.230 | 52.7 | 65.47 | 55 | 988 | 69.80 | 21.95 | 6.21 | 28.16 | 3.53
24 | 3.230 | 52.7 | 65.47 | 55 | 988 | 69.80 | 21.95 | 6.21 | 28.16 | 3.53
25 | 3.230 | 52.7 | 65.47 | 55 | 988 | 69.80 | 21.95 | 6.21 | 28.16 | 3.53
26 | 3.205 | 52.8 | 65.00 | 55 | 999 | 70.18 | 21.60 | 6.20 | 27.79 | 3.48
27 | 3.205 | 52.8 | 65.00 | 55 | 999 | 70.18 | 21.60 | 6.20 | 27.79 | 3.48
28 | 3.205 | 52.8 | 65.00 | 55 | 999 | 70.18 | 21.60 | 6.20 | 27.79 | 3.48
29 | 3.205 | 52.8 | 65.00 | 55 | 999 | 70.18 | 21.60 | 6.20 | 27.79 | 3.48
30 | 3.205 | 52.8 | 65.00 | 55 | 999 | 70.18 | 21.60 | 6.20 | 27.79 | 3.48
31 | 3.205 | 52.8 | 65.00 | 55 | 999 | 70.18 | 21.60 | 6.20 | 27.79 | 3.48
32 | 3.205 | 52.8 | 65.00 | 55 | 999 | 70.18 | 21.60 | 6.20 | 27.79 | 3.48
33 | 3.205 | 52.8 | 65.00 | 55 | 999 | 70.18 | 21.60 | 6.20 | 27.79 | 3.48
34 | 3.205 | 52.8 | 65.00 | 55 | 999 | 70.18 | 21.60 | 6.20 | 27.79 | 3.48
35 | 3.205 | 52.8 | 65.00 | 55 | 999 | 70.18 | 21.60 | 6.20 | 27.79 | 3.48
 |  |  |  |  |  | Sum | 1391.94 | 230.97 | 1622.91 | 
 |  |  |  |  |  | Ploss (CW) | 39.77 | 6.60 | 46.37 | 
 |  |  |  |  |  | Ploss (15 Hz) | 19.88 | 3.30 | 23.18 | 6.03

## Slide 23: Replacement Cavity (60 kV)

## Slide 24: Booster Cavity (55 kV)

## Slide 25
frequency range is 38.0 to 53.1 MHz

## Slide 27: Matched Mechanical Models
Current Booster Cavity
 | Mu=8.4 | Mu=3 | Mu=9 | Mu=3.7
Current Cavity | 40 | 56.4 | 37.8 | 53
Replacement Cavity (slope -0.1, 1st Tsh is removed) 9SP, 4Tsh | 38.3 | 54.2 | 37.2 | 51.2
x
x
Booster Replacement Cavity

## Slide 28
 | Mu=9 | Mu=3.7
10 SP, 1Tsh (removing 3 Tsh) | 38.6 | 53
12 SP (removing 2 Tsh) | 38.5 | 52.8

## Slide 29
 | Mu=9 | Mu=3.7
9SP, 5Tsh | 35.8 | 50
9SP, 4Tsh (Mx1) | 36.4 | 50.5
9SP, 3Tsh (Mx2) | 37.2 | 51.4
9SP, 2Tsh (Mx3) | 38.1 | 52.5
10 SP, 1Tsh (Mx3) | 38.6 | 53
13 SP (Mx1) | 38.0 | 52.2
12 SP (Mx2) | 38.5 | 52.8
12 SP (Ex2) | 41.4 | 55
13 SP (Ex1) | 39.4 | 53.3
 | Mu=9 | Mu=3.7
9SP, 5Tsh | 37.2 | 51.2
10SP, 1Tsh (Mx3) | 39.3 | 53.6
12SP (Mx2) | 39.2 | 53.4
1Tsh,11SP (Mx2) | 38.0 | 52.4
(E1x) 1Tsh,11 SP (Mx1) | 39.5 | 53.5
(E1x) 2Tsh, 10 SP (Mx1) | 38.4 | 52.6
(E1x) 2Tsh, 10 SP (Mx1), B | 38.8 | 52.7
(E1x) 2Tsh,9 SP (Mx1), B | 38.9 | 53.2

## Slide 30: Fine Tuning for Frequency Range with Taper
C=-0.01 | 12 SP (Mx2) | 38.5 | 52.8
C=-0.03 | 12 SP (Mx2) | 38.7 | 53

## Slide 31: R/Q Comparison
Current Cavity |  |  |  |  |  | 
Mu | freq [MHz] | Q | V [kV] | E [mJ] | R/Q | E60kV [mJ]
9 | 37.8 | 260 | 61.119 | 197.087 | 39.9 | 189.94
3.7 | 53 | 809 | 102.21 | 197.087 | 79.59 | 67.92
Replacement Cavity |  |  |  |  |  | 
Mu | freq [MHz] | Q | V [kV] | E [mJ] | R/Q | E60kV [mJ]
9 | 38.7 | 299 | 56.69 | 197.087 | 33.53 | 220.77382
3.7 | 53 | 1014 | 94.228 | 197.087 | 67.64 | 79.90989
R/Q=V^2/(2wU)

## Slide 34: After Adding the Tetrode
 | Mu=9 | Mu=3.7 | Mu=6.6 | Mu=2.1
Current Cavity | 33.3 | 45.9 | 37.7 | 52.9
Replacement Cavity (slope -0.05, 12SP (Mx2) | 37.9 | 47.0 | 39.2 | 53.2

## Slide 35: Adjusting Loss Tangent to Adjust Q
Measurements Booster Cavity | 
f0 [MHz] | Q
26.731 | 132
29.872 | 166
39.912 | 345
49.974 | 847
52.79 | 1077
53.855 | 1197
 | Current Booster |  |  | Replacement Cavity |  | 
mu | 17 | 6.6 | 2.1 | 17 | 6.6 | 2.1
Freq [MHz] | 24.7 | 37.7 | 52.9 | 26.7 | 39.2 | 53.2
Q | 123 | 391 | 2050 | 150 | 469 | 2785
 | Current Booster |  |  | Replacement Cavity |  | 
mu | 17 | 6.6 | 2.1 | 17 | 6.6 | 2.1
Freq [MHz] | 24.7 | 37.7 | 52.9 | 26.7 | 39.2 | 53.2
Adjusted Q | 65 | 208 | 1128 | 79 | 250 | 1544

## Slide 36: Replacement vs Current Booster Cavities
 | Current Booster |  | Replacement Cavity |  | 
mu | 6.6 | 2.1 | 7.35 | 2.1 | 
Freq [MHz] | 37.7 | 52.9 | 37.7 | 53.2 | 
Adjusted Q | 208 | 1128 | 407 | 1544 | 
E[mJ]-60kV | 243.80 | 98.32 | 283.53 | 104.93 | 
R/Q | 31.17 | 55.08 | 26.80 | 51.32 | 
Eav [mJ] | 171.06 |  | 194.23 |  | 
Ecycle [mJ] | 118.03 |  | 134.02 |  | 1.14
R/Q=V^2/(2wU)

## Slide 37: Booster Cavity
Time [ms] | mu | Frequency [MHz] | Energy [mJ] | V [kV] | Q | R/Q | Vol Losses [kW] | Surf Losses [kW] |  | Energy [mJ] 60kV | Vol Losses for 60 kV [kW] | Surf Losses forr 60kV [kW] | Ploss-60kV [kW] | Ratio
0 | 6.64 | 37.7 | 197.087 | 54.113 | 389 | 31.36 | 119.990 | 10.713 |  | 242.30 | 147.52 | 13.17 | 160.69 | 11.20
1 | 6.38 | 38.3 | 197.087 | 55.164 | 409 | 32.08 | 115.840 | 11.155 |  | 233.16 | 137.04 | 13.20 | 150.24 | 10.38
2 | 5.94 | 39.3 | 197.087 | 57.076 | 448 | 33.47 | 108.580 | 11.979 |  | 217.80 | 119.99 | 13.24 | 133.23 | 9.06
3 | 5.39 | 40.7 | 197.087 | 59.374 | 508 | 34.97 | 99.097 | 13.163 |  | 201.26 | 101.20 | 13.44 | 114.64 | 7.53
4 | 4.77 | 42.4 | 197.087 | 63.158 | 598 | 37.99 | 87.801 | 14.751 |  | 177.87 | 79.24 | 13.31 | 92.55 | 5.95
5 | 4.16 | 44.4 | 197.087 | 67.059 | 723 | 40.89 | 76.016 | 16.641 |  | 157.78 | 60.85 | 13.32 | 74.18 | 4.57
6 | 3.75 | 45.8 | 197.087 | 70.036 | 838 | 43.24 | 67.712 | 18.137 |  | 144.65 | 49.70 | 13.31 | 63.01 | 3.73
7 | 3.39 | 47.2 | 197.087 | 72.921 | 971 | 45.49 | 60.179 | 19.627 |  | 133.43 | 40.74 | 13.29 | 54.03 | 3.07
8 | 3.12 | 48.3 | 197.087 | 75.269 | 1099 | 47.36 | 54.395 | 20.853 |  | 125.24 | 34.56 | 13.25 | 47.82 | 2.61
9 | 2.90 | 49.2 | 197.087 | 77.307 | 1229 | 49.05 | 49.614 | 21.958 |  | 118.72 | 29.89 | 13.23 | 43.11 | 2.26
10 | 2.70 | 50.1 | 197.087 | 79.261 | 1372 | 50.63 | 45.228 | 23.020 |  | 112.94 | 25.92 | 13.19 | 39.11 | 1.96
11 | 2.58 | 50.7 | 197.087 | 80.482 | 1474 | 51.58 | 42.586 | 23.689 |  | 109.54 | 23.67 | 13.17 | 36.83 | 1.80
12 | 2.50 | 51.1 | 197.087 | 81.316 | 1549 | 52.25 | 40.823 | 24.148 |  | 107.30 | 22.23 | 13.15 | 35.37 | 1.69
13 | 2.41 | 51.5 | 197.087 | 82.272 | 1642 | 53.07 | 38.840 | 24.678 |  | 104.82 | 20.66 | 13.13 | 33.78 | 1.57
14 | 2.34 | 51.8 | 197.087 | 83.033 | 1721 | 53.74 | 37.299 | 25.100 |  | 102.91 | 19.48 | 13.11 | 32.58 | 1.49
15 | 2.31 | 52 | 197.087 | 83.362 | 1757 | 53.96 | 36.640 | 25.283 |  | 102.10 | 18.98 | 13.10 | 32.08 | 1.45
16 | 2.27 | 52.2 | 197.087 | 83.804 | 1807 | 54.32 | 35.762 | 25.529 |  | 101.03 | 18.33 | 13.09 | 31.42 | 1.40
17 | 2.25 | 52.3 | 197.087 | 84.026 | 1833 | 54.51 | 35.323 | 25.654 |  | 100.49 | 18.01 | 13.08 | 31.09 | 1.38
18 | 2.23 | 52.4 | 197.087 | 84.25 | 1860 | 54.69 | 34.885 | 25.779 |  | 99.96 | 17.69 | 13.07 | 30.77 | 1.35
19 | 2.19 | 52.6 | 197.087 | 84.701 | 1915 | 55.07 | 34.010 | 26.030 |  | 98.90 | 17.07 | 13.06 | 30.13 | 1.31
20 | 2.19 | 52.6 | 197.087 | 84.701 | 1915 | 55.07 | 34.010 | 26.030 |  | 98.90 | 17.07 | 13.06 | 30.13 | 1.31
21 | 2.19 | 52.6 | 197.087 | 84.701 | 1915 | 55.07 | 34.010 | 26.030 |  | 98.90 | 17.07 | 13.06 | 30.13 | 1.31
22 | 2.17 | 52.7 | 197.087 | 84.927 | 1944 | 55.26 | 33.573 | 26.157 |  | 98.37 | 16.76 | 13.06 | 29.81 | 1.28
23 | 2.17 | 52.7 | 197.087 | 84.927 | 1944 | 55.26 | 33.573 | 26.157 |  | 98.37 | 16.76 | 13.06 | 29.81 | 1.28
24 | 2.17 | 52.7 | 197.087 | 84.927 | 1944 | 55.26 | 33.573 | 26.157 |  | 98.37 | 16.76 | 13.06 | 29.81 | 1.28
25 | 2.17 | 52.7 | 197.087 | 84.927 | 1944 | 55.26 | 33.573 | 26.157 |  | 98.37 | 16.76 | 13.06 | 29.81 | 1.28
26 | 2.15 | 52.8 | 197.087 | 85.155 | 1973 | 55.45 | 33.137 | 26.285 |  | 97.85 | 16.45 | 13.05 | 29.50 | 1.26
27 | 2.15 | 52.8 | 197.087 | 85.155 | 1973 | 55.45 | 33.137 | 26.285 |  | 97.85 | 16.45 | 13.05 | 29.50 | 1.26
28 | 2.15 | 52.8 | 197.087 | 85.155 | 1973 | 55.45 | 33.137 | 26.285 |  | 97.85 | 16.45 | 13.05 | 29.50 | 1.26
29 | 2.15 | 52.8 | 197.087 | 85.155 | 1973 | 55.45 | 33.137 | 26.285 |  | 97.85 | 16.45 | 13.05 | 29.50 | 1.26
30 | 2.15 | 52.8 | 197.087 | 85.155 | 1973 | 55.45 | 33.137 | 26.285 |  | 97.85 | 16.45 | 13.05 | 29.50 | 1.26
31 | 2.15 | 52.8 | 197.087 | 85.155 | 1973 | 55.45 | 33.137 | 26.285 |  | 97.85 | 16.45 | 13.05 | 29.50 | 1.26
32 | 2.15 | 52.8 | 197.087 | 85.155 | 1973 | 55.45 | 33.137 | 26.285 |  | 97.85 | 16.45 | 13.05 | 29.50 | 1.26
33 | 2.15 | 52.8 | 197.087 | 85.155 | 1973 | 55.45 | 33.137 | 26.285 |  | 97.85 | 16.45 | 13.05 | 29.50 | 1.26
34 | 2.15 | 52.8 | 197.087 | 85.155 | 1973 | 55.45 | 33.137 | 26.285 |  | 97.85 | 16.45 | 13.05 | 29.50 | 1.26
35 | 2.15 | 52.8 | 197.087 | 85.155 | 1973 | 55.45 | 33.137 | 26.285 |  | 97.85 | 16.45 | 13.05 | 29.50 | 1.26
 |  |  |  |  |  |  |  |  |  | Sum | 1268.43 | 472.74 | 1741.16 | 2.68
 |  |  |  |  |  |  |  |  |  | Ploss (CW) | 35.23 | 13.13 | 48.37 | 
 |  |  |  |  |  |  |  |  |  | Ploss (15 Hz) | 17.62 | 6.57 | 24.18 | 
8 | 3.12 | 48.3 | 197.087 | 75.269 | 1099 | 47.36 | 54.395 | 20.853 |  |  | 34.56 | 13.25 | 47.82 | 2.61

## Slide 38: Booster Replacement Cavity
Time [ms] | mu | Frequency [MHz] | Energy [mJ] | V [kV] | Q | R/Q | Vol Losses [kW] | Surf Losses [kW] |  | Energy [mJ] 60kV | Vol Losses for 60 kV [kW] | Surf Losses forr 60kV [kW] | Ploss-60kV [kW] | Ratio
0 | 7.35 | 37.7 | 197.087 | 50.023 | 216 | 26.80 | 216.032 | 11.104 |  | 283.5443592 | 310.80 | 15.98 | 326.78 | 19.46
1 | 7.05 | 38.3 | 197.087 | 51.078 | 228 | 27.50 | 207.62 | 11.552 |  | 271.9522849 | 286.49 | 15.94 | 302.43 | 17.97
2 | 6.56 | 39.3 | 197.087 | 52.934 | 252 | 28.79 | 193.46 | 12.352 |  | 253.2159472 | 248.56 | 15.87 | 264.43 | 15.66
3 | 5.93 | 40.7 | 197.087 | 55.597 | 289 | 30.66 | 174.444 | 13.520 |  | 229.5396759 | 203.17 | 15.75 | 218.91 | 12.90
4 | 5.25 | 42.4 | 197.087 | 58.882 | 343 | 33.02 | 152.832 | 14.992 |  | 204.6422837 | 158.69 | 15.57 | 174.26 | 10.19
5 | 4.53 | 44.4 | 197.087 | 62.293 | 427 | 35.29 | 128.712 | 16.836 |  | 182.8445357 | 119.41 | 15.62 | 135.03 | 7.65
6 | 4.07 | 45.8 | 197.087 | 65.86 | 503 | 38.24 | 112.68 | 18.200 |  | 163.5750369 | 93.52 | 15.11 | 108.63 | 6.19
7 | 3.66 | 47.2 | 197.087 | 68.743 | 596 | 40.42 | 98.06 | 19.544 |  | 150.1424565 | 74.70 | 14.89 | 89.59 | 5.02
8 | 3.33 | 48.3 | 197.087 | 71.258 | 695 | 42.45 | 86.144 | 20.720 |  | 139.7311463 | 61.07 | 14.69 | 75.76 | 4.16
9 | 3.10 | 49.2 | 197.087 | 73.119 | 782 | 43.88 | 77.816 | 21.588 |  | 132.7088828 | 52.40 | 14.54 | 66.93 | 3.60
10 | 2.85 | 50.1 | 197.087 | 75.243 | 902 | 45.63 | 68.792 | 22.580 |  | 125.3222761 | 43.74 | 14.36 | 58.10 | 3.05
11 | 2.70 | 50.7 | 197.087 | 76.568 | 990 | 46.69 | 63.42 | 23.196 |  | 121.0224312 | 38.94 | 14.24 | 53.19 | 2.73
12 | 2.60 | 51.1 | 197.087 | 77.473 | 1057 | 47.43 | 59.864 | 23.616 |  | 118.2115012 | 35.91 | 14.16 | 50.07 | 2.53
13 | 2.51 | 51.5 | 197.087 | 78.301 | 1125 | 48.07 | 56.692 | 24.000 |  | 115.7246464 | 33.29 | 14.09 | 47.38 | 2.36
14 | 2.43 | 51.8 | 197.087 | 79.047 | 1191 | 48.70 | 53.892 | 24.344 |  | 113.5506685 | 31.05 | 14.03 | 45.08 | 2.21
15 | 2.38 | 52 | 197.087 | 79.519 | 1235 | 49.10 | 52.16 | 24.560 |  | 112.2066664 | 29.70 | 13.98 | 43.68 | 2.12
16 | 2.33 | 52.2 | 197.087 | 79.995 | 1283 | 49.50 | 50.432 | 24.776 |  | 110.8752965 | 28.37 | 13.94 | 42.31 | 2.04
17 | 2.31 | 52.3 | 197.087 | 80.186 | 1302 | 49.64 | 49.748 | 24.864 |  | 110.3477241 | 27.85 | 13.92 | 41.77 | 2.00
18 | 2.30 | 52.4 | 197.087 | 80.282 | 1313 | 49.66 | 49.404 | 24.908 |  | 110.0839776 | 27.59 | 13.91 | 41.51 | 1.98
19 | 2.25 | 52.6 | 197.087 | 80.763 | 1365 | 50.07 | 47.7 | 25.128 |  | 108.7766286 | 26.33 | 13.87 | 40.20 | 1.90
20 | 2.25 | 52.6 | 197.087 | 80.763 | 1365 | 50.07 | 47.7 | 25.128 |  | 108.7766286 | 26.33 | 13.87 | 40.20 | 1.90
21 | 2.25 | 52.6 | 197.087 | 80.763 | 1365 | 50.07 | 47.7 | 25.128 |  | 108.7766286 | 26.33 | 13.87 | 40.20 | 1.90
22 | 2.22 | 52.7 | 197.087 | 81.054 | 1398 | 50.34 | 46.684 | 25.260 |  | 107.9969711 | 25.58 | 13.84 | 39.42 | 1.85
23 | 2.22 | 52.7 | 197.087 | 81.054 | 1398 | 50.34 | 46.684 | 25.260 |  | 107.9969711 | 25.58 | 13.84 | 39.42 | 1.85
24 | 2.22 | 52.7 | 197.087 | 81.054 | 1398 | 50.34 | 46.684 | 25.260 |  | 107.9969711 | 25.58 | 13.84 | 39.42 | 1.85
25 | 2.22 | 52.7 | 197.087 | 81.054 | 1398 | 50.34 | 46.684 | 25.260 |  | 107.9969711 | 25.58 | 13.84 | 39.42 | 1.85
26 | 2.20 | 52.8 | 197.087 | 81.249 | 1421 | 50.48 | 46.008 | 25.352 |  | 107.4792014 | 25.09 | 13.83 | 38.92 | 1.81
27 | 2.20 | 52.8 | 197.087 | 81.249 | 1421 | 50.48 | 46.008 | 25.352 |  | 107.4792014 | 25.09 | 13.83 | 38.92 | 1.81
28 | 2.20 | 52.8 | 197.087 | 81.249 | 1421 | 50.48 | 46.008 | 25.352 |  | 107.4792014 | 25.09 | 13.83 | 38.92 | 1.81
29 | 2.20 | 52.8 | 197.087 | 81.249 | 1421 | 50.48 | 46.008 | 25.352 |  | 107.4792014 | 25.09 | 13.83 | 38.92 | 1.81
30 | 2.20 | 52.8 | 197.087 | 81.249 | 1421 | 50.48 | 46.008 | 25.352 |  | 107.4792014 | 25.09 | 13.83 | 38.92 | 1.81
31 | 2.20 | 52.8 | 197.087 | 81.249 | 1421 | 50.48 | 46.008 | 25.352 |  | 107.4792014 | 25.09 | 13.83 | 38.92 | 1.81
32 | 2.20 | 52.8 | 197.087 | 81.249 | 1421 | 50.48 | 46.008 | 25.352 |  | 107.4792014 | 25.09 | 13.83 | 38.92 | 1.81
33 | 2.20 | 52.8 | 197.087 | 81.249 | 1421 | 50.48 | 46.008 | 25.352 |  | 107.4792014 | 25.09 | 13.83 | 38.92 | 1.81
34 | 2.20 | 52.8 | 197.087 | 81.249 | 1421 | 50.48 | 46.008 | 25.352 |  | 107.4792014 | 25.09 | 13.83 | 38.92 | 1.81
35 | 2.20 | 52.8 | 197.087 | 81.249 | 1421 | 50.48 | 46.008 | 25.352 |  | 107.4792014 | 25.09 | 13.83 | 38.92 | 1.81
 |  |  |  |  |  |  |  |  |  | Sum | 2337.46 | 515.80 | 2853.26 | 4.53
 |  |  |  |  |  |  |  |  |  | Ploss (CW) | 66.78 | 14.74 | 81.52 | 
 |  |  |  |  |  |  |  |  |  | Ploss (15 Hz) | 33.39 | 7.37 | 40.76 | 
 | 3.48 | 47.8 | 197.087 | 70.093 | 646 | 41.50 | 22.893 | 5.044 |  |  | 16.77 | 3.70 | 20.47 | 4.54

## Slide 43: Reduced Alumina Loss Tangent from 0.0004 to 0.0001
Booster Cavity
Replacement Cavity

## Slide 44: Reduced Alumina Loss Tangent from 0.0004 to 0.0001 Cont.
Booster Cavity
Replacement Cavity
With Convective Cooling Boundaries

## Slide 45: Ceramic Stresses
Booster Cavity
Replacement Cavity

## Slide 46: Booster Cavity with 84 MHz Damper
 | Current Booster | 
 | Without Damper | With Damper
Freq [MHz] | 84.354 | 84.362
Rsh [kΩ] | 6940 | 10.59

## Slide 47: With HOM Damper
84 MHz
All Dampers (quarter symmetry)
 | Current Booster |  | Replacement Cavity | 
mu | 6.6 | 2.1 | 7.35 | 2.1
Freq [MHz] | 37.737.3 | 52.952.4 | 37.737 | 53.252.1
 | Current Booster |  |  | Replacement Cavity |  | 
mu | 6.6 | 2.1 | 2.0 | 7.35 | 2.1 | 2.0
Freq [MHz] | 37.737.2 | 52.952.2 | 52.8 | 37.7 | 53.2 | 52.55

## Slide 48: Booster Replacement Cavity with 84 MHz Damper
 | Current Booster |  | Replacement Cavity |  |  | 
 | w/o Damper | w Damper | w/o Damper | w Damper | Damper moved by +10 cm | Damper trimmed
Freq [MHz] | 52.383 | 52.384 | 53.226 | 52.546 | 52.905 | 52.770
Freq (HOM1) [MHz] | 84.354 | 84.362 | 83.786 | 84.855 | 84.224 | 84.620
Rsh [kΩ] | 6940 | 10.59 | 1767 | 6.85 | 11.05 | 8.51

## Slide 49: HOM Meas
Cavity with no bias
Tertode port was matched with load
Cavity Frequency
S21 Gap Probe to Gap Probe
84 MHz Large HOM
2nd
Green: 84 MHz Port is open
Red: 84 MHz Port is matched

## Slide 50: HOM Meas Cont.
S21 Gap Probe (US) to 84 MHz Port (DS)
84 MHz Large HOM, Q=185

## Slide 51: HOM Meas Cont.
Q-undamped (84 MHz) ~2700
Q-damped (84 MHz)~115
Simulated Q0 (84 MHz)=75000
Simulated Q-damped (84 MHz) =116
84 MHz Large HOM
S21 Gap Probe (US) to 165 Port (DS)
Green: 84 MHz Port is open
Red: 84 MHz Port is matched

## Slide 52: HOM Meas Cont.
This mode doesn’t look dangerous
S21 Gap Probe (US) to 165 Port (DS)
Green: 217 MHz Port is open
Red: 217 MHz Port is matched

## Slide 53: HOM Meas Cont.
84 MHz is the most dangerous HOM with very large shunt impedance (in agreement with simulation)
Other two modes doesn’t look dangerous
217 MHz was noticed in meas but the 165 MHz was not observed