## Slide 2: LHC Operation & Status
Rende Steerenberg
CERN, BE-OP
With thanks to many colleagues for their input and material

## Slide 3: Topics
The CERN Accelerator Complex
Looking Back at the 2017 LHC Run
Beam Variants From Injectors
2018 LHC Schedule
CERN Upgrade Projects (LIU & HL-LHC)

## Slide 4: The CERN Accelerator Complex

## Slide 5: The CERN Accelerator Complex

## Slide 6: LINAC 2
Accelerates beam up to 50 MeV over a length of 33m, using Alvarez structures
Provides a beam pulse every 1.2s
Duoplasmatron proton source
Extract protons at 90 keV from H2

## Slide 7: PS Booster
1st Synchrotron in the chain with 4 superposed rings
Circumference of 157m
Increases proton energy from 50 MeV to 1.4 GeV on a 1.2s cycle
The LINAC2 pulse is distributed over the four rings, using kicker magnets
Each ring will inject over multiple turns, accumulating beam in the horizontal phase space
This means that the beam size (transverse emittance) increases when the intensity increases  ~ constant density
The PS Booster determines the transverse Brightness of the LHC beam

## Slide 8: PS
The oldest operating synchrotron at CERN
Circumference of 628m
  4 x PSB circumference
Increases proton energy from 1.4 GeV to a range of energies up to 26 GeV
Cycle length varies depending on the final energy, but ranges from 1.2s to 3.6s
The many different RF systems allow for complex RF gymnastics:
  10 MHz, 13/20 MHz, 40 MHz, 80 MHz, 200 MHz
Various types of extractions:
  Fast extraction
  Multi-turn extraction (MTE)
  Slow extraction
The PS determines the time structure of the LHC beam

## Slide 9: SPS
The first synchrotron in the chain at about 30m under ground
Circumference of 6.9 km
  11 x PS circumference
Increases proton beam energy up to 450 GeV with up to ~5x1013 protons per cycle
Provides slow extracted beam to the North Area fixed target experiments
Provides fast extracted beam to LHC, AWAKE and HiRadMat
The SPS accumulates up to 4 batches and being them up to 450 GeV

## Slide 10: LHC
Situated on average ~100 m under ground
Four major experiments (ATLAS, CMS, ALICE, LHCb)
Circumference 26.7 km
Two separate beam pipes going through the same cold mass 19.4 cm apart
150 tons of liquid helium to keep the magnets cold and superconducting

## Slide 11: LHC
1232 main dipoles of 15 m each that deviate the beams around the 27 km circumference
858 main quadrupoles that keep the beam focused
6000 corrector magnets to preserve the beam quality
Main magnets use superconducting cables (Cu-cladded Nb-Ti)
12’000 A provides a nominal field of 8.33 Tesla
Operating in superfluid helium at 1.9K

## Slide 12: Looking Back at the 2017 LHC Run

## Slide 13: 2017,…another eventful year
2017
Jan Feb Mar Apr May Jun Jul Aug Sep Oct Nov Dec
Apr 29th
First 2017 beam
June 5th
1 week scrubbing run and1st signs of losses in 16L2
May 23rd
First Stable Beams
April 1st
Gradual start of powering tests
Jul 3rd - 7th
TS #1
Sep 18th - 20th
TS #2
Aug 12th
16L2 beam induced Quench
Jun 9th
1st time 2820
Bunches at 450 GeV
Jun 3rd
RF full de-tuning
operational
<100 ps p-p
Jul 19th
Stable beams
2556 bunches
Jul 20th
Orbit corrector
mitigation 16L2
Aug 9th
Record Peak
Lumi: 1.74x1034
Sep 4st
Switch to 8b4e
Sep 21st
𝛽* 40 cm  30 cm
Aug 10th
Planned 16L2 beam screen flushing
Oct 30th
45 fb-1 reached
Oct 2nd
Switch to high
Brightness 8b4e
Nov 11th
Start Special Runs
Dec 4th
End of 2017 run
Nov 2nd
Record Peak
Lumi: 2.05x1034
Extended
Year
End
Technical
Stop
Magnet exchange in
sector 1-2

## Slide 14: 2017 Availability & Stable Beam Time
 | Duration [h]
Stable Beams | 1633.9
Operations | 1018.1
Fault/Downtime | 652.9
Pre-Cycle | 57.2
140 ½ days physics ≈ 3362.1 hours
= 3362.1
Stable beam ratio of previous years:
  2015  33%
  2016  49%

## Slide 15: Integrated Performance
ATLAS / CMS : 50 fb-1
LHCb: 2 fb-1 (levelled)
ALICE: 19 pb-1 (levelled)
The total integrated luminosity since the start of LHC is approaching 125 fb-1
2017 forecast: ~45 fb-1
Beyond expectations
2017

## Slide 16: LHC Peak Luminosity
The design luminosity of 1x1034 cm-2s-1 was reached in 2016
  Despite limitation on number of bunches imposed by the SPS internal dump problem
Fastest peak luminosity ramp up in 2017
  November 2nd 2017, 2.05x1034 cm-2s-1 was reached  More than twice the design value
  Despite 16L2 issues

## Slide 17: LHC Luminosity 2017
2556 bunches until early August, despite 16L2 induced beam loss
Beam screen flushing failed to mitigate 16L2 issue
Stable operation only with ~1900 bunches could be established with the 8b4e beam
Despite 16L2 the LHC ran well above design peak luminosity, >2x1034 cm-2s-1, but no longer visible due to levelling at 1.5x1034 cm-2s-1 as requested by ATLAS and CMS
BCMS: Max 2556 bunches
8b4e: Max 1916 bunches
Un-levelled 8b4e
Difficult period with many beam dumps and reduced number of bunches

## Slide 18: Another strange phenomenon in the LHC
In the lifetime of the LHC until 2017 we found:
  Electrons clouds
By performing scrubbing runs the vacuum chamber’s secondary electron emission yield is reduced

## Slide 19: Another strange phenomenon in the LHC
In the lifetime of the LHC until 2017 we found:
  Electrons clouds
  UFOs
Unidentified Falling Objects are tiny dust particles that fall into the beam and cause beam losses and some times beam dumps
By prolonged running they seem to be conditioning away

## Slide 20: Another strange phenomenon in the LHC
In the lifetime of the LHC until 2017 we found:
  Electrons clouds
  UFOs
  ULO
The Unidentified Lying Object is most likely a small piece of material in one of the vacuum chambers that if the beam hits it causes beam losses and beam dump
By applying a small local orbit bump the object can be avoided

## Slide 21: Another strange phenomenon in the LHC
In the lifetime of the LHC until 2017 we had:
  Electrons clouds
  UFOs
  ULOs
  GrUFfalO
New phenomena with sudden beam losses in 16L2, often resulting in beam dumps
  A (friendly) monster than woke up from time to time to bother us
http://www.gruffalo.com

## Slide 22: 2017 Intensity ramp up (BCMS Beam)
Smooth intensity ramp up, increasing the number of bunches
First dumps on 16L2 losses experienced
Technical Stop 1
Up to 1741 bunches

## Slide 23: Beam Screen Flushing, August 10th
Warm up the beam screen to 80K such that the gas evaporates and condensates on the cold bore, which remains at 1.9 K.
Elsewhere this has proven to be beneficial
For the 16L2 case the situation actually degraded

## Slide 24: Losing and Reconditioning
BS Flush
16L2 Quench
16L2 Beam Loss “signature” that resulted often in beam dumps
Variation of number of bunches during the “struggle” period
Attempting 2556 bunches
Ramp up to 1500 bunches
Running with 1500 bunches & frequent dumps

## Slide 25: 16L2, at some point we were puzzled…

## Slide 26: Attempts to Defeat the Gruffalo
Increased diagnostics
  Improving the signal to noise ratio
  Understand loss signals
No, this is not dynamite, but these are Beam Loss Monitors
Confirm hypothesis that e-cloud played a role
  Crash program to develop a solenoid to evacuate electrons from the interconnection

## Slide 27: Cryo Heat Load: BCMS vs 8b4E
8b+4e
8b4e intensity ramp up
BCMS 1500 bunches
8b4e running with 1900 bunches
16L2
16L2
16L2

## Slide 28: The Origin of the Gruffalo
Recently, sector 1-2 was recenlty warmed up to 80K and the vacuum chambers were pumped
  It was confirmed that air had entered in the vacuum chambers in a phase when the machine was cold (~ 7 liters per aperture)
  Nitrogen, oxygen and water condensate / frost must have appeared on the beam screen & cold bore
https://www.youtube.com/watch?v=c0rK2bLTimQ
Frozen nitrogen in vacuum
Gas analysis during pumping has confirmed the presence of N2, O2 and Ar
Sector 1-2 now back at 20K

## Slide 29: The 16L2 Layout
Interconnection
B2
B1
MB16L2
Thermal shield
at ~50K
MB17L2
Q16L2
P1
P2
P2
P1

## Slide 30: Optimisations - Increasing Luminosity
  150 𝜇rad
  140 𝜇rad
  130 𝜇rad
  120 𝜇rad
Half crossing angle
Reduction of 𝛽* from 40 cm to 30 cm
Crossing angle optimisation
  Following initial luminosity burn-off the long range beam-beam effect allows reducing crossing angle, hence increasing instantaneous luminosity
  Was done in 3 steps of 10 𝜇rad each
  ~ 5% gain in integrated luminosity over 16hrs
Continuous crossing angle reduction was also successfully tested and might be used in 2018

## Slide 31: Beam Variants From Injectors

## Slide 32: Standard 25 ns Beam
Injection
  1st: 4 bunches
  2nd : 2 bunches
Triple splitting
Acceleration
2 x splitting
  72 bunches at 25 ns
For 25 ns the intensity of a PSB bunches is divided by a factor 12
  ILHC = 1.2x1011 ppb
  IPSB = 14.4x1011 ppb
50 ns
25 ns: Each PSB bunch divided by: 12  6 x 3 x 2 x 2 = 72
72 bunches
Eject 36 or
Inject 4+2 bunches
h = 7
h = 21
h = 84
Eject 36 or
72 bunches
Controlled blow-ups
gtr
Triple splitting at Ekin = 2.5 GeV
Split in four at flat top energy
25 ns
Ekin = 2.5 GeV
2nd injection
26 GeV/c

## Slide 33: PS Booster Multi-turn Injection
The PSB performs a multi-turn injection, accumulating the LINAC beam in the PSB horizontal phase space
  Increasing intensity also increases transverse beam size, hence more or less constant density
PSB bunch intensity to be divided by 12 for standard 25 ns beam to reach bunch intensity of 1.1x1011 protons
1
2
3
x
x’

## Slide 34: BCMS 25 ns Beam
BCMS = Batch Compression, Merging & Splitting
BCMS
50 ns
25 ns: PSB bunches ‘divided’ by: 6  8/2 x 3 x 2 x 2 = 48
72 bunches
Eject 36 or
Inject 4+4 bunches
h = 9
h = 21
h = 84
Eject 24 or
48 bunches
Controlled blow-ups
gtr
Batch Compression, merging & splitting
Split in four at flat top energy
25 ns
Ekin = 2.5 GeV
2nd injection
26 GeV/c
High brightness
For same LHC bunch intensity PSB bunch intensity and transverse emittance is ~50% of standard scheme
For 25 ns the intensity of two PSB bunches are divided by a factor 6
  ILHC = 1.2x1011 ppb
  IPSB = 7.2x1011 ppb

## Slide 35: Standard 25 ns 8b4e Beam
8b4e 25 ns: PSB bunches divided by : 2  7 x 2 x 2 x 2 = 56
Each PSB bunch divided by 2 leaving 1 bucket empty at h=21
At high energy each bunch/bucket split in 4  8b4e
72 bunches
Eject 36 or
Inject 4+2 (3) bunches
h = 7
h = 21
h = 84
Eject 48 or
56 bunches
Controlled blow-ups
gtr
Double splitting at Ekin = 2.5 GeV
Split in four at flat top energy
25 ns
Ekin = 2.5 GeV
26 GeV/c
High brightness
Empty buckets
Due to the gaps in the 25ns bunch trains the electron cloud production is largely suppressed
Similar scheme as for the 25 ns standard beam
At 2.5 GeV triple splitting, populating only two first buckets and leaving 3rd empty
8b4e = 8 bunches + 4 empty buckets

## Slide 36: 8b4e BCS Beam
For same LHC bunch intensity PSB bunch intensity and transverse emittance is ~50% of standard scheme
No longer splitting but batch compression by adding empty buckets
8b4e 25 ns: PSB bunches only merged: 8  8 x 2 x 2 = 32
At high energy each bunch/bucket split in 4  8b4e
72 bunches
Eject 36 or
Inject 4+4 bunches
h = 9
h = 21
h = 84
Eject 24 or
48 bunches
Controlled blow-ups
gtr
Batch Compression, merging & splitting
Split in four at flat top energy
25 ns
Ekin = 2.5 GeV
2nd injection
26 GeV/c
High brightness
Empty buckets
Batch
Compression
8b4e = 8 bunches + 4 empty buckets

## Slide 37: 2018 LHC Schedule

## Slide 38: Draft 2018 LHC schedule - Q1 & Q2

## Slide 39: Draft 2018 LHC schedule – Q3

## Slide 40: Summary Table 2018 - 2017 - 2016
 | 2018 |  | 2017 |  | 2016 | 
Phase | Days | Ratio [%] | Days | Ratio [%] | Days | Ratio [%]
Comm. & Intensity ramp up | 28 | 11.4 | 35 | 16.1 | 28* | 11.3
Scrubbing | 4 | 1.6 | 7 | 3.3 | 2 | 0.8
25 ns Proton Physics | 138 | 56.3 | 127 | 58.5 | 139 | 56.3
Special Physics Runs | 9 | 3.7 | 18 | 8.3 | 10 | 4
Setting up Pb-Pb ion run | 4 | 1.6 | - | - | 6 | 2.4
Pb-Pb ion run | 24 | 9.8 | - | - | 23 | 9.3
Machine Developments (MD) | 20 | 8.2 | 18 | 8.3 | 21 | 8.5
Technical Stops (TS1 & TS2) | 13 | 5.4 | 8 | 3.7 | 12 | 5
Technical Stop Recovery | 5 | 2 | 4 | 1.8 | 6 | 2.4
Total | 245 | 100 | 217 | 100 | 247 | 100
Integrated luminosity [fb-1] | ~ 60 (tbc) |  | 50.2 |  | 39.7 | 
* Did not fully include intensity ramp up – interleaved commissioning and interleaved intensity ramp up was as of 2017

## Slide 41: CERN Upgrade Projects (LIU & HL-LHC)

## Slide 42: Luminosity, the Figure of Merit
More or less fixed:
  Revolution period
  Number of bunches
Intensity per bunch
Beam dimensions
Number of bunches
Geometrical
Correction
factors
High-Luminosity LHC
X 2
Parameters to optimise:
  Number of particles per bunch
  Beam dimensions
  Geometrical correction factors

## Slide 43: LIU: What will be changed ?
PS:
  Injection energy increase from 1.4 GeV to 2 GeV
  New Finemet® RF Longitudinal feedback system
  New RF beam manipulation scheme to increase beam brightness
LINAC4 – PS Booster:
  New LINAC 4 with H- injection
  Higher injection energy (160 MeV)
  New Finemet® RF cavity system
  Increase of extraction energy to 2 GeV
SPS
  Machine Impedance reduction (instabilities)
  New 200 MHZ RF system
  Vacuum chamber coating against e-cloud
These are only the main modifications and this list is not exhaustive

## Slide 44: HL-LHC: What will be changed ?
New IR-quads (inner triplets)
  New 11T short dipoles
  Collimation upgrade
  Cryogenics upgrade
  Crab Cavities
  Cold powering
  Machine protection
  …
Major intervention on more than 1.2 km of the LHC
These are only the main modifications and this list is not exhaustive

## Slide 45: Some HL-LHC Parameters
HL-LHC main parameters for proton collisions (re-baselining summer 2016)

## Slide 46: Crab Cavities
Crab cavities will reduce the effect of the geometrical factor on the luminosity and ”compensate” for the larger crossing angle needed with the HL-LHC beams

## Slide 47: Luminosity Levelling
In certain conditions and depending on the experiments request, it is required to adapt the luminosity dynamically with beams in collision – levelling
  Each levelling technique has its advantages and drawbacks
Levelling by beam offset / separation
Levelling by crossing angle
Complexity
Already tested & Operational
Already tested & Operational
Levelling by b* (= beam size at IP)
Tested & to be deployed operationally

## Slide 48: Luminosity Levelling & Anti-Levelling
In 2017 we initially levelled the ATLAS & CMS luminosity down to 1.5x1034 cm-2s-1, using beam separation
Once the luminosity burn-off kicks in we apply anti-levelling by reducing the crossing angle and increase the instantaneous luminosity
In 2018 we might add b* anti-levelling to reduce the b* further (< 30 cm) once the beam had sufficient luminosity burn-off

## Slide 49: The Long Term Schedule

## Slide 50
“We shall have no better conditions in the future if we are satisfied with all those which we have at present.”
Thomas A. Edison
Inventor and businessman, 1874 – 1931
E. Lawrence who invented the cyclotron in 1929
The LHC Today
… much has changed ….

## Slide 51
Any Questions

## Slide 52: Abstract
The CERN Large Hadron Collider continues to provide tremendous amounts of hadron collision data to its experiments. Over the past years the performance of the LHC and its injector chain was gradually increased to largely surpass its nominal performance in terms of luminosity.
In this seminar, the CERN accelerator complex will be recalled, with the focus on the LHC injector chain and the LHC itself. Enhancements in the injectors beam production schemes together with the introduction in the LHC of concepts actually foreseen for HL-LHC and key for the success in 2017, will be discussed.
The seminar will conclude with a brief outline of 2018 plans, the LHC Injector Upgrade (LIU) project and the High Luminosity LHC (HL-LHC) project.