## Slide 1
Chandra Bhat
Fermilab Workshop on Megawatt Rings & IOTA/FAST Collaboration Meeting
8 May 2018
Booster Upgrades to Achieve
~MW Beam in the Fermilab Complex

## Slide 2: Acknowledgements
W. Pellico
M. Convery
C. Tan
K. Seiya
S. Chaurize
F. Garcia
T. Sullivan
K. Triplett
B. Zwaska
C. Drennan
N. Eddy
V. Grzelak
J. Reid
V. Lebedev
D. Johnson
T. Johnson
B. Hendrick,
G. Vogel
A. Waller
V. Kapin
V. Sidorov
N. Mokhov
K. Gollwitzer
E. Stern –group (CD)
D. Harding – group (TD)
…..

## Slide 3
Chart: Protons delivered (pph)
PIP II
PIP +
LBNF Shutdown
PIP III ?
W. Pellico
From Yesterday’s talk
4.53E12ppBc
6.7E12ppBc

## Slide 4: Motivation
PIP-II is our future; goal is >1.2MW proton beam power on the DUNE neutrino target with 6.57E12ppBc with about 96% efficiency from the current Booster.
But!
  Booster is 47 year old RCS
  Is Booster ready now for PIP –II type beam intensity operation? NO
  Can we moderately increase the beam intensity output from the Booster using the existing LINAC ? YES
  Details on many devices built during the first 2-3 decades are not available.
  Therefore, we must prepare the Booster for high intensity beam operation ahead of PIP-II.
Beam measurements with increased beam intensities in stages is the way to go  This takes time

## Slide 5: Upgrade Path to Achieve ~MW
An Accelerator Improvement Program (PIP +) has been initiated
  With the goal to increase beam power output from the Proton Source to get 0.9MW (~MW) on the NuMI target &
  Simultaneously increase power to the BNB and other planned HEP experiments in the complex.
We have identified a few major areas of improvements in the Booster
  Studies on Beam dynamics to identify the issues and fix them to increase intensity ~5.5E12ppBc (primary goal)
    Injection to extraction beam studies and modeling (beam capture, acceleration, Transition crossing & extraction)
  Improvement in Collimation to localize the beam losses for the first few msec in the cycle
  Development of Transverse and Longitudinal Dampers to eliminate beam emittance dilution
  Booster shielding assessment

## Slide 6: Parameter Table
Current
Projected
With Beam Properties at extraction
L0.1 eVs/bunch &
dp/p(1)@Exit  0.035(%) or
E @Exit  3.1 MeV
T<16 -mm-mr

## Slide 7: Increasing the Beam Intensity & Address the Beam Dynamics Issues

## Slide 8: Increasing the Beam Intensity in the Booster & Adiabatic Beam Capture
Booster
Magnet Ramp
15 Hz
~49 s LINAC Beam
at 400 MeV
Booster
Booster
Synchrotron
Bmax
(8 GeV)
~200s
Beam Acceleration
using 37-52 MHz
RF system
Bmin (400 MeV)
~260s
for Capture
~49s
Inj.
Energy Acceptance ~5MeV
Beam E  1.6MeV
pseudo front-porch
Since late 2015 Early Injection Scheme gave us
An ability to inject more beam e.g.,
~15BT to ~20BT beam (~30%)
An additional 200 s for adiabatic beam
capture …

## Slide 9: ESME Simulations Beam Injection to Extraction
Simulation Parameters: with SC
1. LINAC Beam E = 1.2 to 1.6 MeV,
2. Beam Int.= 2-12E12ppBc
E Dist.
30
-30
0
E (MeV)
Line-Charge Dist.
E-t Phase space (8.2E12ppc)
2
-2
0
Azimuthal Angle(deg)
E@Inj
= 1.5 MeV
3. Booster machine parameters
4. Snap Bunch Rotation
Simulations suggest
one can achieve <20% emittance growth during capture.
L@Exit ~0.06 eVs (95%)
No particle losses
E @Exit< 2.75 MeV

## Slide 10: Beam Loading
Currently, Booster does not have any beam loading compensation.
  Intensity/Booster batch = 5.5e+12 ppBc @ Injection
  Beam Power at Extraction = 105 kW
  Beam Current=0.55 Amp
  Number of Cavities = 22 & Gaps/Cavity = 2
  Shunt Impedance/Cavity/gap = 15000 Ohms & Q = 720
  Beam Induced Voltage per cavity = -14.5 kV
  RF beam current/DC beam current= 2.00
  dP/dt(Max) = 373.91 GeV/c/sec
  Minimum Vrf @(dP/dt)max = 0.77 MV for acceleration
  Minimum Vrf required with Beam Loading = 1.1 MV
  Min. Power needed for Beam Accel. = 326 kW at
  dP/dt(Max)
  Optimum Generator Power = 0.87 MW
  Cavity Detuning Angle "phisZ" = 9.052 deg
For intensities ~5.5E12ppBc the RF system used for PIP is quite adequate. But, reliability may become an issue.
Confirmed by
simulations
Available
Vrf=1.1MV from
22 RF stations

## Slide 11: Booster Beam Transmission from Injection to Extraction
(xE12ppBc)
Inj. to Ext. Efficiency
But!
2
4
6
8
10
12
14
16
18
20 Booster Turn
Intensity (xE12 ppBc)
Injection at 400MeV & Extraction at 8 GeV
Booster Magnet Ramp
(schematic)
Transition Crossing
(T=5.47)
Beam power loss of
1W/m
~2W/m
Majority of the losses occur in the first 4 msec of the cycle
This loss can not be explained by Transverse dynamics (see C.Tan’s talk from yesterday).
There is an indication that this loss might be due to RF system misalignment (see my talk from yesterday).
Iteratively fix Trans.Dynamics  Long. Beam dynamics issues.
Operational Beam Intensity
1 MW (1.2sec/MI cycle)
0.92MW (1.33sec/MI cycle)
0.94MW (1.2sec/MI cycle) or
0.85MW (1.33sec/MI cycle)
0.70 MW (1.33sec/MI cycle)
One can achieve with
12 out of 15 Booster Batches
5.56E12ppBc
5.2E12ppBc

## Slide 12: Beam Emittance Measurements
WCM – Adabatic Capture
5.6E12ppBc@ Inj
Beam Inj & Capture
WCM – Operational
5.0E12ppBc@ Inj
Transverse Emittances
NuMI 700kW
V
H
dp/p
(no bunch rotation)
dp/p –with
bunch rotation
Booster is tuned for intensity required for 700kW on NuMI target and the intensity is varied for these measurements.
L(@end of Capture)
L(@extraction)
Longitudinal Emittance
NuMI 700kW
Adiabatic Capture
(95%)

## Slide 13: Transition Crossing Issues

## Slide 14: Bunch Rotation to lower dp/p @extraction for slip-stacking in RR
With Snap bunch rotation one can achieve small dp/p at extraction.
WCM Amplitude
Time Span nsec
4.5E12ppBc@Extraction
Tomography in RR
WCM Data
E2.6 MeV
L(4)0.085eVs
RR Tomo.
RR Tomo.
E3.1 MeV
L(4)0.073eVs
Operational Bunch Rotation
Snap Bunch Rotation
Vrf
Vrf-Input
Beam
Simulations showed that with 2nd harmonic RF cavity one can accept ~30% larger L to have acceptable dp/p at extraction for RR/MI.

## Slide 15: Collimator Improvement

## Slide 16: Existing Collimation System in the Booster
Commissioning (2004):
1) reduced activation by 40% around much of ring;
2) No advantages from the 2-stage Collimator (2SC) as implemented above
Currently we use it in 1SC mode
From V. Kapin
Lessons from current 2SC in Booster
apertures from magnets inside the collimation system were not optimal.
thicker foils were necessary.
Betatron phase for collimators location were not optimal in the available long sections.
This called for a new design for 2SC.

## Slide 17: New 2-Stage Collimator (2SC)
Currently we are working on a 2SC collimator to go in the L8 (or L9 or L10) of the Booster Ring as a part of the new AIP.
Three main designs are proposed by V. Kapin and V. Sidorov and one is selected.
N. Mokhov’s group in collaboration with V. Kapin and V. Sidorov are performing MARS/MADX simulation to understand the proton losses, prompt radiation distribution and needed shielding to protect the downstream devices in the Booster tunnel, ground water and surface water contamination, …
Primary
collimator
Drift tube
Stationary
collimator
Secondary
horizontal
Secondary
vertical
Stationary
collimator
V. Kapin and V. Sidorov
This work is in progress

## Slide 18: Dampers

## Slide 19: Longitudinal Dampers
Current Longitudinal Dampers (S. Chaurize’talk from yesterday)
Between 2015-17 the old analog higher order dampers have been replaced with active digital dampers to suppress the following modes
  45, 46, 47, 48, 49, 50, 51, 52, 53, 1 and 2
Longitudinal quad-dampers: To minimize the large bunch-bucket shape mismatch at transition.
Current performance of these dampers are quite adequate for PIP intensity except for mode-2. We would like to have a dedicated cavity for mode-2.
L11: Active Longitudinal digital Damper
Upgrades to the Longitudinal Dampers:
For increased Booster intensity, we are planning to reinstall a 65 MHz wide-band RF cavity in the Booster ring and use it as longitudinal damper with upgraded electronics.
Upgrade: Use 65 MHz wideband rf cavity in addition to the old system
Use the same FE electronics fed to the main RF system

## Slide 20: Transverse Dampers
Current Transverse Digital Damper:
During the PIP era an effort was made to upgrade the electronics to the existing damper system. Have demonstrated a feasibility of FPGA based digital bunch-by-bunch damper to control transverse oscillations from injection to extraction.
Vertical Damper
kicker
Horizontal Damper
kicker
H&V Damper
pickups
Damper Controller
For PIP intensity the Booster is operated with large chromaticities to control the transverse beam instabilities. Hence, the transverse dampers are not used.
However, with the increased beam intensities for the AIP and for PIP- II, we plan to use the digital dampers and are planning for further upgrades to the existing damper electronics.
Damper Off
Damper On
N. Eddy

## Slide 21: Booster Shielding
Current Shielding assessment: As a part of PIP project a complete shielding assessment has been performed for the Booster and approved for operation up to 2.7E17 p/hr. This implies that the existing shielding assessment is adequate for 900 kW operation. In future, beam power >2.7E17p/h ta new assessment need to be performed.
K. Gollwitzer

## Slide 22: On-going/Planned Additional Efforts
RF upgrades –local and global phase issues (CBhat, CTan, VGrzelak, JReid) (my talk from yesterday)
Replacement RF cavities (AD & TD) (Matt Slabaugh’s talk yesterday)
Booster Fast Loss Monitors (FLM)—R.Tesarek
Phase Jump near TX (CDrennan and BSchupbach, CBhat),
Wide aperture magnets at injection and extraction regions (KSeiya and DJohnson, W. Pellico),
Active Beam loading compensation,
…

## Slide 23: Summary
PIP will be officially complete by the end of FY18 and met its goals ahead of schedule.
Booster will still a play major role during PIP –II era.
An AIP is undertaken with a goal of increasing beam intensity in the Booster to achieve 0.9 MW beam power on the NuMI target. In view of this, following tasks are being addressed in Booster
  Beam physics: Longitudinal and transverse beam dynamics, better understanding of the Booster lattice and RF issues.
  Development of a new collimation system to localize radiation contamination and reduce irradiation on accelerator components.
  Upgrades to transverse and longitudinal dampers to handle higher intensity beam.
  Development of wider aperture dipole magnets around injection and extraction region.
Each of these tasks in this AIP is
extremely important for the success of PIP-II.

## Slide 24: Backup Slides

## Slide 25: Booster Layout
Booster is 47 years old. Details on many devices built during the first 2-3 decades are not available.
LINAC 400 MeV p Beam
8 GeV Beam
FDOODFO X 24 Period
Independent Corrector at
short and Long
Each corrector (12 poles) Includes
H, V dipoles, Q, SQ,SX, SSX
WCM
Collimators
Absorber
H&V Trans. Dampers
Inj. ORBUMP
Extra. Dogleg
H&V IPMs
Notcher
C= 475 Meter
# of RF Cavities= 22
Vrf (Volt)/Cavity= 50 KV
R/Q = 20 , Rs= 15 K
C=475 m, Trev=2.2-1.59s
h=84
RF
19-20
RF
15-16
RF
13-14
RF
11-12
RF
9-10
RF
21-22
RF
17-18
RF
7-8
RF
5,6
RF
1-2
RF
3-4
PIP Specification:
Vrf(total) = 1 MV
22 RF cavities with 50kV/cavity & swing freq. from 37.8 MHz-52.8 MHz

## Slide 26
Transverse Emittance in the MI8 Beamline (MW Data of 20160222 and 20161229, by Ming-Jen)
L:D7TOR~21mA
L:D7TOR~25mA
L (95%) <0.1 eVs
Does this imply, lower LINAC current and higher number of BT is better for higher intensity beam power on the neutrino target?
Or
Transition crossing scheme changed from time based to rf frequency based and better Booster tuning?

## Slide 27: Collimator
N.Mokhov et.al., PAC’2003: Purpose to localize losses (99% with 2SC)
in straight sections 6 and 7 and immediately downstream.
Designed in 2001-2004: single-stage (1SC) & two-stage (2SC) collimation
A.Drozhdin (2011):
Simulations with codes
STRUCT + MARS
to optimize 2SC
Losses spread over 50m
(Total length of 3 sec. colls ~4m)
Commissioning (2004):
1) reduced activation by 40% around much of ring;
2) No advantages for 2SC vs 1SC => Booster always uses 1SC mode
From V. Kapin
Existing Collimation System in Booster

## Slide 28: New Study on 2SC within PIP (2015-2017)
1)Simulations 2SC with MADX+MARS to optimize primary foil thickness
V.Kapin et al, “Study 2SC in Fermilab Booster”, 2017, Beams-Docs-5519-v1
Reasons for a low efficiency of 2SC in Booster (vs 1SC):
small apertures of magnets inside collimation system => no thick foils
not optimal phase locations of collimators in available long sections
thinner foil - useless in Boo (require constant trajectories on many turns)
2) Experimental studies with optimal Al foil : no advantages for 2SC vs 1SC (comparisons for BLM readings installed around the ring)
Eff (solid) = N_lost_colls/N_halo;
Eff (dash)=N_lost_colls/N_lost_ring
3 Cu foils - t [um] (10 & 100 turns):
1) Old foil before 2014 - worse;
2) Design 2004 best for 100 turns
3) New foil – better after ~10 turns
Booster – variable parameters =>
variable “c.o.+envelope” vs turns
From V. Kapin

## Slide 29: Booster Fast Loss Monitors (FLM)—R.Tesarek
Advanced design scintillation counters
  Single RF bucket resolution
  Desensitized to activation
Uses:
  Tune notch formation kicker parameters (oscilloscope)
  Monitor loss rates continuously for critical booster events: injection, notch formation, transition, extraction, etc. (ACNET)
Example: Notch formation losses:
  Remnant RF buckets persist after notching
magnet 5-3
collimator 6B
notch losses persist 250μs
notch
booster cycle
magnet 5-3
collimator 6B
notch
booster cycle
1 revolution
Notcher Absorber
3 RF buckets each
RF buckets
maximum deflection allowed by gradient magnet aperture
central orbit
“notched orbit”
remnant RF buckets

## Slide 30: Acceleration: Impedance modeling and simulation (1)
Impedance modeling for the laminated combined function magnet
Calculated impedance for F and D magnets
Modified impedance for F and D magnets
based on the measurement
Measured impedance for F and D magnets
  Theoretical model yields results close to the wire measurements
  Parameters of the impedance model are adjusted to match beam based measurements
V. Lebedev

## Slide 31
Laslett SC tune shift
SC = -0.32 (@4.6E12ppBc) to -0.49 ( @6.8E12ppBc) at injection