## Slide 1: Where in the world are the relevant BNB accelerator timing signals?
Alyssa R Miller
External Beams Department

## Slide 2: Signals BNB cares about and why
BES
  BES + delay [? RFC/ns] = beam arrival time
BRF
  Used to delay BES by 38-52 MHz cycles (RFC)
Delayed BES
  = BES + BRF
TCLK
  Events: $1D, sometimes $A9 (reflected MIBS $74) , $1F (reflected BES)
  10 MHz, 100 ns instability
MIBS
  Events: $74 (MI extraction to NuMI)
  Locked to MIRF 52-53 MHz / 7 = ~7.5 MHz
BNB and NuMI RWMs
  Leading edge is incoming beam

## Slide 3: Where are these signals available?
Notes: SciBooNE has MIBS and TCLK, but needs modules in the IRM to decode the clocks
MiniBooNE has MIBS but needs an IRM module to decode it

## Slide 4: How do I use these signals?
TCLK and MIBS can be decoded and delayed by an IRM
Delays are settable on ACNET
All signal carrying modules accept lemo terminated cables
Notes: Do I need to send a signal from a repeater into another module before using it for logic etc?

## Slide 5: What availability is in the future?
BNB RWM, NuMI RWM, BES and BRF at all active experiment service buildings
  On fiber
  (TCLK and MIBS are already there)
Notes: Greg says all these signals will be available in all the BNB experiment service buildings in the future, possibly via MFTUs?

## Slide 6: What is an MFTU?
Paired with copper to fiber converter
  4 inputs
  6 outputs for (copies of) each input
MultiFunctional Timing Unit
  Take converted fiber signals
  4 inputs
    + 1 dedicated TCLK
Notes: Dedicated clock inputs?
MFTUs taking in
BES, BRF, MIBS, TCLK

## Slide 7: MFTU example: Bill Badgett’s setup (version 0x007)
Outputs (Group A)
  Channels 1-8
    Armed on TCLK $1D
      Hard coded
    Trigger = BES
    Clock = BRF
      Count settable in ACNET
    Fine delay enabled
      0 - 255 ns settable in ACNET
  Channels 9-14
    Armed on TCLK $1D (presently)
      16 different events settable on ACNET
    Trigger = $1D
      Same as arming signal
      Set up like C377 timers
    Clock = 1us counter synced with TCLK
      Counts settable in ACNET
    Fine delay not enabled
  Channel 15
    Monitor of BES
  Channel 16
    Monitor of BRF
Inputs
  BRF
  BES
  (Unused trigger)
  MIBS
  TCLK
  (1us pulsed HI output when done counting)
  Special outputs:
  15 A monitors BES
  16 A monitors BRF
  1
Outputs (Group B)
  Channels 1-8
    Always armed
    Trigger = MIBS $74
    Clock is tick of MIBS CLK
      ~7.5 MHz
      Count settable in ACNET
    Fine delay not enabled
  Channels 9-16
    Armed on $1D
      16 different events settable on ACNET
    Trigger = $1D
      Same as arming signal
      Set up like C377 timers
    Clock = 1us counter synced with TCLK
      Counts settable in ACNET
    Fine delay not enabled
Notes: Others:
LArTF?
Inputs
  Delayed BES
  MIBS $74
  BNB RWM
  NuMI RWM
  TCLK
IRM
  TCLK
  MIBS
MI 12 SB?
4 inputs
  BES
  BRF
  MIBS
  BNB RWM
  + TCLK
8 outputs (copies)
  Each has individual settable delay on ACNET